1	gesis® FLEX – Modular, flat, direct pluggable KNX building automation system	3

1.1	Base modules	3

1.2	Power supply modules	6

1.3	Binary inputs	8

1.4	Binary outputs	10

1.5	Shutter outputs	12

1.6	System-compatible housings	14

1.7	Extension cables	16

1.8	Mounting frames	18

2	gesis® EIB RM – Modular KNX building automation system	20

2.1	Base module	20

2.2	Power supplies	21

2.3	Binary input	22

2.4	Switching output	23

2.5	Sunblind outputs	24

2.6	Dimming outputs	25

2.7	Semiconductor outputs	27

2.8	Radio controlled input	29

2.9	Accessories	30

3	gesis® LON RM – Modular LON building automation system	31

3.1	Base module	31

3.2	Power supplies	32

3.3	Binary input	33

3.4	Switching output	34

3.5	Sunblind outputs	35

3.6	Dimming outputs	36

3.7	Semiconductor outputs	38

3.8	Radio controlled input	40

3.9	EnOcean gateway	41

3.10	Accessories	42

4	gesis® EIB V – Flat, direct pluggable KNX building automation system	43

4.1	Switching outputs	43

4.2	Sunblind outputs	45

4.3	Combined actuators	46

4.4	Switch/dim outputs	48

4.5	Gateway EnOcean	50

4.6	Accessories	53

5	gesis® EIB M2 – Modular, direct pluggable KNX building automation system	54

5.1	Base module	54

5.2	Binary inputs	55

5.3	Switching output	56

5.4	Sunblind output	57

5.5	Switch/dim output	58

5.6	Accessories	59

6	gesis® KNX – System components and room automation	60

6.1	Presence and motion sensors	60

6.2	DALI	62

6.3	Single room temperature control	63

6.4	Push button interface	66

6.5	System components	68

7	gesis® RC – EnOcean technology	72

7.1	Flat, direct pluggable actuators	72

7.2	Switching outputs for outside applications	75

7.3	Plug adapter / flush-mounted actuator	77

7.4	Alarm input	79

7.5	Window contact	80

7.6	EnOcean Gateway	81

7.7	Handheld transmitter	84

7.8	Multivendor radio switches	86

7.9	Radio switch,	91

7.10	Hotel-Card-Switch	100

7.11	Accessories	102

8	gesis® ELECTRONIC IP+ – EnOcean Receiver and LED control gear IP68	103

8.1	EnOcean Receiver	103

8.2	Constant current generator	105

8.3	Constant voltage generator	106

8.4	Transformer for low-voltage halogen luminaires	107

8.5	Accessories	108

# gesis® FLEX – Modular, flat, direct pluggable KNX building automation system

The modular KNX series gesis® FLEX is designed for decentral installation without further housing. A device always consists of a base module and expansion modules. The modules can control lighting, shutters, valves or integrate potential-free contacts with binary inputs in building automation. The mains supply and the internal bus contact automatically when the modules are combined. In-between feed-in modules allow separate fuses for different functions.
Because of the flat shape, the connection from one side, well-thought-out mounting options and the modular concept of this system fits in almost any space. The strictly pluggable design allows a fast, secure, and simple connection. The manual control directly on the modules simplifies start-up and troubleshooting. In combination with the plug ability this results in a clear interface between system integration and installation. Because only standard modules are used, changes during the planning, implementation or operational phase can be realized quickly.

## Base modules

gesis® FLEX base module with 3-phase supply

System gesis® FLEX - The 3-phase supplied KNX base module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, supports 6 expansion modules. They support all the common inputs and outputs, and they provide extensive room automation with only one physical address. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation.

Supply KNX:

Nominal voltage: KNX System voltage

Nominal current: ca. 5 mA

Supply mains:

Nominal voltage: 230/400 V AC

Nominal current: 3x16 A

Expandability:

Expansion module: 6, system-compatible

Power supply module: any

System-compatible housing: any

System extension: with pre-fabricated cable max. 1 m

Maximum length: summation of all modules width incl. system extension

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: connections for sensors and loads according to IEC 61535, incl.

mains supply, KNX connection according to KNX handbook

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 115 mm (127 mm incl. left and right end cap)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed end caps are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis KNX FLEX-BAS

Part No.: 83.020.0600.0

gesis® FLEX base module with 3-phase supply incl. gesis® plugs

System gesis® FLEX - The 3-phase supplied KNX base module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, supports 6 expansion modules. They support all the common inputs and outputs, and they provide extensive room automation with only one physical address. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation. All necessary plugs are enclosed.

Supply KNX:

Nominal voltage: KNX System voltage

Nominal current: ca. 5 mA

Supply mains:

Nominal voltage: 230/400 V AC

Nominal current: 3x16 A

Expandability:

Expansion module: 6, system-compatible

Power supply module: any

System-compatible housing: any

System extension: with pre-fabricated cable max. 1 m

Maximum length: summation of all modules width incl. system extension

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: connections for sensors and loads according to IEC 61535, incl.

mains supply, KNX connection according to KNX handbook

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 115 mm (127 mm incl. left and right end cap)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed end caps as well as plugs are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis KNX FLEX-BAS Z

Part No.: 83.020.0600.1

gesis® FLEX base module with 1-phase supply

System gesis® FLEX - The 1-phase supplied KNX base module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, supports 6 expansion modules. They support all the common inputs and outputs, and they provide extensive room automation with only one physical address. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation.

Supply KNX:

Nominal voltage: KNX System voltage

Nominal current: ca. 5 mA

Supply mains:

Nominal voltage: 230 V AC

Nominal current: 16 A

Expandability:

Expansion module: 6, system-compatible

Power supply module: any

System-compatible housing: any

System extension: with pre-fabricated cable max. 1 m

Maximum length: summation of all modules width incl. system extension

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: connections for sensors and loads according to IEC 61535, incl.

mains supply, KNX connection according to KNX handbook

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 115 mm (127 mm incl. left and right end cap)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed end caps are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis KNX FLEX-BAS SP

Part No.: 83.020.0601.0

gesis® FLEX base module with 1-phase supply incl. gesis® plugs

System gesis® FLEX - The 1-phase supplied KNX base module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, supports 6 expansion modules. They support all the common inputs and outputs, and they provide extensive room automation with only one physical address. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation. All necessary plugs are enclosed.

Supply KNX:

Nominal voltage: KNX System voltage

Nominal current: ca. 5 mA

Supply mains:

Nominal voltage: 230 V AC

Nominal current: 16 A

Expandability:

Expansion module: 6, system-compatible

Power supply module: any

System-compatible housing: any

System extension: with pre-fabricated cable max. 1 m

Maximum length: summation of all modules width incl. system extension

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: connections for sensors and loads according to IEC 61535, incl.

mains supply, KNX connection according to KNX handbook

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 115 mm (127 mm incl. left and right end cap)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed end caps as well as plugs are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis KNX FLEX-BAS SP Z

Part No.: 83.020.0601.1

## Power supply modules

gesis® FLEX power supply module 3-phase

System gesis® FLEX - The 3-phase power supply module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, allows a mains supply separate from the base module within a modular system. This means that the output loads can be split over different fuse circuits. It can be integrated in the system as often as required. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation.

Supply mains:

Nominal voltage: 230/400 V AC

Nominal current: 3x16 A

Electrical connections: Mains supply according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 95 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-MS

Part No.: 83.020.0610.0

gesis® FLEX power supply module 3-phase incl. gesis® plugs

System gesis® FLEX - The 3-phase power supply module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, allows a mains supply separate from the base module within a modular system. This means that the output loads can be split over different fuse circuits. It can be integrated in the system as often as required. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation. All necessary plugs are enclosed.

Supply mains:

Nominal voltage: 230/400 V AC

Nominal current: 3x16 A

Electrical connections: Mains supply according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 95 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed plugs are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis FLEX-MS Z

Part No.: 83.020.0610.1

gesis® FLEX power supply module 1-phase

The 1-phase power supply module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, allows a mains supply separate from the base module within a modular system. This means that the output loads can be split over different fuse circuits. It can be integrated in the system as often as required. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation.

Supply mains:

Nominal voltage: 230 V AC

Nominal current: 16 A

Electrical connections: Mains supply according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 95 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-MS SP

Part No.: 83.020.0611.0

gesis® FLEX power supply module 1-phase incl. gesis® plugs

System gesis® FLEX - The 1-phase power supply module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, allows a mains supply separate from the base module within a modular system. This means that the output loads can be split over different fuse circuits. It can be integrated in the system as often as required. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation. All necessary plugs are enclosed.

Supply mains:

Nominal voltage: 230 V AC

Nominal current: 16 A

Electrical connections: Mains supply according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 95 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed plugs are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis FLEX-MS SP Z

Part No.: 83.020.0611.1

## Binary inputs

gesis® FLEX binary input 8-fold

System gesis® FLEX - The 8-fold binary input 12 VDC, for connecting potential-free contacts, with flat surface mounted housing which can be fitted on in DIN rail for decentralized installation, is managed by the base module. It receives mains and bus supply from the upstream module. The extensive parameter set enables different automation functions. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation.

Supply KNX: via upstream module

Supply mains: via upstream module

Signal voltage: 12 V DC (SELV)

Power-on time: 100 % for all inputs at a time

Max. cable length: 100 m

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: all connections for sensors according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 95 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-8/0 (12)

Part No.: 83.020.0622.0

gesis® FLEX binary input 8-fold incl. gesis® plugs

System gesis® FLEX - The 8-fold binary input 12 VDC, for connecting potential-free contacts, with flat surface mounted housing which can be fitted on in DIN rail for decentralized installation, is managed by the base module. It receives mains and bus supply from the upstream module. The extensive parameter set enables different automation functions. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation. All necessary plugs are enclosed.

Supply KNX: via upstream module

Supply mains: via upstream module

Signal voltage: 12 V DC (SELV)

Power-on time: 100 % for all inputs at a time

Max. cable length: 100 m

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: all connections for sensors according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 95 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed plugs are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis FLEX-8/0 (12) Z

Part No.: 83.020.0622.1

## Binary outputs

gesis® FLEX binary output 4-fold

System gesis® FLEX - The 4-fold relay output 230 V/16 A, with flat surface mounted housing which can be fitted on DIN rails for decentralized installation, is managed by the base module. It receives mains and bus supply from the upstream module. The extensive parameter set enables different automation functions. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation.

Supply KNX: via upstream module

Supply mains: via upstream module

Nominal voltage: 230 V AC

Nominal current: 16 A (ohmic load)

Inrush current: max. 200 A (50 ms)

Number: 4 binary outputs (bistable relay)

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: all connections for loads according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 130 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-0/4

Part No.: 83.020.0623.0

gesis® FLEX binary output 4-fold incl. gesis® plugs

System gesis® FLEX - The 4-fold relay output 230 V/16 A, with flat surface mounted housing which can be fitted on DIN rails for decentralized installation, is managed by the base module. It receives mains and bus supply from the upstream module. The extensive parameter set enables different automation functions. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation. All necessary plugs are enclosed.

Supply KNX: via upstream module

Supply mains: via upstream module

Nominal voltage: 230 V AC

Nominal current: 16 A (ohmic load)

Inrush current: max. 200 A (50 ms)

Number: 4 binary outputs (bistable relay)

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: all connections for loads according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 130 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed plugs are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis FLEX-0/4 Z

Part No.: 83.020.0623.1

## Shutter outputs

gesis® FLEX shutter output 2-fold

System gesis® FLEX - The 2-fold shutter output 230 V/8 A, with flat surface mounted housing which can be fitted on in DIN rail for decentralized installation, is managed by the base module. It receives mains and bus supply from the upstream module. The parameter set enables different automation functions. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation.

Supply KNX: via upstream module

Supply mains: via upstream module

Nominal voltage: 230 V AC

Nominal current: 8 A (ohmic load)

Number: 2 shutter outputs (4-pole, up/down)

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: all connections for loads according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 130 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-0/2W

Part No.: 83.020.0624.0

gesis® FLEX shutter output 2-fold incl. gesis® plugs

System gesis® FLEX - The 2-fold shutter output 230 V/8 A, with flat surface mounted housing which can be fitted on in DIN rail for decentralized installation, is managed by the base module. It receives mains and bus supply from the upstream module. The parameter set enables different automation functions. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation. All necessary plugs are enclosed.

Supply KNX: via upstream module

Supply mains: via upstream module

Nominal voltage: 230 V AC

Nominal voltage: 230 V AC

Nominal current: 8 A (ohmic load)

Number: 2 shutter outputs (4-pole, up/down)

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: all connections for loads according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 130 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed plugs are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis FLEX-0/2W Z

Part No.: 83.020.0624.1

## System-compatible housings

gesis® FLEX system-compatible housing 4 MW

System gesis® FLEX - The system-compatible housing module for DIN rail surface mounting for decentralized installation can be used to install DIN rail mounted devices according to DIN 43880 with up to four module width. Mains and bus supply are passed from upstream to downstream module. Main supply can be internally gripped. Cable glands have to be yield on side.

Mounting possibility: DIN rail mounted device according to DIN 43880, 4 MW (72 mm)

Supply KNX: extern

Supply mains: via upstream module, can be gripped internally

Through wiring: Mains- and bus are passed from upstream to downstream module

Dimensions:

Length: 130 mm (assembled)

Width: approx. 140 mm

Height: 80 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-REG4

Part No.: 83.020.0660.0

gesis® FLEX system-compatible housing 4 MW with cable glands

System gesis® FLEX - The system-compatible housing module for DIN rail surface mounting for decentralized installation can be used to install DIN rail mounted devices according to DIN 43880 with up to four module width. Mains and bus supply are passed from upstream to downstream module. Main supply can be internally gripped. The module comes with 3 cable glands.

Mounting possibility: DIN rail mounted device according to DIN 43880, 4 MW (72 mm)

Supply KNX: extern

Supply mains: via upstream module, can be gripped internally

Through wiring: Mains- and bus are passed from upstream to downstream module

Cable glands: 1x cable diameter 5-9 mm, 2x cable diameter 7-13 mm

Dimensions:

Length: 130 mm (assembled)

Width: approx. 173 mm (incl. cable glands)

Height: 80 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-REG4 V

Part No.: 83.020.0661.0

gesis® FLEX system-compatible housing 4 MW with clear cover

System gesis® FLEX - The system-compatible housing module for DIN rail surface mounting for decentralized installation can be used to install DIN rail mounted devices according to DIN 43880 with up to four module width. Mains and bus supply are passed from upstream to downstream module. Main supply can be internally gripped. Cable glands have to be yield on side. The module has a clear cover to protect the internal device.

Mounting possibility: DIN rail mounted device according to DIN 43880, 4 MW (72 mm)

Supply KNX: extern

Supply mains: via upstream module, can be gripped internally

Through wiring: Mains- and bus are passed from upstream to downstream module

Clear cover: for 4 MW

Dimensions:

Length: 130 mm (assembled)

Width: approx. 140 mm

Height: 94 mm without DIN rail (incl. clear cover)

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-REG4 D

Part No.: 83.020.0662.0

gesis® FLEX system-compatible housing 4 MW with cable glands and clear cover

System gesis® FLEX - The system-compatible housing module for DIN rail surface mounting for decentralized installation can be used to install DIN rail mounted devices according to DIN 43880 with up to four module width. Mains and bus supply are passed from upstream to downstream module. Main supply can be internally gripped. The module comes with 3 cable glands and has a clear cover to protect the internal device.

Mounting possibility: DIN rail mounted device according to DIN 43880, 4 MW (72 mm)

Supply KNX: extern

Supply mains: via upstream module, can be gripped internally

Through wiring: Mains- and bus are passed from upstream to downstream module

Cable glands: 1x cable diameter 5-9 mm, 2x cable diameter 7-13 mm

Clear cover: for 4 MW

Dimensions:

Length: 130 mm (assembled)

Width: approx. 173 mm (incl. cable glands)

Height: 94 mm without DIN rail (incl. clear cover)

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-REG4 DV

Part No.: 83.020.0663.0

## Extension cables

gesis® FLEX extension cable mains 0.5 m

System gesis® FLEX - An extension of the internal mains for the flat, DIN rail surface mounted system for decentralized installation is possible with up to 1.0 m. It interlocks automatically if it is plugged. Because of the mechanical coding main and bus supply cannot be mixed.

Length: 0.5 m

Nominal voltage: 230/400 V AC

Nominal current: 3x16 A

Plug-system: GST15i5 white

Brand: Wieland Electric GmbH

Type: GST15i5KS BS X15 V 05WS

Part No.: 91.257.0500.2

gesis® FLEX extension cable mains 1.0 m

System gesis® FLEX - An extension of the internal mains for the flat, DIN rail surface mounted system for decentralized installation is possible with up to 1.0 m. It interlocks automatically if it is plugged. Because of the mechanical coding main and bus supply cannot be mixed.

Length: 1.0 m

Nominal voltage: 230/400 V AC

Nominal current: 3x16 A

Plug-system: GST15i5 white

Brand: Wieland Electric GmbH

Type: GST15i5KS BS X15 V 10WS

Part No.: 91.257.1000.2

gesis® FLEX extension cable bus 0.5 m

System gesis® FLEX - An extension of the internal bus for the flat, DIN rail surface mounted system for decentralized installation is possible with up to 1.0 m. It interlocks automatically if it is plugged. Because of the mechanical coding main and bus supply cannot be mixed.

Length: 0.5 m

Nominal voltage: 50 V

Nominal current: 10 A

Plug-system: GST15i5 lighting blue

Brand: Wieland Electric GmbH

Type: GST15i5KS BSX05_V 05BL02

Part No.: 99.400.9999.8

gesis® FLEX extension cable bus 1.0 m

System gesis® FLEX - An extension of the internal bus for the flat, DIN rail surface mounted system for decentralized installation is possible with up to 1.0 m. It interlocks automatically if it is plugged. Because of the mechanical coding main and bus supply cannot be mixed.

Length: 1.0 m

Nominal voltage: 50 V

Nominal current: 10 A

Plug-system: GST15i5 lighting blue

Brand: Wieland Electric GmbH

Type: GST15i5KS BSX05_V 10BL02

Part No.: 99.401.9999.8

## Mounting frames

gesis® FLEX mounting frame 40 cm

System gesis® FLEX - The fit-up aid for the flat, DIN rail surface mounted system for decentralized installation alleviates the mounting to cable trays, in suspended ceilings or raised floors. It grabs different numbers of modules according to its length and comes with a fixing possibility for connected cables. The hole pattern and incl. screws enable a quick mounting.

Length: 40 cm

DIN rail: TH35x7.5

Locking holes: round-, long- and keyhole

Fixing material: roundhead and hook screw for cable trays are part of the delivery

Brand: Wieland Electric GmbH

Type: MB TH35-7,5 HK 40x20 Z

Part No.: Z5.524.1410.0

gesis® FLEX mounting frame 50 cm

System gesis® FLEX - The fit-up aid for the flat, DIN rail surface mounted system for decentralized installation alleviates the mounting to cable trays, in suspended ceilings or raised floors. It grabs different numbers of modules according to its length and comes with a fixing possibility for connected cables. The hole pattern and incl. screws enable a quick mounting.

Length: 50 cm

DIN rail: TH35x7.5

Locking holes: round-, long- and keyhole

Fixing material: roundhead and hook screw for cable trays are part of the delivery

Brand: Wieland Electric GmbH

Type: MB TH35-7,5 HK 50x20 Z

Part No.: Z5.524.1510.0

gesis® FLEX mounting frame 60 cm

System gesis® FLEX - The fit-up aid for the flat, DIN rail surface mounted system for decentralized installation alleviates the mounting to cable trays, in suspended ceilings or raised floors. It grabs different numbers of modules according to its length and comes with a fixing possibility for connected cables. The hole pattern and incl. screws enable a quick mounting.

Length: 60 cm

DIN rail: TH35x7.5

Locking holes: round-, long- and keyhole

Fixing material: roundhead and hook screw for cable trays are part of the delivery

Brand: Wieland Electric GmbH

Type: MB TH35-7,5 HK 60x20 Z

Part No.: Z5.524.1610.0

gesis® FLEX mounting frame 70 cm

System gesis® FLEX - The fit-up aid for the flat, DIN rail surface mounted system for decentralized installation alleviates the mounting to cable trays, in suspended ceilings or raised floors. It grabs different numbers of modules according to its length and comes with a fixing possibility for connected cables. The hole pattern and incl. screws enable a quick mounting.

Length: 70 cm

DIN rail: TH35x7.5

Locking holes: round-, long- and keyhole

Fixing material: roundhead and hook screw for cable trays are part of the delivery

Brand: Wieland Electric GmbH

Type: MB TH35-7,5 HK 70x20 Z

Part No.: Z5.524.1710.0

gesis® FLEX mounting frame 80 cm

System gesis® FLEX - The fit-up aid for the flat, DIN rail surface mounted system for decentralized installation alleviates the mounting to cable trays, in suspended ceilings or raised floors. It grabs different numbers of modules according to its length and comes with a fixing possibility for connected cables. The hole pattern and incl. screws enable a quick mounting.

Length: 80 cm

DIN rail: TH35x7.5

Locking holes: round-, long- and keyhole

Fixing material: roundhead and hook screw for cable trays are part of the delivery

Brand: Wieland Electric GmbH

Type: MB TH35-7,5 HK 80x20 Z

Part No.: Z5.524.1810.0

gesis® FLEX mounting frame 90 cm

System gesis® FLEX - The fit-up aid for the flat, DIN rail surface mounted system for decentralized installation alleviates the mounting to cable trays, in suspended ceilings or raised floors. It grabs different numbers of modules according to its length and comes with a fixing possibility for connected cables. The hole pattern and incl. screws enable a quick mounting.

Length: 90 cm

DIN rail: TH35x7.5

Locking holes: round-, long- and keyhole

Fixing material: roundhead and hook screw for cable trays are part of the delivery

Brand: Wieland Electric GmbH

Type: MB TH35-7,5 HK 90x20 Z

Part No.: Z5.524.1910.0

gesis® FLEX mounting frame 100 cm

System gesis® FLEX - The fit-up aid for the flat, DIN rail surface mounted system for decentralized installation alleviates the mounting to cable trays, in suspended ceilings or raised floors. It grabs different numbers of modules according to its length and comes with a fixing possibility for connected cables. The hole pattern and incl. screws enable a quick mounting.

Length: 100 cm

DIN rail: TH35x7.5

Locking holes: round-, long- and keyhole

Fixing material: roundhead and hook screw for cable trays are part of the delivery

Brand: Wieland Electric GmbH

Type: MB TH35-7,5 HK 100x20 Z

Part No.: Z5.524.2010.0

# gesis® EIB RM – Modular KNX building automation system

Modular KNX system for mounting in decentral distribution boxes. Applications: Lighting, shutter as well as electro thermal valves control and gathering potential-free or radio-based signals.

The modularity offers a flexible combination of in- and outputs with only one physical address. Therefore the gesis RM system can be optimized to a perfect solution for each project.

More complex applications can be realized through the extensive software equipment. The devices are built into distribution boxes and wired to gesis® connectors. The distribution boxes are individually manufactured according to customer requirements and meet their needs in the electronic equipment, the number and type of pluggable connections and also in the dimensions with a minimum height of 55 mm.

## Base module

gesis® EIB RM base module

System gesis® RM - The KNX base module can manage up to four system compatible extension modules. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. There

are input, switching, sunblind, switch/dim, DALI and semiconductor extension modules available. Because of the variety of extension modules a lot of room automation features can be fulfilled.

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 12 V DC

Nominal current: 160 mA

Electrical connections: screw-type terminals

Outputs:

4 connections for extension modules

Connections: pluggable ribbon cable

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: EIB RM2-BAS

Part No.: 83.020.0400.3

## Power supplies

gesis® RM power supply 0,16 A

System gesis® RM - The power supply (SELV) has a nominal current of 160 mA. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. It is used to power the system compatible base modules or other devices. All electrical connections are screw terminated.

Main supply:

Nominal voltage: 230 V AC

Output:

Nominal voltage: 12 V DC, SELV

Nominal current: 160 mA

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-PS

Part No.: 83.020.0401.0

gesis® RM power supply 0,4 A

System gesis® RM - The low loss power supply (SELV) has a nominal current of 400mA. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. It is used to power the system compatible base modules or other devices. All electrical connections are screw terminated.

Main supply:

Nominal voltage: 230 V AC

Output:

Nominal voltage: 12 V DC, SELV

Nominal current: 400 mA

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-PS 12/5

Part No.: 83.020.0421.0

## Binary input

gesis® RM binary input 8-fold

System gesis® RM - The extension module has 8 inputs and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The binary inputs are connected to potential free contacts like installation switches. They can be configured to fulfill different functions within the building automation system. The scanning voltage is provided by the module.

Main supply:

Nominal voltage: 230 V AC

Connection to base module: ribbon cable, included in delivery

Inputs: 8

Type: for potential-free contacts

Scanning voltage: 12 V, made in module

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-8/0 (12)

Part No.: 83.020.0402.0

## Switching output

gesis® RM switching output 4-fold

System gesis® RM - The extension module has 4 outputs and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The outputs are potential free, galvanized and are separately and independently controllable.

Outputs:

4 switching outputs, potential-free

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/4

Part No.: 83.020.0403.0

## Sunblind outputs

gesis® RM sunblind output 2-fold, 230 V

System gesis® RM - The extension module has 2 sunblind outputs, automated drive time measurement and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The outputs can control 230 V motors for two directions of rotation. The outputs have one common micro-fuse but are separately and independently controlled.

Outputs:

2 Sunblind outputs

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 5 A joint

Fuse: 5 AT micro-fuse

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/2W SI

Part No.: 83.020.0404.0

gesis® RM sunblind output 2-fold, 24 V

System gesis® RM - The extension module has 2 sunblind outputs, automated drive time measurement and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The outputs can control 24 V motors for two directions of rotation. The outputs have one common micro-fuse but are separately and independently controlled.

Outputs:

2 Sunblind outputs

Nominal voltage: 24 V DC

Nominal current: 5 A joint

Fuse: 5 AT micro-fuse

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/2W DC

Part No.: 83.020.0407.0

## Dimming outputs

gesis® RM switch/dim output 2-fold

System gesis® RM - The extension module has 2 switch/dim outputs and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The separated outputs are able to control dynamic electronic ballasts with 1-10V interface.

Main supply:

Nominal voltage: 230 V AC

Nominal current: 1 6A

Outputs:

Count: 2 switch/dim outputs

Nominal voltage mains: 230 V AC, 50...60 Hz

Nominal current mains: 16 A ohmic load

Nominal voltage signal: 1-10V

Nominal current signal: maximal 50 mA (passive)

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/2SD

Part No.: 83.020.0405.0

gesis® RM universal dimming output 2-fold

System gesis® RM - The extension module has 2x 250 VA universal dimming outputs, and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The separated outputs can scan the type of load (resistive, capacitive or inductive) and adjust the necessary dimming behavior. Each channel is able to handle a load up to 250 VA.

Outputs:

2 universal dimming outputs

Nominal voltage: 0-230 V AC, 50...60 Hz

Output load: 30-250 VA

Load type: R, L, C,

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/2D

Part No.: 83.020.0409.0

gesis® RM DALI output 2-fold

System gesis® RM - The extension module has 2x DALI outputs and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. Each DALI channel is working as a master and can handle up to eight DALI ballast's, using the broadcast mode. The DALI error message will be transferred as a collective report to the base module

Outputs:

2 DALI channels

Nominal voltage: DALI system voltage (approx. 16 V)

Output load: max. 8 DALI ballast's

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/2DA

Part No.: 83.020.0410.0

## Semiconductor outputs

gesis® RM semiconductor output 4-fold, AC/DC

System gesis® RM - The extension module has 4 wide range semiconductor outputs and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The outputs can be used for example, as 2-level valve control. The input voltage can be from 24 to 230V.

Outputs:

4 semiconductor switches

Nominal voltage: 230 V AC or 24 V DC

Nominal current: 0.5 A each output, short-cut-proof

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/4 HL

Part No.: 83.020.0406.0

gesis® RM semiconductor output 4-fold, AC

System gesis® RM - The extension module has 4 semiconductor outputs 230V AC and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The outputs can be used for example, as 2-level valve control. The input voltage can be from 12 to 230V AC.

Outputs:

4 semiconductor switches

Nominal voltage: 230 V AC (min. 12 V max. 253 V AC)

Nominal current: 0.5 A

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/4 HL AC

Part No.: 83.020.0411.0

gesis® RM semiconductor output 4-fold, DC

System gesis® RM - The extension module has 4 semiconductor outputs 24V DC and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The outputs can be used for example, as 2-level valve control. The input voltage can be from 12 to 45V AC.

Outputs:

4 semiconductor switches

Nominal voltage: 24 V DC (min.12 V max. 45 V DC)

Nominal current: 0.5 A

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/4 HL DC

Part No.: 83.020.0412.0

## Radio controlled input

gesis® RM radio controlled input 2x8-fold

System gesis® RM - The extension module has 16 radio controlled inputs and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The input can map 170 radio channels to 16 input channels. The allocation of the radio channels to the input channels will be done at the module.

Main supply: via connection to base module

Connection to base module: ribbon cable, included in delivery

Inputs: 16 in two groups, 8 each

Receiving frequency: 868.3 MHz

Antenna terminal: SMA female

Transmission protocol: EnOcean

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-16/0 (RC)

Part No.: 83.020.0408.0

## Accessories

gesis® RC antenna 868 MHz SMA male

System gesis® RC - The antenna with SMA socket is for 868 MHz nominal frequency. The black antenna can be mounted using a magnetic foot and has a 2.5 m connection cable.

Transmission frequency: 868.3 MHz

Connection: SMA angle male plug

Cable length: 2.5 m

Mounting: magnet base

Dimension: 28.5 mm base diameter, 117 mm antenna height

Color: black

Brand: Wieland Electric GmbH

Type: RC A-A1SWL25

Part No.: 83.020.0503.0

# gesis® LON RM – Modular LON building automation system

Modular LON system for mounting in decentral distribution boxes. Applications: Lighting, shutter as well as electro thermal valves control and gathering potential-free or radio-based signals.

The modularity offers a flexible combination of in- and outputs with only one node. Therefore the gesis RM system can be optimized to a perfect solution for each project.

More complex applications can be realized through the extensive software equipment. The devices are built into distribution boxes and wired to gesis® connectors. The distribution boxes are individually manufactured according to customer requirements and meet their needs in the electronic equipment, the number and type of pluggable connections and also in the dimensions with a minimum height of 55 mm.

## Base module

gesis® LON RM base module

System gesis® RM - The LON base module can manage up to four system compatible extension modules. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. There

are input, switching, sunblind, switch/dim, DALI and semiconductor extension modules available. Because of the variety of extension modules a lot of room automation features can be fulfilled.

Transceiver: TP/FT10 (FTT10A Transceiver)

Main supply:

Nominal voltage: 12 V DC

Nominal current: 190 mA

Electrical connections: screw-type terminals

Outputs:

4 connections for extension modules

Connections: pluggable ribbon cable

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: LON RM2-BAS

Part No.: 83.020.0300.3

## Power supplies

gesis® RM power supply 0,16 A

System gesis® RM - The power supply (SELV) has a nominal current of 160 mA. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. It is used to power the system compatible base modules or other devices. All electrical connections are screw terminated.

Main supply:

Nominal voltage: 230 V AC

Output:

Nominal voltage: 12 V DC, SELV

Nominal current: 160 mA

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-PS

Part No.: 83.020.0401.0

gesis® RM power supply 0,4 A

System gesis® RM - The low loss power supply (SELV) has a nominal current of 400mA. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. It is used to power the system compatible base modules or other devices. All electrical connections are screw terminated.

Main supply:

Nominal voltage: 230 V AC

Output:

Nominal voltage: 12 V DC, SELV

Nominal current: 400 mA

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-PS 12/5

Part No.: 83.020.0421.0

## Binary input

gesis® RM binary input 8-fold

System gesis® RM - The extension module has 8 inputs and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The binary inputs are connected to potential free contacts like installation switches. They can be configured to fulfill different functions within the building automation system. The scanning voltage is provided by the module.

Main supply:

Nominal voltage: 230 V AC

Connection to base module: ribbon cable, included in delivery

Inputs: 8

Type: for potential-free contacts

Scanning voltage: 12 V, made in module

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-8/0 (12)

Part No.: 83.020.0402.0

## Switching output

gesis® RM switching output 4-fold

System gesis® RM - The extension module has 4 outputs and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The outputs are potential free, galvanized and are separately and independently controllable.

Outputs:

4 switching outputs, potential-free

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/4

Part No.: 83.020.0403.0

## Sunblind outputs

gesis® RM sunblind output 2-fold, 230 V

System gesis® RM - The extension module has 2 sunblind outputs, automated drive time measurement and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The outputs can control 230 V motors for two directions of rotation. The outputs have one common micro-fuse but are separately and independently controlled.

Outputs:

2 Sunblind outputs

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 5 A joint

Fuse: 5 AT micro-fuse

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/2W SI

Part No.: 83.020.0404.0

gesis® RM sunblind output 2-fold, 24 V

System gesis® RM - The extension module has 2 sunblind outputs, automated drive time measurement and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The outputs can control 24 V motors for two directions of rotation. The outputs have one common micro-fuse but are separately and independently controlled.

Outputs:

2 Sunblind outputs

Nominal voltage: 24 V DC

Nominal current: 5 A joint

Fuse: 5 AT micro-fuse

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/2W DC

Part No.: 83.020.0407.0

## Dimming outputs

gesis® RM switch/dim output 2-fold

System gesis® RM - The extension module has 2 switch/dim outputs and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The separated outputs are able to control dynamic electronic ballasts with 1-10V interface.

Main supply:

Nominal voltage: 230 V AC

Nominal current: 1 6A

Outputs:

Count: 2 switch/dim outputs

Nominal voltage mains: 230 V AC, 50...60 Hz

Nominal current mains: 16 A ohmic load

Nominal voltage signal: 1-10V

Nominal current signal: maximal 50 mA (passive)

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/2SD

Part No.: 83.020.0405.0

gesis® RM universal dimming output 2-fold

System gesis® RM - The extension module has 2x 250 VA universal dimming outputs, and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The separated outputs can scan the type of load (resistive, capacitive or inductive) and adjust the necessary dimming behavior. Each channel is able to handle a load up to 250 VA.

Outputs:

2 universal dimming outputs

Nominal voltage: 0-230 V AC, 50...60 Hz

Output load: 30-250 VA

Load type: R, L, C,

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/2D

Part No.: 83.020.0409.0

gesis® RM DALI output 2-fold

System gesis® RM - The extension module has 2x DALI outputs and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. Each DALI channel is working as a master and can handle up to eight DALI ballast's, using the broadcast mode. The DALI error message will be transferred as a collective report to the base module

Outputs:

2 DALI channels

Nominal voltage: DALI system voltage (approx. 16 V)

Output load: max. 8 DALI ballast's

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/2DA

Part No.: 83.020.0410.0

## Semiconductor outputs

gesis® RM semiconductor output 4-fold, AC/DC

System gesis® RM - The extension module has 4 wide range semiconductor outputs and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The outputs can be used for example, as 2-level valve control. The input voltage can be from 24 to 230V.

Outputs:

4 semiconductor switches

Nominal voltage: 230 V AC or 24 V DC

Nominal current: 0.5 A each output, short-cut-proof

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/4 HL

Part No.: 83.020.0406.0

gesis® RM semiconductor output 4-fold, AC

System gesis® RM - The extension module has 4 semiconductor outputs 230V AC and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The outputs can be used for example, as 2-level valve control. The input voltage can be from 12 to 230V AC.

Outputs:

4 semiconductor switches

Nominal voltage: 230 V AC (min. 12 V max. 253 V AC)

Nominal current: 0.5 A

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/4 HL AC

Part No.: 83.020.0411.0

gesis® RM semiconductor output 4-fold, DC

System gesis® RM - The extension module has 4 semiconductor outputs 24V DC and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The outputs can be used for example, as 2-level valve control. The input voltage can be from 12 to 45V AC.

Outputs:

4 semiconductor switches

Nominal voltage: 24 V DC (min.12 V max. 45 V DC)

Nominal current: 0.5 A

Connection to base module: ribbon cable, included in delivery

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-0/4 HL DC

Part No.: 83.020.0412.0

## Radio controlled input

gesis® RM radio controlled input 2x8-fold

System gesis® RM - The extension module has 16 radio controlled inputs and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The input can map 170 radio channels to 16 input channels. The allocation of the radio channels to the input channels will be done at the module.

Main supply: via connection to base module

Connection to base module: ribbon cable, included in delivery

Inputs: 16 in two groups, 8 each

Receiving frequency: 868.3 MHz

Antenna terminal: SMA female

Transmission protocol: EnOcean

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-16/0 (RC)

Part No.: 83.020.0408.0

## EnOcean gateway

gesis® LON R gateway EnOcean

System gesis® R - The Gateway can map 170 EnOcean channels to 56 LON network variables. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The necessary antenna can be connected by a SMA socket. The electrical connections are carried out with screw connection.

Receiving frequency: 868.3 MHz

Antenna terminal: SMA female

Transmission protocol: EnOcean

Main supply:

Nominal voltage: 12 V DC, SELV

Nominal current: 60 mA

Transceiver: TP/FT-10

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD)

Software: starting with LNS 3

Brand: Wieland Electric GmbH

Type: LON R-56/0 (RC)

Part No.: 83.020.0320.0

## Accessories

gesis® RC antenna 868 MHz SMA male

System gesis® RC - The antenna with SMA socket is for 868 MHz nominal frequency. The black antenna can be mounted using a magnetic foot and has a 2.5 m connection cable.

Transmission frequency: 868.3 MHz

Connection: SMA angle male plug

Cable length: 2.5 m

Mounting: magnet base

Dimension: 28.5 mm base diameter, 117 mm antenna height

Color: black

Brand: Wieland Electric GmbH

Type: RC A-A1SWL25

Part No.: 83.020.0503.0

# gesis® EIB V – Flat, direct pluggable KNX building automation system

The gesis® EIB V series is directly ready for use without wiring work and characterized by its particularly flat design and direct connectivity to the 7-pole flat cable system. The installation is completed locally in suspended ceilings or elevated floors, without installing an additional housing. All electrical connections are pluggable.

## Switching outputs

gesis® EIB V switching output 4-fold, 3-phase

System gesis® EIB V - The switching output features a very low profile, has a three phase mains supply and four outputs. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 3~

Nominal current: each phase 16 A

Outputs:

Count: 4

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-0/4B

Part No.: 83.020.0225.0

gesis® EIB V Switching output 4-fold, 1-phase

System gesis® EIB V - The switching output features a very low profile, has a one phase mains supply and four outputs. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 1~

Nominal current: 16 A

Outputs:

Count: 4

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-0/4B SP

Part No.: 83.020.0225.4

gesis® EIB V Switching output 6-fold, 3-phase

System gesis® EIB V - The switching output features a very low profile, has a three phase mains supply and six outputs. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 3~

Nominal current: each phase 16 A

Outputs:

Count: 6

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-0/6

Part No.: 83.020.0214.0

## Sunblind outputs

gesis® EIB V sunblind output 2-fold, 3-phase

System gesis® EIB V - The sunblind output for shutter automation features a very low profile, has a three phase mains supply and two sunblind outputs. The software allows very comfortable and energy saving shutter automation. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 3~

Nominal current: each phase 16 A

Outputs:

Count: 2

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-0/2W B

Part No.: 83.020.0221.0

gesis® EIB V sunblind output 2-fold, 1-phase

System gesis® EIB V - The sunblind output for shutter automation features a very low profile, has a one phase mains supply and two sunblind outputs. The software allows very comfortable and energy saving shutter automation. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 1~

Nominal current: 16 A

Outputs:

Count: 2

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-0/2W B SP

Part No.: 83.020.0221.4

## Combined actuators

gesis® EIB V combined actuator 2-fold Switching output, 1-fold Jalousieausgang, 3-phase

System gesis® EIB V - The combined output features a very low profile, has a three phase mains supply, two switching and one sunblind output. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 3~

Nominal current: each phase 16 A

Outputs:

Count: 2 Switching outputs

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Count: 1 Jalousieausgang

Nominal voltage: 230 V AC, 50...60Hz

Nominal current: 8 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-0/2+1W

Part No.: 83.020.0212.0

gesis® EIB V combined actuator 2-fold Switching output, 1-fold Jalousieausgang, 1-phase

System gesis® EIB V - The combined output features a very low profile, has a one phase mains supply, two switching and one sunblind output. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 1~

Nominal current: 16 A

Outputs:

Count: 2 Switching outputs

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Count: 1 Jalousieausgang

Nominal voltage: 230 V AC, 50...60Hz

Nominal current: 8 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-0/2+1W SP

Part No.: 83.020.0212.4

## Switch/dim outputs

gesis® EIB V Switch/dim output 2-fold, 3-phase

System gesis® EIB V - The switch/dim output features a very low profile, has a three phase mains supply and two outputs for signal dimming 1-10V with switched 230V. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 3~

Nominal current: each phase 16 A

Outputs:

Count: 2

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Nominal voltage signal: 1-10 V

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-0/2SD

Part No.: 83.020.0213.0

gesis® EIB V Switch/dim output 2-fold, 1-phase

System gesis® EIB V - The switch/dim output features a very low profile, has a one phase mains supply and two outputs for signal dimming 1-10V with switched 230V. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 1~

Nominal current: 16 A

Outputs:

Count: 2

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Nominal voltage signal: 1-10 V

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-0/2SD SP

Part No.: 83.020.0213.4

## Gateway EnOcean

gesis® EIB V gateway EnOcean, switching output 4-fold, 3-phase

System gesis® EIB V - The EnOcean gateway features a very low profile, has a three phase mains supply and four independent outputs. It manages 170 EnOcean telegrams and transfers them to 56 KNX objects. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 3~

Nominal current: each phase 16 A

Outputs:

Count: 4

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-56/4 (RC)

Part No.: 83.020.0220.0

gesis® EIB V gateway EnOcean, switching output 4-fold, 1-phase

System gesis® EIB V - The EnOcean gateway features a very low profile, has a one phase mains supply and four independent outputs. It manages 170 EnOcean telegrams and transfers them to 56 KNX objects. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 1~

Nominal current: 16 A

Outputs:

Count: 4

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-56/4 RCSP

Part No.: 83.020.0220.1

gesis® EIB V Gateway EnOcean, switching output 4-fold, 3-phase, ext. antenna

System gesis® EIB V - The EnOcean gateway features a very low profile, has a three phase mains supply and four independent outputs. It manages 170 EnOcean telegrams and transfers them to 56 KNX objects. The SMA socket allows the connection of an antenna. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Antenna terminal: SMA female

Transmission protocol: EnOcean

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 3~

Nominal current: each phase 16 A

Outputs:

Count: 4

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-56/4 B (RC)

Part No.: 83.020.0220.2

gesis® EIB V gateway EnOcean, switching output 4-fold, 1-phase, ext. antenna

System gesis® EIB V - The EnOcean gateway features a very low profile, has a one phase mains supply and four independent outputs. It manages 170 EnOcean telegrams and transfers them to 56 KNX objects. The SMA socket allows the connection of an antenna. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Antenna terminal: SMA female

Transmission protocol: EnOcean

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 1~

Nominal current: 16 A

Outputs:

Count: 4

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-56/4 B RCSP

Part No.: 83.020.0220.3

## Accessories

gesis® RC antenna 868 MHz SMA male

System gesis® RC - The antenna with SMA socket is for 868 MHz nominal frequency. The black antenna can be mounted using a magnetic foot and has a 2.5 m connection cable.

Transmission frequency: 868.3 MHz

Connection: SMA angle male plug

Cable length: 2.5 m

Mounting: magnet base

Dimension: 28.5 mm base diameter, 117 mm antenna height

Color: black

Brand: Wieland Electric GmbH

Type: RC A-A1SWL25

Part No.: 83.020.0503.0

# gesis® EIB M2 – Modular, direct pluggable KNX building automation system

The gesis® EIB M2 series is a modular KNX device system. The base module can be combined with various extension modules. This results in a high degree of flexibility. The devices are designed for a direct mounting in suspended ceilings or elevated floors without an additional housing. The assembly is carried out on a mounting rail TH35. All electrical connections are pluggable.

## Base module

gesis® EIB M2 base module

System gesis® EIB M2 - The base module can manage up to six system compatible extension modules. It is for decentralized installation, can be fixed on a DIN rail and doesn't need an additional housing. The available extension modules are inputs, switching, sunblind and switch/dim outputs. Because of the variety of extension modules a lot of room automation features can be fulfilled. All electrical connections are pluggable.

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: < 5mA

Main supply:

Nominal voltage: 230/400 V AC, 3~

Nominal current: each phase 16 A (forwarded to all extension modules)

Electrical connections: all pluggable

Mounting: on-wall with mounting railTH35

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 120x80x62 (HxDxW)

Brand: Wieland Electric GmbH

Type: EIB M2-BAS

Part No.: 83.020.1020.0

## Binary inputs

gesis® EIB M2 binary input 4-fold, 230 V

System gesis® EIB M2 - The extension module has four 230 V inputs and will be managed by a system compatible base module. It is for decentralized installation, can be fixed on a DIN rail and doesn't need an additional housing. The inputs are connected to potential free contacts like installation switches. They can be configured to fulfill different functions. The scanning voltage of 230 V is provided by the modules. All electrical connections are pluggable.

Main supply: via base module, contacted if added

Inputs:

Count: 4

Nominal voltage: 230 V AC (coming from base module)

Contact type: potential-free contacts

Cable length: 100 m maximal

Electrical connections: all pluggable

Mounting: on-wall with mounting railTH35

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 120x80x62 (HxDxW)

Brand: Wieland Electric GmbH

Type: EIB M2-4/0

Part No.: 83.020.1021.0

gesis® EIB M2 binary input 4-fold, 24 V

System gesis® EIB M2 - The extension module has 4, 24 V inputs and will be managed by a system compatible base module. It is for decentralized installation, can be fixed on a DIN rail and doesn't need an additional housing. The binary inputs are connected to potential free contacts like installation switches. They can be configured to fulfill different functions within the building automation. The scanning voltage of 24 V is provided by the module. All electrical connections are pluggable.

Main supply: via base module, contacted if added

Inputs:

Count: 4

Nominal voltage: 24 V DC (coming from base module)

Contact type: potential-free contacts

Cable length: 100 m maximal

Electrical connections: all pluggable

Mounting: on-wall with mounting railTH35

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 120x80x62 (HxDxW)

Brand: Wieland Electric GmbH

Type: EIB M2-4/0 (24)

Part No.: 83.020.1022.0

## Switching output

gesis® EIB M2 switching output 2-fold

System gesis® EIB M2 - The extension module has 2 outputs and will be managed from a system compatible base module. It is for decentralized installation, can be fixed on a DIN rail and doesn't need an additional housing. The used phase for both outputs can be defined using a jumper. The functions of the outputs are independent. All electrical connections are pluggable.

Main supply: via base module, contacted if added

Outputs:

Count: 2

Nominal voltage: 230 V AC

Nominal current: 16 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall with mounting railTH35

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 120x80x62 (HxDxW)

Brand: Wieland Electric GmbH

Type: EIB M2-0/2

Part No.: 83.020.1023.0

## Sunblind output

gesis® EIB M2 sunblind output 1x2-fold

System gesis® EIB M2 - The extension module has 2 parallel working sunblind outputs and will be managed by a system compatible base module. It is for decentralized installation, can be fixed on a DIN rail and doesn't need an additional housing. The used phase for both outputs can be defined using a jumper. Both outputs are separated with relays that work in parallel. All electrical connections are pluggable.

Main supply: via base module, contacted if added

Outputs:

Count: 2 Sunblind outputs, controlled in parallel

Nominal voltage: 230 V AC

Nominal current: je 8 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall with mounting railTH35

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 120x80x62 (HxDxW)

Brand: Wieland Electric GmbH

Type: EIB M2-0/1WX2

Part No.: 83.020.1024.0

## Switch/dim output

gesis® EIB M2 switch/dim output 1-fold

System gesis® EIB M2 - The extension module has one switch-/dimming output and will be managed from a system compatible base module. It is for decentralized installation, can be fixed on a DIN rail and doesn't need an additional housing. The output is able to control dynamic electronic ballasts with 1-10V control signal. The used phase can be defined using a jumper. All electrical connections are pluggable.

Main supply: via base module, contacted if added

Output:

Count: 1

Nominal voltage mains: 230 V AC, 50...60 Hz

Nominal current mains: 16 A ohmic load

Nominal voltage signal: 1-10V

Nominal current signal: maximal 50 mA (passive)

Electrical connections: all pluggable

Mounting: on-wall with mounting railTH35

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 120x80x62 (HxDxW)

Brand: Wieland Electric GmbH

Type: EIB M2-0/1SD

Part No.: 83.020.1026.0

## Accessories

gesis® EIB M2 assembly set

System gesis® EIB M2 - DIN rail TH35 x7.5 for fixation of a gesis® EIB M2 module arrangement with a maximum of one basic module and six extension modules. It includes an end clamp for the fixation.

Brand: Wieland Electric GmbH

Type: EIB M2-MS500

Part No.: 99.002.9999.9

# gesis® KNX – System components and room automation

The Wieland gesis® KNX series implies products for the KNX topology as well as products for a complete room automation with KNX.

## Presence and motion sensors

gesis® KNX presence detector

System gesis® KNX - The ceiling mounted presence detector is specifically for office installations. At a mounting height of 3 meters the detection range is 7x7 m and squarish. The mixed light measurement as well as the fully- or semi-automatic operation allows a comfortable light automation for two separate output channels. The integrated presence detection without daylight sensing allows control of the room HVAC for optimized comfort and energy savings.

Main supply:

Nominal voltage: KNX system voltage

Nominal current: <10 mA

Connection: spring clamp terminal

Detection area:

Angle: horizontal 360°, vertical 120°

Range:

6x6 m at mounting height of 2.5 m

7x7 m at mounting height of 3.0 m

Mounting:

Mounting height: 2 m up to 3 m

Mounting: flush-mounted socket, diameter 55 mm

Type of protection: IP40

Housing color: white

Dimension in mm: 102x102x60 (LxWxD)

Visible mounting height: 33 mm

Brand: Wieland Electric GmbH

Type: KNX P CO

Part No.: 83.020.1400.0

gesis® KNX motion detector

System gesis® KNX - Motion detector for installation in the ceiling with integrated bus coupling unit for brightness and motion dependent control of lighting particularly in office and corridor spaces (including constant light regulation with master/ slave function).

Main supply:

Nominal voltage: KNX system voltage

Nominal current: <10 mA

Connection: spring clamp terminal

Detection area:

Angle: Horizontal 360°

Range:

7m diameter at mounting height of 2,8 m

Mounting:

Mounting height: 2 m up to 3 m

Mounting: ceiling cutout 64-68 mm diameter

Type of protection: IP20

Housing color: white

Dimension in mm: 76x69 (DxT)

Visible mounting height: 4 mm

Brand: Wieland Electric GmbH

Type: KNX M 331

Part No.: F0.000.0032.2

## DALI

gesis® KNX DALI gateway

System gesis® KNX - The DALI gateway N 141 is a KNX device with a DALI output for up to 64 DALI actuators (e.g. electronic ballasts with DALI interface). DALI sensors are not allowed to be connected to the output. All gateway functions are configured through the ETS.

DALI output according to IEC 60929, for max. 64 DALI ballasts with integrated DALI supply, short-cut-proof

Nominal voltage: AC/DC 110 - 240 V

Nominal voltage: KNX system voltage

Nominal current: <10 mA

Operation display: green LED

Operator button to switch between bus and direct control, with yellow LED to indicate direct control

Operator buttons for common on or off switching of all luminaires with red LED
Contact system to data rail

Mounting on mounting rail TH35 DIN EN 60715, 4 MW (1 MW = 18 mm),

Brand: Wieland Electric GmbH

Type: KNX N 141

Part No.: F0.000.0017.3

## Single room temperature control

gesis® KNX single room temperature control

System gesis® KNX - Room thermostat with integrated KNX bus coupling unit for control and regulation of valves and heating actuators. Three integrated inputs can be used for conventional switches/pushbuttons or even for external temperature sensors (optional), window contacts or presence signals.

Main supply:

Nominal voltage: KNX system voltage

Nominal current: <10 mA

Connection: spring clamp terminal

Inputs: 3, for potential-free contacts

Application: room temperature regulation for heating and cooling systems

Mounting:

Mounting: flush-mounted socket, diameter 55 mm

Type of protection: IP20

Housing color: white

Dimension in mm: 84x80x27

Brand: Wieland Electric GmbH

Type: KNX RTR SP

Part No.: F0.000.0032.0

gesis® KNX single room temperature control fan coil

System gesis® KNX - The room thermostat with integrated bus coupling unit is used to control fan coil systems. It integrates a manual button for selection of the operating modes Off and Auto as well as the fan position. The three available binary inputs can be parameterized freely.

Main supply:

Nominal voltage: KNX system voltage

Nominal current: <10mA

Connection: spring clamp terminal

Inputs: 3, for potential-free contacts

Application: room temperature regulation for heating and cooling systems with fan coils

Mounting:

Mounting: flush-mounted socket, diameter 55mm

Type of protection: IP20

Housing color: white

Dimension in mm: 84x80x27

Brand: Wieland Electric GmbH

Type: KNX RTR FC

Part No.: F0.000.0032.7

gesis® KNX motor-driven, continuous

System gesis® KNX - This motor-driven valve control with two binary inputs and valve stroke indicator can be mounted to customary valves using an adapter (within the scope of supply). A fully automatic valve stroke detection dynamically adapts the contact path to the used valve.

Main supply:

Nominal voltage: KNX system voltage

Nominal current: <10 mA

Connection: 2 m, 5-pole cable

Inputs: 2, for potential-free contacts

Mounting: with adapter included in delivery on heating and cooling valves

Type of protection: IP21

Housing color: white

Dimension in mm: 84x80x27

Brand: Wieland Electric GmbH

Type: KNX TH S

Part No.: F0.000.0032.1

gesis® KNX valve actuator, 2-point, electro thermal, 230 V

System gesis® KNX - The electro thermal 2-point valve control for 230 V can be mounted to customary valves, simply by using a valve adapter. Valve adapters are not included in the scope of supply.

Main supply:

Nominal voltage: 230 V

Nominal load: 1.8 W

Inrush current: max 300 mA for max. 200 ms

Connection: 2-polee cable, 1 m

Valve actuator current less: valve closed

Mounting: with adapter on heating and cooling valves (not included)

Type of protection: IP54

Housing color: white

Dimension in mm: 60x44x61

Brand: Wieland Electric GmbH

Type: TH P230

Part No.: F0.000.0032.3

gesis® KNX valve actuator, 2-Punkt, electro thermal, 24 V

System gesis® KNX - The electro thermal 2-point valve control for 24 V can be mounted to customary valves, simply by using a valve adapter. Valve adapters are not included in the scope of supply.

Main supply:

Nominal voltage: 24 V AC/DC

Nominal load: 1.8 W

Inrush current: max 300 mA for max. 200 ms

Connection: 2-polee cable, 1 m

Valve actuator current less: valve closed

Mounting: with adapter on heating and cooling valves (not included)

Type of protection: IP54

Housing color: white

Dimension in mm: 60x44x61

Brand: Wieland Electric GmbH

Type: TH P24

Part No.: F0.000.0032.6

gesis® valve adapter VA78

System gesis® KNX - Valve adapter ring VA 78 for easy installation of the valve controls. The adapter ring is placed on the valve and the valve control is snapped on. Applicable valves: Danfoss RA

Brand: Wieland Electric GmbH

Type: TH VA78

Part No.: F0.000.0032.4

gesis® valve adapter VA80

System gesis® KNX - Valve adapter ring VA 80 for easy installation of the valve controls. The adapter ring is placed on the valve and the valve control is snapped on. Applicable valves: Onda, Schlösser after '93/1993, Oventropp M30 x 1.5, Heimeier, Herb, Therm-Concept, Frank, Roth (distribution units), Dinotherm (distribution units).

Brand: Wieland Electric GmbH

Type: TH VA80

Part No.: F0.000.0032.5

gesis® KNX FanCoil output

System gesis® KNX - The fan coil actuator for DIN rail mounting with integrated bus coupling unit is used to control fan coil devices with heating/cooling circuits and 3-level fans. Furthermore this actuator has two potential free inputs that can be used for condensate monitoring or for window contacts.

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <10 mA

Connection: screw-type terminals

Main supply:

Nominal voltage: 230 V AC

Inputs: 2, for potential-free contacts, for temperature sensors

Outputs switching current:

Ventilator output: max. 8 A

Valve output: max. 0.5 A with 24 V...230 V AC

Additional relay: max. 16 A

Mounting method: mounting rail TH35 (4 MW)

Type of protection: IP20

Housing color: light gray

Dimension: 90x72x68 (4 MW)

Brand: Wieland Electric GmbH

Type: KNX FC 1-3

Part No.: F0.000.0032.8

## Push button interface

gesis® KNX push button interface 2-fold

System gesis® KNX - The 2 channel pushbutton interface with integrated bus coupling unit can be used as binary in- or output. In this way, conventional switches can be integrated into the building automation to control e.g. blinds and lighting.

Main supply:

Nominal voltage: KNX system voltage

Nominal current: <10 mA

Connection: spring clamp terminal

In-/Outputs:

Count: 2, switchable

Inputs: for potential-free contacts

Outputs: for low current LEDs (1 mA)

Interface cable: 30 cm

Interface extension: up to 5 m

Mounting: e.g. in flush-mounted sockets

Type of protection: IP54

Dimension in mm: 10x37x37

Brand: Wieland Electric GmbH

Type: KNX TA 2/2

Part No.: 83.020.1404.0

gesis® KNX push button interface 4-fold

System gesis® KNX - The 4 channel pushbutton interface with integrated bus coupling unit can be used as binary in- or output. In this way conventional switches can be integrated into the building automation to control e.g. blinds and lighting.

Main supply:

Nominal voltage: KNX system voltage

Nominal current: <10 mA

Connection: spring clamp terminal

In-/Outputs:

Count: 4, switchable

Inputs: for potential-free contacts

Outputs: for low current LEDs (1 mA)

Interface cable: 30 cm

Interface extension: up to 5 m

Mounting: e.g. in flush-mounted sockets

Type of protection: IP54

Dimension in mm: 10x37x37

Brand: Wieland Electric GmbH

Type: KNX TA 4/4

Part No.: 83.020.1405.0

gesis® KNX push button interface 6-fach

System gesis® KNX - The 6 channel pushbutton interface with integrated bus coupling unit can be used as binary in- or output. In this way conventional switches can be integrated into the building automation to control e.g. blinds and lighting.

Main supply:

Nominal voltage: KNX system voltage

Nominal current: <10 mA

Connection: spring clamp terminal

In-/Outputs:

Count: 6, switchable

Inputs: for potential-free contacts

Outputs max. 4: for low current LEDs (1 mA)

Interface cable: 30 cm

Interface extension: up to 5 m

Mounting: e.g. in flush-mounted sockets

Type of protection: IP54

Dimension in mm: 10x37x37

Brand: Wieland Electric GmbH

Type: KNX TA 6/4

Part No.: 83.020.1406.0

## System components

gesis® KNX power supply 160 mA

System gesis® KNX - The DIN rail mounted power supply (PELV) with integrated choke is specifically for KNX networks. The nominal current of 160 mA is sufficient for 32 standard KNX devices. In case of power failure and nominal load the time gap of 200 ms can be bridged.

Main supply:

Nominal voltage: 120 - 230 V AC, 50/60 Hz

Connection: screw-type terminals 0.5 mm²...2.5 mm²

Output:

Nominal voltage: DC 29 V

Nominal current: 160 mA

Short cut current: limited to 1 A

Time gap power failure: 200 ms at nominal load

Connection: spring clamp terminal

Type of protection: IP20

Mounting method: mounting rail TH35 (4 MW)

Dimension: 4 MW (72 mm)

Brand: Wieland Electric GmbH

Type: KNX PS 160

Part No.: 83.020.1413.0

gesis® KNX power supply 320 mA

System gesis® KNX - The DIN rail mounted power supply (PELV) with integrated choke is specifically for KNX networks. The nominal current of 320 mA is sufficient for 64 standard KNX devices. In case of power failure and nominal load the time gap of 200 ms can be bridged.

Main supply:

Nominal voltage: 120 - 230 V AC, 50/60 Hz

Connection: screw-type terminals 0.5 mm²...2.5 mm²

Output:

Nominal voltage: DC 29 V

Nominal current: 160 mA

Short cut current: limited to 1 A

Time gap power failure: 200 ms at nominal load

Connection: spring clamp terminal

Type of protection: IP20

Mounting method: mounting rail TH35 (4 MW)

Dimension: 4 MW (72 mm)

Brand: Wieland Electric GmbH

Type: KNX PS 320

Part No.: 83.020.1414.0

gesis® KNX Spannungsversorgung 640 mA

System gesis® KNX - The DIN rail mounted power supply (PELV) with integrated choke is specifically for KNX networks. The nominal current of 640 mA is sufficient for 64 standard KNX devices. The current can be split into one output with choke and one without choke. In case of power failure and nominal load the time gap of 200ms can be bridged.

Main supply:

Nominal voltage: 120 - 230 V AC, 50/60 Hz

Connection: screw-type terminals 0.5 mm²...2.5 mm²

Output:

Nominal voltage: DC 29 V

Nominal current: 640 mA

Short cut current: limited to 1.5 A

Time gap power failure: 200 ms at nominal load

Connection: spring clamp terminal

Type of protection: IP20

Mounting method: mounting rail TH35 (4 MW)

Dimension: 4 MW (72 mm)

Brand: Wieland Electric GmbH

Type: KNX PS 640

Part No.: 83.020.1415.0

gesis® KNX USB interface

System gesis® KNX - The DIN rail mounted USB interface is used for the bidirectional connection between a PC and the KNX twisted pair topology. The USB connection has a galvanic separation to the KNX twisted pair network.

Main supply:

USB: via connected PC, <200 mW

KNX: via connected KNX line, <300 mW

Connection:

KNX TP: spring clamp terminal

USB: female, type B

Type of protection: IP20

Mounting method: mounting rail TH35 (2 MW)

Dimension: 2 MW (36 mm)

Brand: Wieland Electric GmbH

Type: KNX USB

Part No.: 83.020.1418.0

gesis® KNX line/area coupler

System gesis® KNX - The DIN rail mounted line and backbone coupler is connecting hierarchy levels within a twisted pair KNX topology. The device makes a galvanic separation and can be commissioned with filter tables for telegrams. The device needs no external power supply. The necessary power is pulled out of the connected lines.

Main supply:

Higher line:

Nominal voltage: 24 V DC (21-29 V DC)

Nominal current: ca. 6 mA

Connection: spring clamp terminal

Lower Line:

Nominal voltage: 24 V DC (21-29 V DC)

Nominal current: ca. 8 mA

Connection: spring clamp terminal

Type of protection: IP20

Mounting method: mounting rail TH35 (2 MW)

Dimension: 2 MW (36 mm)

Brand: Wieland Electric GmbH

Type: KNX LK

Part No.: 83.020.1416.0

gesis® KNX IP router

System gesis® KNX - The DIN rail mounted IP router enables the communication between twisted pair lines over LAN (IP) as a fast backbone. In parallel the device can be used as an interface for bus access via IP.

Main supply:

Nominal voltage: 12-24 V DC, alternatively, Power over IP

Connection:

KNX TP: spring clamp terminal

Main supply: screw-type terminals

LAN: RJ45

Ethernet:

Transfer rate: 10BaseT

Supported protocols: ARP, ICMP, IGMP, UDP/IP, DHCP

Type of protection: IP20

Mounting method: mounting rail TH35 (2 MW)

Dimension: 2 MW (36 mm)

Brand: Wieland Electric GmbH

Type: KNX IP-R

Part No.: 83.020.1417.0

gesis® KNX surge arrester

System gesis® KNX - The type 2 arrester with KNX certification for KNX-TP systems has been tested according to EN 61643-21. It can directly replace the terminal block on KNX devices. The 200 mm grounding conductor is connected directly to the device.

Electrical data:

Arrester class: type 2

Rated/continuous voltage 24 V/45 V (for KNX TP)

KNX connection: spring contact (as terminal, directly pluggable to KNX device)

Cables Ø 0.8 mm / 200 mm long

Ground connection: cables 0.75 mm² / 200 mm long

Mechanical data:

Dimension: in mm 12x11x11

Cables: length ca. 200 mm

Brand: Wieland Electric GmbH

Type: KNX OVP

Part No.: F0.000.0008.3

gesis® KNX connection module

System gesis® KNX - The KNX connection module enables a simple tap of the KNX TP1 network in distribution units. The system integrator can access the network with the connection module, without removing field covers and therefore without interfering with the electrical installation.

Electrical data:

KNX Twisted Pair (SELV)

Nominal current: 3 A

Connection type: terminal block (under distributor cover)

Pluggable to outside: BST 14i2

Mechanical data:

Montage auf TH35 e.g. in distribution boxes

Width: 2 MW (36 mm)

Accessories: Connectors BST14i2 e.g. 93.422.0553.1

Brand: Wieland Electric GmbH

Type: KNX REG AM

Part No.: F0.000.0033.8

# gesis® RC – EnOcean technology

The radio system is based on the open standard of EnOcean and controls various applications of the electrical installation in buildings. Complex building automation solutions can be constructed by coupling with gateway to standardized systems of KNX and LON. The pluggable radio switching devices are easily installable in suspended ceilings or raised floors due to its low construction height. The pushbuttons and sensors for controlling the switching devices are battery-less and maintenance-free. They can be mounted anywhere, because of the radio-based, wireless communication.

## Flat, direct pluggable actuators

gesis® RC radio-based switching output 4-fold

System gesis® RC - The EnOcean switching output features a very low profile, has a single phase mains supply and four outputs. Up to 30 pairs of rockers from EnOcean switches can be programmed in. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

4 Switching outputs, normally open

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A ohmic load

Connection: pluggable

Mounting: on-wall, screw fastening

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: RC V-0/4 1PH

Part No.: 83.020.0500.0

gesis® RC radio-based switching 4-fold, ext. antenna

System gesis® RC - The EnOcean switching output features a very low profile, has a single phase mains supply and four outputs. Up to 30 pairs of rockers from EnOcean switches can be programmed in. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. The necessary antenna can be connected by a SMA socket. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Antenna terminal: SMA female

Transmission protocol: EnOcean

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

4 Switching outputs, normally open

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A ohmic load

Connection: pluggable

Mounting: on-wall, screw fastening

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: RC V-0/4 B 1PH

Part No.: 83.020.0500.2

gesis® RC radio-based sunblind output 2-fold

System gesis® RC - The EnOcean shutter output features a very low profile, has a single phase mains supply and four outputs. Up to 30 pairs of rockers from EnOcean switches can be programmed in. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

2 Sunblind outputs

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 5 A ohmic load

Connection: pluggable

Mounting: on-wall, screw fastening

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: RC V-0/2W AL 1PH

Part No.: 83.020.0501.1

gesis® RC radio-based sunblind 2-fold, ext. antenna

System gesis® RC - The EnOcean shutter output features a very low profile, has a single phase mains supply and four outputs. Up to 30 pairs of rockers from EnOcean switches can be programmed in. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. The necessary antenna can be connected by a SMA socket. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Antenna terminal: SMA female

Transmission protocol: EnOcean

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

2 Sunblind outputs

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 5 A ohmic load

Connection: pluggable

Mounting: on-wall, screw fastening

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: RC V-0/2W AL B 1PH

Part No.: 83.020.0501.2

## Switching outputs for outside applications

gesis® RC radio based switching output 1-fold, IP68

System gesis® RC - The EnOcean switching output has an IP68 housing for surface mounting with one relay output as well as a forwarded main supply and can be controlled by up to 30 EnOcean pushbuttons. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

Count: 1

Type: normally open 1-pole, phase switched

Nominal voltage: 230 V, 50...60 Hz

Nominal load: 1100 VA ohmic load

Connection: pluggable

1 through wiring

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 20 A

Connection: pluggable

Mounting: on-wall, screw fastening

Type of protection: IP68

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: black

Dimension in mm: 58x104x162 (HxWxL)

Brand: Wieland Electric GmbH

Type: RC RST-0/1

Part No.: 83.020.0504.0

gesis® RC radio based switching output 1x2-fold, IP68

System gesis® RC - The EnOcean switching output has an IP68 housing for surface mounting with one relay output, connected to two connectors and can be controlled by up to 30 EnOcean pushbuttons. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

Count: 1

Type: normally open 1-pole, phase switched

Nominal voltage: 230 V, 50...60 Hz

Nominal load: 1100 VA ohmic load

Connection: pluggable

1 through wiring

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 20 A

Connection: pluggable, 2-fold parallel

Mounting: on-wall, screw fastening

Type of protection: IP68

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: black

Dimension in mm: 58x104x162 (HxWxL)

Brand: Wieland Electric GmbH

Type: RC RST-0/1x2

Part No.: 83.020.0504.1

gesis® RC radio based switching output 4-fold, IP68

System gesis® RC - The EnOcean switching output has an IP68 housing for surface mounting with four independent relay outputs as well as a forwarded main supply and can be controlled by up to 30 EnOcean pushbuttons. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

Count: 4

Type: normally open 1-pole, phase switched

Nominal voltage: 230 V, 50...60 Hz

Nominal load: each output max. 6 A ohmic load

Connection: pluggable

1 through wiring

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 20 A

Connection: pluggable, 2-fold parallel

Mounting: on-wall, screw fastening

Type of protection: IP68

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: black

Dimension in mm: 96x104x162 (HxWxL)

Brand: Wieland Electric GmbH

Type: RC RST-0/4

Part No.: 83.020.0505.0

## Plug adapter / flush-mounted actuator

gesis® RC radio-based plug adapter switching output, 1-fold

System gesis® RC - The radio controlled (EnOcean) output has an on wall housing. It has one relay output and up to 30 pairs of rockers from EnOcean switches that can be programmed in. It can be installed as an adapter between feed in cable and e.g. luminaries. The electrical connections are carried out with screw connection.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Connection: pluggable

Output:

1 Switching output, normally open

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A max., ohmic load

Connection: pluggable

Type of protection: IP20

Dimension in mm: 74x71x33 (LxWxH)

Brand: Wieland Electric GmbH

Type: RC ZW-0/1

Part No.: F0.000.0016.9

gesis® RC radio-based plug adapter dimming output, 1-fold

System gesis® RC - The radio controlled (EnOcean) dimming output, for 60-200 VA resistive and inductive load has an on wall housing. Up to 30 pairs of rockers from EnOcean switches can be programmed in. It can be installed as an adapter between feed in cable and e.g. luminaries. The electrical connections are carried out with screw connection.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Connection: pluggable

Output:

1 Dimmausgang

Load type: R, L

Nominal voltage: 230 V, 50...60 Hz

Nominal load: 210 W

Connection: pluggable

Type of protection: IP20

Dimension in mm: 74x71x33 (LxWxH)

Brand: Wieland Electric GmbH

Type: RC ZW-0/1D

Part No.: F0.000.0017.0

gesis® RC radio-based switching output, 1-fold, flush-mounted

System gesis® RC - The radio controlled (EnOcean) output is for mounting in or on wall installation boxes. It has one relay output and up to 30 pairs of rockers from EnOcean switches that can be programmed in. The electrical connections are carried out with screw connection.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Connection: screw-type terminals

Output:

1 Switching output, normally open

Connection: screw-type terminals

Nominal voltage: 230 V, 50...60 Hz

Nominal load: 1100 VA ohmic load

Type of protection: IP30

Dimension in mm: 48x29x35 (LxWxH)

Brand: Wieland Electric GmbH

Type: RC UP-0/1

Part No.: 83.020.0506.0

## Alarm input

gesis® RC alarm input for sunblind control and binary input

System gesis® RC - The DIN rail mounted EnOcean binary input has 16 input channels for potential free contacts. Eight are standard inputs eight are alarm inputs for shutter application. For commissioning and test, all input scan be activated at the device. The necessary antenna can be connected by a SMA socket. The electrical connections are carried out with screw connection.

Transmission frequency: 868.3 MHz

Antenna terminal: SMA female

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 30 m in floors, approx. 100 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Main supply:

Nominal voltage: 24 V DC

Nominal current: 35 mA

Scanning voltage: 24 V DC

Type of protection: IP20

Housing: plastic, halogen-free

Mounting method: mounting rail TH35

Dimension in mm: 100x93x51 (HxWxD)

Brand: Wieland Electric GmbH

Type: RC V-16/0

Part No.: 83.020.0502.0

## Window contact

gesis® RC window contact

System gesis® RC - The white radio (EnOcean) window contact is battery-less, powered from a solar panel and is maintenance-free. If the internal energy buffer is completely charged, the power reserve will last a minimum of 14 hours. The small-sized sender and scanning magnet allows an inconspicuous installation.

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Type of protection: IP20

Min. brightness: 100 Lux (optimal from 400 lux)

Mounting: on-wall

Dimension in mm:

Window contact: 110x19x15

Magnet: 23x14x6

Brand: Wieland Electric GmbH

Type: RC S-SRWSENFK

Part No.: F0.000.0009.0

## EnOcean Gateway

gesis® EIB V gateway EnOcean, switching output 4-fold, 3-phase

System gesis® EIB V - The EnOcean gateway features a very low profile, has a three phase mains supply and four independent outputs. It manages 170 EnOcean telegrams and transfers them to 56 KNX objects. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 3~

Nominal current: each phase 16 A

Outputs:

Count: 4

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-56/4 (RC)

Part No.: 83.020.0220.0

gesis® EIB V gateway EnOcean, switching output 4-fold, 1-phase

System gesis® EIB V - The EnOcean gateway features a very low profile, has a one phase mains supply and four independent outputs. It manages 170 EnOcean telegrams and transfers them to 56 KNX objects. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 1~

Nominal current: 16 A

Outputs:

Count: 4

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-56/4 RCSP

Part No.: 83.020.0220.1

gesis® EIB V Gateway EnOcean, switching output 4-fold, 3-phase, ext. antenna

System gesis® EIB V - The EnOcean gateway features a very low profile, has a three phase mains supply and four independent outputs. It manages 170 EnOcean telegrams and transfers them to 56 KNX objects. The SMA socket allows the connection of an antenna. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Antenna terminal: SMA female

Transmission protocol: EnOcean

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 3~

Nominal current: each phase 16 A

Outputs:

Count: 4

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-56/4 B (RC)

Part No.: 83.020.0220.2

gesis® EIB V gateway EnOcean, switching output 4-fold, 1-phase, ext. antenna

System gesis® EIB V - The EnOcean gateway features a very low profile, has a one phase mains supply and four independent outputs. It manages 170 EnOcean telegrams and transfers them to 56 KNX objects. The SMA socket allows the connection of an antenna. No additional housings are required for mounting e.g. in suspended ceilings or false floors. It features an option for direct connection to the flat cable. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Antenna terminal: SMA female

Transmission protocol: EnOcean

KNX supply:

Nominal voltage: KNX system voltage

Nominal current: <5 mA

Main supply:

Nominal voltage: 230/400 V AC, 1~

Nominal current: 16 A

Outputs:

Count: 4

Nominal voltage: 230 V AC, 50...60 Hz

Nominal current: 16 A ohmic load

Electrical connections: all pluggable

Mounting: on-wall

Type of protection: IP20

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: light gray RAL 7035

Dimension in mm: 32x112x254 (HxWxL)

Brand: Wieland Electric GmbH

Type: EIB V-56/4 B RCSP

Part No.: 83.020.0220.3

gesis® LON R gateway EnOcean

System gesis® R - The Gateway can map 170 EnOcean channels to 56 LON network variables. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The necessary antenna can be connected by a SMA socket. The electrical connections are carried out with screw connection.

Receiving frequency: 868.3 MHz

Antenna terminal: SMA female

Transmission protocol: EnOcean

Main supply:

Nominal voltage: 12 V DC, SELV

Nominal current: 60 mA

Transceiver: TP/FT-10

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD)

Software: starting with LNS 3

Brand: Wieland Electric GmbH

Type: LON R-56/0 (RC)

Part No.: 83.020.0320.0

gesis® RM radio controlled input 2x8-fold

System gesis® RM - The extension module has 16 radio controlled inputs and will be managed by a system compatible base module. It can be fixed on a DIN rail and has to be assembled in a distribution box for decentralized installation. The input can map 170 radio channels to 16 input channels. The allocation of the radio channels to the input channels will be done at the module.

Main supply: via connection to base module

Connection to base module: ribbon cable, included in delivery

Inputs: 16 in two groups, 8 each

Receiving frequency: 868.3 MHz

Antenna terminal: SMA female

Transmission protocol: EnOcean

Type of protection: IP00

Mounting method: mounting rail TH35

Housing: black, halogen-free

Dimension in mm: 100x49x51 (HxWxD), width approx. 2.7 MW

Brand: Wieland Electric GmbH

Type: RM-16/0 (RC)

Part No.: 83.020.0408.0

## Handheld transmitter

gesis® RC handheld transmitter 4-channel, white

System gesis® RC - The white 4-channel battery-less, handheld radio (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. It has four rockers which can be used e.g. for light or shutter control.

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Dimension in mm: 50x82x21

Color: alike RAL 9010

Brand: Wieland Electric GmbH

Type: RC B-04WSSOH

Part No.: F0.000.0009.1

gesis® RC handheld transmitter4-channel, black

System gesis® RC - The black 4-channel battery, less handheld radio (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. It has four rockers which can be used e.g. for light or shutter control.

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Dimension in mm: 50x82x21

Color: alike RAL 9005

Brand: Wieland Electric GmbH

Type: RC B-04SWSOH

Part No.: F0.000.0009.2

gesis® RC handheld transmitter4-channel, silver

System gesis® RC - The silver finish 4-channel battery-less, handheld radio (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. It has four rockers which can be used e.g. for light or shutter control.

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Dimension in mm: 50x82x21

Color: silver finished

Brand: Wieland Electric GmbH

Type: RC B-04SISOH

Part No.: F0.000.0009.3

gesis® RC comfort handheld transmitter, black

System gesis® RC - The convenient handheld transmitter allows for control of the complete building. Whether complex lighting concepts or comprehensive actions according to a detailed schedule: this handheld terminal lets you program building functions in the twinkling of an eye. Menu navigation is intuitive and is supported by easily understandable symbols.

Additionally, the device offers service functions for the installer regarding range planning and can be used for function testing during commissioning.

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Buttons:

Control cross, single and short-cut buttons

Main supply:

3 AAA-NiMH batteries

Charging device: USB charging device and separate USB cable (included in delivery)

Dimension in mm: 165x55x21

Color: black

Brand: Wieland Electric GmbH

Type: RC B-00 SW SPH

Part No.: F0.000.0024.4

## Multivendor radio switches

gesis® RC multivendor radio switch, light 2-channel, white

System gesis® RC - The white 2-channel battery-less radio switch (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with I/O symbols. It fits into 55x55 mm frames from different switch manufacturers. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "I" / "O"

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: white

Brand: Wieland Electric GmbH

Type: RC B-02WSSPHB01

Part No.: F0.000.0005.6

gesis® RC multivendor radio switch, light 2-channel, anthracite

System gesis® RC - The anthracite 2-channel battery-less radio switch (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with I/O symbols. It fits into 55x55 mm frames from different switch manufacturers. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "I" / "O"

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: anthracite

Brand: Wieland Electric GmbH

Type: RC B-02ANSPHB01

Part No.: F0.000.0007.5

gesis® RC multivendor radio switch, light 2-channel, aluminumminum finished

System gesis® RC - The aluminum finished 2-channel battery-less radio switch (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with I/O symbols. It fits into 55x55 mm frames from different switch manufacturers. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "I" / "O"

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: aluminum finished

Brand: Wieland Electric GmbH

Type: RC B-02ALSPHB01

Part No.: F0.000.0007.6

gesis® RC multivendor radio switch, sunblind 2-channel, white

System gesis® RC - The white 2-channel battery-less radio switch (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with up/down symbols. It fits into 55x55 mm frames from different switch manufacturers. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "Up" / "Down" (symbols),

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: white

Brand: Wieland Electric GmbH

Type: RC B-02WSSPHB02

Part No.: F0.000.0005.8

gesis® RC multivendor radio switch, sunblind 2-channel, anthracite

System gesis® RC - The anthracite 2-channel battery-less radio switch (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with up/down symbols. It fits into 55x55 mm frames from different switch manufacturers. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "Up" / "Down" (symbols),

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: anthracite

Brand: Wieland Electric GmbH

Type: RC B-02ANSPHB02

Part No.: F0.000.0007.7

gesis® RC multivendor radio switch, sunblind 2-channel, aluminumminum finished

System gesis® RC - The aluminum finished 2-channel battery-less radio switch (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with up/down symbols. It fits into 55x55 mm frames from different switch manufacturers. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "Up" / "Down" (symbols),

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: aluminum finished

Brand: Wieland Electric GmbH

Type: RC B-02ALSPHB02

Part No.: F0.000.0007.8

gesis® RC multivendor radio switch, light 4-channel, white

System gesis® RC - The white 4-channel battery-less radio switch (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with I/O symbols. It fits into 55x55 mm frames from different switch manufacturers. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "I" / "O"

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: white

Brand: Wieland Electric GmbH

Type: RC B-04WSSPHB01

Part No.: F0.000.0005.7

gesis® RC multivendor radio switch, light 4-channel, anthracite

System gesis® RC - The anthracite 4-channel battery-less radio switch (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with I/O symbols. It fits into 55x55 mm frames from different switch manufacturers. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "I" / "O"

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: anthracite

Brand: Wieland Electric GmbH

Type: RC B-04ANSPHB01

Part No.: F0.000.0007.9

gesis® RC multivendor radio switch, light 4-channel, aluminumminum finished

System gesis® RC - The aluminum finished 4-channel battery-less radio switch (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with I/O symbols. It fits into 55x55 mm frames from different switch manufacturers. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "I" / "O"

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: aluminum finished

Brand: Wieland Electric GmbH

Type: RC B-04ALSPHB01

Part No.: F0.000.0008.0

gesis® RC multivendor radio switch, sunblind 4-channel, white

System gesis® RC - The white 4-channel battery-less radio switch (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with up/down symbols. It fits into 55x55 mm frames from different switch manufacturers. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "Up" / "Down" (symbols),

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: white

Brand: Wieland Electric GmbH

Type: RC B-04WSSPHB02

Part No.: F0.000.0005.9

gesis® RC multivendor radio switch, sunblind 4-channel, anthracite

System gesis® RC - The anthracite 4-channel battery-less radio switch (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with up/down symbols. It fits into 55x55 mm frames from different switch manufacturers. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "Up" / "Down" (symbols),

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: anthracite

Brand: Wieland Electric GmbH

Type: RC B-04ANSPHB02

Part No.: F0.000.0008.1

gesis® RC multivendor radio switch, sunblind 4-channel, aluminumminum finished

System gesis® RC - The aluminum finished 4-channel battery-less radio switch (EnOcean) generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with up/down symbols. It fits into 55x55 mm frames from different switch manufacturers. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "Up" / "Down" (symbols),

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: aluminum finished

Brand: Wieland Electric GmbH

Type: RC B-04ALSPHB02

Part No.: F0.000.0008.2

## Radio switch,

gesis® RC radio switch, light 2-channel, white

System gesis® RC - The white 2-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with I/O symbols. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "I" / "O"

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: white, bright surface

Brand: Wieland Electric GmbH

Type: RC B-02WSSPNB01

Part No.: F0.000.0025.0

gesis® RC radio switch, light 2-channel, piano black

System gesis® RC - The piano black 2-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with I/O symbols. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "I" / "O"

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: piano black, bright surface

Brand: Wieland Electric GmbH

Type: RC B-02SWSPNB01

Part No.: F0.000.0025.9

gesis® RC radio switch, light 2-channel, aluminum

System gesis® RC - The aluminum 2-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with I/O symbols. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "I" / "O"

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: aluminum, bright surface

Brand: Wieland Electric GmbH

Type: RC B-02ALSPNB01

Part No.: F0.000.0026.8

gesis® RC radio switch, sunblind 2-channel, white

System gesis® RC - The white 2-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with up/down symbols. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "Up" / "Down" (symbols),

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: white, bright surface

Brand: Wieland Electric GmbH

Type: RC B-02WSSPNB02

Part No.: F0.000.0025.2

gesis® RC radio switch, sunblind 2-channel, piano black

System gesis® RC - The piano black 2-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with up/down symbols. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "Up" / "Down" (symbols),

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: piano black, bright surface

Brand: Wieland Electric GmbH

Type: RC B-02SWSPNB02

Part No.: F0.000.0026.1

gesis® RC radio switch, sunblind 2-channel, aluminum

System gesis® RC - The aluminum 2-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with up/down symbols. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "Up" / "Down" (symbols),

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: aluminum, bright surface

Brand: Wieland Electric GmbH

Type: RC B-02ALSPNB02

Part No.: F0.000.0027.0

gesis® RC radio switch 2-channel, white

System gesis® RC - The white 2-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: white, bright surface

Brand: Wieland Electric GmbH

Type: RC B-02WSSPNB00

Part No.: F0.000.0025.4

gesis® RC radio switch 2-channel, piano black

System gesis® RC - The piano black 2-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: piano black, bright surface

Brand: Wieland Electric GmbH

Type: RC B-02SWSPNB00

Part No.: F0.000.0026.3

gesis® RC radio switch 2-channel, aluminum

System gesis® RC - The aluminum 2-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: aluminum, bright surface

Brand: Wieland Electric GmbH

Type: RC B-02ALSPNB00

Part No.: F0.000.0027.2

gesis® RC radio switch, light 4-channel, white

System gesis® RC - The white 4-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with I/O symbols. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "I" / "O"

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: white, bright surface

Brand: Wieland Electric GmbH

Type: RC B-04WSSPNB01

Part No.: F0.000.0025.1

gesis® RC radio switch, light 4-channel, piano black

System gesis® RC - The piano black 4-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with I/O symbols. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "I" / "O"

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: piano black, bright surface

Brand: Wieland Electric GmbH

Type: RC B-04SWSPNB01

Part No.: F0.000.0026.0

gesis® RC radio switch, light 4-channel, aluminum

System gesis® RC - The aluminum 4-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with I/O symbols. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "I" / "O"

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: aluminum, bright surface

Brand: Wieland Electric GmbH

Type: RC B-04ALSPNB01

Part No.: F0.000.0026.9

gesis® RC radio switch, sunblind 4-channel, white

System gesis® RC - The white 4-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with up/down symbols. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "Up" / "Down" (symbols),

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: white, bright surface

Brand: Wieland Electric GmbH

Type: RC B-04WSSPNB02

Part No.: F0.000.0025.3

gesis® RC radio switch, sunblind 4-channel, piano black

System gesis® RC - The piano black 4-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with up/down symbols. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "Up" / "Down" (symbols),

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: piano black, bright surface

Brand: Wieland Electric GmbH

Type: RC B-04SWSPNB02

Part No.: F0.000.0026.2

gesis® RC radio switch, sunblind 4-channel, aluminum

System gesis® RC - The aluminum 4-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position and marked with up/down symbols. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Marking: "Up" / "Down" (symbols),

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: aluminum, bright surface

Brand: Wieland Electric GmbH

Type: RC B-04ALSPNB02

Part No.: F0.000.0027.1

gesis® RC radio switch 4-channel, white

System gesis® RC - The white 4-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: white, bright surface

Brand: Wieland Electric GmbH

Type: RC B-04WSSPNB00

Part No.: F0.000.0025.5

gesis® RC radio switch 4-channel, piano black

System gesis® RC - The piano black 4-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: piano black, bright surface

Brand: Wieland Electric GmbH

Type: RC B-04SWSPNB00

Part No.: F0.000.0026.4

gesis® RC radio switch 4-channel, aluminum

System gesis® RC - The aluminum 4-channel battery-less radio switch (EnOcean) with bright surface generates its own energy while pressing the pushbutton and is maintenance-free. The rocker is in neutral center position. It fits into system compatible frames. It can be mounted on flat surfaces with screws or adhesive pads (included in delivery).

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: aluminum, bright surface

Brand: Wieland Electric GmbH

Type: RC B-04ALSPNB00

Part No.: F0.000.0027.3

gesis® RC combination frame 1-fold, white

System gesis® RC - White combination frame with bright surface for one radio switch 2 or 4 channel.

Color: white, bright surface

Dimension: 83x83 mm outside dimension

Brand: Wieland Electric GmbH

Type: RC A-BFWSSPN1F

Part No.: F0.000.0025.6

gesis® RC combination frame 1-fold, piano black

System gesis® RC - Piano black combination frame with bright surface for one radio switch 2 or 4 channel.

Color: piano black, bright surface

Dimension: 83x83 mm outside dimension

Brand: Wieland Electric GmbH

Type: RC A-BFSWSPN1F

Part No.: F0.000.0026.5

gesis® RC combination frame 1-fold, aluminum

System gesis® RC - Aluminum combination frame with bright surface for one radio switch 2 or 4 channel.

Color: aluminum, bright surface

Dimension: 83x83 mm outside dimension

Brand: Wieland Electric GmbH

Type: RC A-BFALSPN1F

Part No.: F0.000.0027.4

gesis® RC combination frame 2-fold, white

System gesis® RC - White combination frame with bright surface for two radio switch 2 or 4 channel.

Color: white, bright surface

Dimension: 83x83 mm outside dimension

Brand: Wieland Electric GmbH

Type: RC A-BFWSSPN2F

Part No.: F0.000.0025.7

gesis® RC combination frame 2-fold, piano black

System gesis® RC - Piano black combination frame with bright surface for two radio switch 2 or 4 channel.

Color: piano black, bright surface

Dimension: 83x83 mm outside dimension

Brand: Wieland Electric GmbH

Type: RC A-BFSWSPN2F

Part No.: F0.000.0026.6

gesis® RC combination frame 2-fold, aluminum

System gesis® RC - Aluminum combination frame with bright surface for two radio switch 2 or 4 channel.

Color: aluminum, bright surface

Dimension: 83x83 mm outside dimension

Brand: Wieland Electric GmbH

Type: RC A-BFALSPN2F

Part No.: F0.000.0027.5

gesis® RC combination frame 3-fold, white

System gesis® RC - White combination frame with bright surface for three radio switch 2 or 4 channel.

Color: white, bright surface

Dimension: 83x83 mm outside dimension

Brand: Wieland Electric GmbH

Type: RC A-BFWSSPN3F

Part No.: F0.000.0025.8

gesis® RC combination frame 3-fold, piano black

System gesis® RC - Piano black combination frame with bright surface for three radio switch 2 or 4 channel.

Color: piano black, bright surface

Dimension: 83x83 mm outside dimension

Brand: Wieland Electric GmbH

Type: RC A-BFSWSPN3F

Part No.: F0.000.0026.7

gesis® RC combination frame 3-fold, aluminum

System gesis® RC - Aluminum combination frame with bright surface for three radio switch 2 or 4 channel.

Color: aluminum, bright surface

Dimension: 83x83 mm outside dimension

Brand: Wieland Electric GmbH

Type: RC A-BFALSPN3F

Part No.: F0.000.0027.6

## Hotel-Card-Switch

gesis® RC hotel-card-switch, white

System gesis® RC - Energy self-sufficient, white hotel-card-switch for storage and simultaneous sending of an EnOcean telegram. Together with suitable actuators from the gesis® RC device series, the power supply of the room can be operated directly or the signal can be transmitted to the building automation.

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: white, bright surface

Brand: Wieland Electric GmbH

Type: RC S-SRWSCS

Part No.: F0.000.0024.6

gesis® RC hotel-card-switch, piano black

System gesis® RC - Energy self-sufficient, piano black hotel-card-switch for storage and simultaneous sending of an EnOcean telegram. Together with suitable actuators from the gesis® RC device series, the power supply of the room can be operated directly or the signal can be transmitted to the building automation.

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: piano black, bright surface

Brand: Wieland Electric GmbH

Type: RC S-SRSWCS

Part No.: F0.000.0024.7

gesis® RC hotel-card-switch, aluminum

System gesis® RC - Energy self-sufficient, aluminum hotel-card-switch for storage and simultaneous sending of an EnOcean telegram. Together with suitable actuators from the gesis® RC device series, the power supply of the room can be operated directly or the signal can be transmitted to the building automation.

Transmission frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Mounting:

Flush-mounted, without housing,

Screw or sticking fastening

Color: aluminum, bright surface

Brand: Wieland Electric GmbH

Type: RC S-SRALCS

Part No.: F0.000.0024.8

## Accessories

gesis® RC repeater

System gesis® RC - The repeater receives EnOcean telegrams and sends these as they are with maximum transmitting power, either in 1 or 2-level operation. This amplifies the radio signal twice at the maximum and enhances the radio range significantly.

Transmission/Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

Nominal range: 300 m on free field

Line of sight: approx. 50 m in floors, approx. 200 m in halls

Plasterboard / dry wood: approx. 30 m; approx. 5 walls

Brick walls / aerated concrete: approx. 20 m; approx. 3 walls

Supply voltage: 230 V AC

Type of protection: IP20

Mounting: flush-mounted e.g. in 55 mm outlet socket

Brand: Wieland Electric GmbH

Type: RC A-SRGN2L

Part No.: F0.000.0024.5

gesis® RC antenna 868 MHz SMA male

System gesis® RC - The antenna with SMA socket is for 868 MHz nominal frequency. The black antenna can be mounted using a magnetic foot and has a 2.5 m connection cable.

Transmission frequency: 868.3 MHz

Connection: SMA angle male plug

Cable length: 2.5 m

Mounting: magnet base

Dimension: 28.5 mm base diameter, 117 mm antenna height

Color: black

Brand: Wieland Electric GmbH

Type: RC A-A1SWL25

Part No.: 83.020.0503.0

# gesis® ELECTRONIC IP+ – EnOcean Receiver and LED control gear IP68

## EnOcean Receiver

gesis® RC radio based switching output 1-fold, IP68

System gesis® RC - The EnOcean switching output has an IP68 housing for surface mounting with one relay output as well as a forwarded main supply and can be controlled by up to 30 EnOcean pushbuttons. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

Count: 1

Type: normally open 1-pole, phase switched

Nominal voltage: 230 V, 50...60 Hz

Nominal load: 1100 VA ohmic load

Connection: pluggable

1 through wiring

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 20 A

Connection: pluggable

Mounting: on-wall, screw fastening

Type of protection: IP68

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: black

Dimension in mm: 58x104x162 (HxWxL)

Brand: Wieland Electric GmbH

Type: RC RST-0/1

Part No.: 83.020.0504.0

gesis® RC radio based switching output 1x2-fold, IP68

System gesis® RC - The EnOcean switching output has an IP68 housing for surface mounting with one relay output, connected to two connectors and can be controlled by up to 30 EnOcean pushbuttons. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

Count: 1

Type: normally open 1-pole, phase switched

Nominal voltage: 230 V, 50...60 Hz

Nominal load: 1100 VA ohmic load

Connection: pluggable

1 through wiring

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 20 A

Connection: pluggable, 2-fold parallel

Mounting: on-wall, screw fastening

Type of protection: IP68

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: black

Dimension in mm: 58x104x162 (HxWxL)

Brand: Wieland Electric GmbH

Type: RC RST-0/1x2

Part No.: 83.020.0504.1

gesis® RC radio based switching output 4-fold, IP68

System gesis® RC - The EnOcean switching output has an IP68 housing for surface mounting with four independent relay outputs as well as a forwarded main supply and can be controlled by up to 30 EnOcean pushbuttons. All electrical connections are pluggable.

Receiving frequency: 868.3 MHz

Transmission protocol: EnOcean

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

Count: 4

Type: normally open 1-pole, phase switched

Nominal voltage: 230 V, 50...60 Hz

Nominal load: each output max. 6 A ohmic load

Connection: pluggable

1 through wiring

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 20 A

Connection: pluggable, 2-fold parallel

Mounting: on-wall, screw fastening

Type of protection: IP68

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: black

Dimension in mm: 96x104x162 (HxWxL)

Brand: Wieland Electric GmbH

Type: RC RST-0/4

Part No.: 83.020.0505.0

## Constant current generator

gesis® ELECTRONIC IP+ constant current generator 350 mA DC

System gesis® ELECTRONIC IP+ - The power supply in IP68 surface-mounted housing is suitable for the connection of LED applications with a nominal current of 350 mA. The power supply delivers up to 12 Watts of power and has a through-wired power supply. All electrical connections are pluggable.

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

1 mains output, through wiring

1 LED output

Nominal current: 350 mA DC

Nominal load: 12 W

Connections: steckbar

Ambient temperature: -25 °C up to +55 °C

Mounting: on-wall, screw fastening

Type of protection: IP68

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: black

Dimension in mm: 96x104x162 (HxWxL)

Brand: Wieland Electric GmbH

Type: RST PSI 350/12 LED

Part No.: 83.020.0902.0

gesis® ELECTRONIC IP+ constant current generator 700 mA DC

System gesis® ELECTRONIC IP+ - The power supply in IP68 surface-mounted housing is suitable for the connection of LED applications with a nominal current of 700 mA. The power supply delivers up to 12 Watts of power and has a through-wired power supply. All electrical connections are pluggable.

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

1 mains output, through wiring

1 LED output

Nominal current: 700 mA DC

Nominal load: 12 W

Connections: steckbar

Ambient temperature: -25 °C up to +55 °C

Mounting: on-wall, screw fastening

Type of protection: IP 68

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: black

Dimension in mm: 96x104x162 (HxWxL)

Brand: Wieland Electric GmbH

Type: RST PSI 700/12 LED

Part No.: 83.020.0903.0

## Constant voltage generator

gesis® ELECTRONIC IP+ constant voltage generator 12 V DC

System gesis® ELECTRONIC IP+ - The power supply in IP68 surface-mounted housing is suitable for the connection of LED applications with a nominal voltage of 12 V. The power supply delivers up to 12 Watts of power and has a through-wired power supply. All electrical connections are pluggable.

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

1 mains output, through wiring

1 LED output

Nominal voltage: 12 V DC

Nominal load: 12 W

Connections: steckbar

Ambient temperature: -25 °C up to +55 °C

Mounting: on-wall, screw fastening

Type of protection: IP68

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: black

Dimension in mm: 96x104x162 (HxWxL)

Brand: Wieland Electric GmbH

Type: RST PSU 12/12 LED

Part No.: 83.020.0900.0

gesis® ELECTRONIC IP+ constant voltage generator 24 V DC

System gesis® ELECTRONIC IP+ - The power supply in IP68 surface-mounted housing is suitable for the connection of LED applications with a nominal voltage of 24 V. The power supply delivers up to 12 Watts of power and has a through-wired power supply. All electrical connections are pluggable.

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

1 mains output, through wiring

1 LED output

Nominal voltage: 24 V DC

Nominal load: 12 W

Connections: steckbar

Ambient temperature: -25 °C up to +55 °C

Mounting: on-wall, screw fastening

Type of protection: IP68

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: black

Dimension in mm: 96x104x162 (HxWxL)

Brand: Wieland Electric GmbH

Type: RST PSU 24/12 LED

Part No.: 83.020.0901.0

## Transformer for low-voltage halogen luminaires

gesis® ELECTRONIC IP+ transformer for low-voltage halogen luminaires 12 V AC

System gesis® ELECTRONIC IP+ - The electronic transformer in IP68 surface-mounted housing is suitable for the connection of low-voltage halogen luminaire applications with a nominal voltage of 12 V. The power supply delivers 20 - 70 Watts of power and has a through-wired power supply. All electrical connections are pluggable.

Main supply:

Nominal voltage: 230 V, 50...60 Hz

Nominal current: 16 A

Connection: pluggable

Outputs:

1 mains output, through wiring

1 output for low-voltage halogen luminaires

Nominal voltage: 12 V AC

Nominal load: 20-70 W

Connections: steckbar

Ambient temperature: 0 °C up to +45 °C

Mounting: on-wall, screw fastening

Type of protection: IP68

Housing: halogen-free

Fire behavior: UL 94-V-2

Housing color: black

Dimension in mm: 96x104x162 (HxWxL)

Brand: Wieland Electric GmbH

Type: RST PSU 12/70 LVH

Part No.: 83.020.0904.0

## Accessories

gesis® Cover piece IP66/68 for male, 2-3-pole, captive against loss, black

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i2 and RST20i3, captive against loss, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2 VS SW

Part No.: 99.416.6205.2

gesis® Cover piece IP66/68 for male, 2-3-pole, black

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i2 and RST20i3, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2 VS SW

Part No.: 05.564.4453.1

gesis® Cover piece IP66/68 for female, 2-3-pole, captive against loss, black

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i2 and RST20i3, with locking, captive against loss, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2 VS SW

Part No.: 99.414.6205.2

gesis® Cover piece IP66/68 for female, 2-3-pole, black

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i2 and RST20i3, with locking, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2 VS SW

Part No.: Z5.564.4553.1

05.564.4453.1	108

83.020.0212.0	46

83.020.0212.4	47

83.020.0213.0	48

83.020.0213.4	48

83.020.0214.0	44

83.020.0220.0	50, 81

83.020.0220.1	51, 82

83.020.0220.2	51, 82

83.020.0220.3	52, 83

83.020.0221.0	45

83.020.0221.4	45

83.020.0225.0	43

83.020.0225.4	44

83.020.0300.3	31

83.020.0320.0	41, 83

83.020.0400.3	20

83.020.0401.0	21, 32

83.020.0402.0	22, 33

83.020.0403.0	23, 34

83.020.0404.0	24, 35

83.020.0405.0	25, 36

83.020.0406.0	27, 38

83.020.0407.0	24, 35

83.020.0408.0	29, 40, 83

83.020.0409.0	25, 36

83.020.0410.0	26, 37

83.020.0411.0	27, 38

83.020.0412.0	28, 39

83.020.0421.0	21, 32

83.020.0500.0	72

83.020.0500.2	73

83.020.0501.1	73

83.020.0501.2	74

83.020.0502.0	79

83.020.0503.0	30, 42, 53, 102

83.020.0504.0	75, 103

83.020.0504.1	76, 104

83.020.0505.0	76, 104

83.020.0506.0	78

83.020.0600.0	3

83.020.0600.1	4

83.020.0601.0	5

83.020.0601.1	5

83.020.0610.0	6

83.020.0610.1	6

83.020.0611.0	7

83.020.0611.1	7

83.020.0622.0	8

83.020.0622.1	9

83.020.0623.0	10

83.020.0623.1	11

83.020.0624.0	12

83.020.0624.1	13

83.020.0660.0	14

83.020.0661.0	14

83.020.0662.0	15

83.020.0663.0	15

83.020.0900.0	106

83.020.0901.0	106

83.020.0902.0	105

83.020.0903.0	105

83.020.0904.0	107

83.020.1020.0	54

83.020.1021.0	55

83.020.1022.0	55

83.020.1023.0	56

83.020.1024.0	57

83.020.1026.0	58

83.020.1400.0	60

83.020.1404.0	66

83.020.1405.0	66

83.020.1406.0	67

83.020.1413.0	68

83.020.1414.0	68

83.020.1415.0	69

83.020.1416.0	69

83.020.1417.0	70

83.020.1418.0	69

91.257.0500.2	16

91.257.1000.2	16

99.002.9999.9	59

99.400.9999.8	16

99.401.9999.8	17

99.414.6205.2	108

99.416.6205.2	108

F0.000.0005.6	86

F0.000.0005.7	88

F0.000.0005.8	87

F0.000.0005.9	89

F0.000.0007.5	86

F0.000.0007.6	87

F0.000.0007.7	87

F0.000.0007.8	88

F0.000.0007.9	89

F0.000.0008.0	89

F0.000.0008.1	90

F0.000.0008.2	90

F0.000.0008.3	70

F0.000.0009.0	80

F0.000.0009.1	84

F0.000.0009.2	84

F0.000.0009.3	84

F0.000.0016.9	77

F0.000.0017.0	77

F0.000.0017.3	62

F0.000.0024.4	85

F0.000.0024.5	102

F0.000.0024.6	100

F0.000.0024.7	100

F0.000.0024.8	101

F0.000.0025.0	91

F0.000.0025.1	94

F0.000.0025.2	92

F0.000.0025.3	95

F0.000.0025.4	93

F0.000.0025.5	97

F0.000.0025.6	98

F0.000.0025.7	98

F0.000.0025.8	99

F0.000.0025.9	91

F0.000.0026.0	95

F0.000.0026.1	92

F0.000.0026.2	96

F0.000.0026.3	94

F0.000.0026.4	97

F0.000.0026.5	98

F0.000.0026.6	98

F0.000.0026.7	99

F0.000.0026.8	92

F0.000.0026.9	95

F0.000.0027.0	93

F0.000.0027.1	96

F0.000.0027.2	94

F0.000.0027.3	97

F0.000.0027.4	98

F0.000.0027.5	98

F0.000.0027.6	99

F0.000.0032.0	63

F0.000.0032.1	64

F0.000.0032.2	61

F0.000.0032.3	64

F0.000.0032.4	64

F0.000.0032.5	65

F0.000.0032.6	64

F0.000.0032.7	63

F0.000.0032.8	65

F0.000.0033.8	70

Z5.524.1410.0	18

Z5.524.1510.0	18

Z5.524.1610.0	18

Z5.524.1710.0	19

Z5.524.1810.0	19

Z5.524.1910.0	19

Z5.524.2010.0	19

Z5.564.4553.1	108