1	gesis® FLEX – Modular, flat, direct pluggable KNX building automation system	2

1.1	Base modules	2

1.2	Power supply modules	5

1.3	Binary inputs	7

1.4	Binary outputs	9

1.5	Shutter outputs	11

1.6	System-compatible housings	13

1.7	Extension cables	15

1.8	Mounting frames	17

# gesis® FLEX – Modular, flat, direct pluggable KNX building automation system

The modular KNX series gesis® FLEX is designed for decentral installation without further housing. A device always consists of a base module and expansion modules. The modules can control lighting, shutters, valves or integrate potential-free contacts with binary inputs in building automation. The mains supply and the internal bus contact automatically when the modules are combined. In-between feed-in modules allow separate fuses for different functions.
Because of the flat shape, the connection from one side, well-thought-out mounting options and the modular concept of this system fits in almost any space. The strictly pluggable design allows a fast, secure, and simple connection. The manual control directly on the modules simplifies start-up and troubleshooting. In combination with the plug ability this results in a clear interface between system integration and installation. Because only standard modules are used, changes during the planning, implementation or operational phase can be realized quickly.

## Base modules

gesis® FLEX base module with 3-phase supply

System gesis® FLEX - The 3-phase supplied KNX base module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, supports 6 expansion modules. They support all the common inputs and outputs, and they provide extensive room automation with only one physical address. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation.

Supply KNX:

Nominal voltage: KNX System voltage

Nominal current: ca. 5 mA

Supply mains:

Nominal voltage: 230/400 V AC

Nominal current: 3x16 A

Expandability:

Expansion module: 6, system-compatible

Power supply module: any

System-compatible housing: any

System extension: with pre-fabricated cable max. 1 m

Maximum length: summation of all modules width incl. system extension

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: connections for sensors and loads according to IEC 61535, incl.

mains supply, KNX connection according to KNX handbook

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 115 mm (127 mm incl. left and right end cap)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed end caps are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis KNX FLEX-BAS

Part No.: 83.020.0600.0

gesis® FLEX base module with 3-phase supply incl. gesis® plugs

System gesis® FLEX - The 3-phase supplied KNX base module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, supports 6 expansion modules. They support all the common inputs and outputs, and they provide extensive room automation with only one physical address. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation. All necessary plugs are enclosed.

Supply KNX:

Nominal voltage: KNX System voltage

Nominal current: ca. 5 mA

Supply mains:

Nominal voltage: 230/400 V AC

Nominal current: 3x16 A

Expandability:

Expansion module: 6, system-compatible

Power supply module: any

System-compatible housing: any

System extension: with pre-fabricated cable max. 1 m

Maximum length: summation of all modules width incl. system extension

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: connections for sensors and loads according to IEC 61535, incl.

mains supply, KNX connection according to KNX handbook

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 115 mm (127 mm incl. left and right end cap)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed end caps as well as plugs are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis KNX FLEX-BAS Z

Part No.: 83.020.0600.1

gesis® FLEX base module with 1-phase supply

System gesis® FLEX - The 1-phase supplied KNX base module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, supports 6 expansion modules. They support all the common inputs and outputs, and they provide extensive room automation with only one physical address. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation.

Supply KNX:

Nominal voltage: KNX System voltage

Nominal current: ca. 5 mA

Supply mains:

Nominal voltage: 230 V AC

Nominal current: 16 A

Expandability:

Expansion module: 6, system-compatible

Power supply module: any

System-compatible housing: any

System extension: with pre-fabricated cable max. 1 m

Maximum length: summation of all modules width incl. system extension

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: connections for sensors and loads according to IEC 61535, incl.

mains supply, KNX connection according to KNX handbook

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 115 mm (127 mm incl. left and right end cap)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed end caps are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis KNX FLEX-BAS SP

Part No.: 83.020.0601.0

gesis® FLEX base module with 1-phase supply incl. gesis® plugs

System gesis® FLEX - The 1-phase supplied KNX base module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, supports 6 expansion modules. They support all the common inputs and outputs, and they provide extensive room automation with only one physical address. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation. All necessary plugs are enclosed.

Supply KNX:

Nominal voltage: KNX System voltage

Nominal current: ca. 5 mA

Supply mains:

Nominal voltage: 230 V AC

Nominal current: 16 A

Expandability:

Expansion module: 6, system-compatible

Power supply module: any

System-compatible housing: any

System extension: with pre-fabricated cable max. 1 m

Maximum length: summation of all modules width incl. system extension

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: connections for sensors and loads according to IEC 61535, incl.

mains supply, KNX connection according to KNX handbook

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 115 mm (127 mm incl. left and right end cap)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed end caps as well as plugs are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis KNX FLEX-BAS SP Z

Part No.: 83.020.0601.1

## Power supply modules

gesis® FLEX power supply module 3-phase

System gesis® FLEX - The 3-phase power supply module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, allows a mains supply separate from the base module within a modular system. This means that the output loads can be split over different fuse circuits. It can be integrated in the system as often as required. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation.

Supply mains:

Nominal voltage: 230/400 V AC

Nominal current: 3x16 A

Electrical connections: Mains supply according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 95 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-MS

Part No.: 83.020.0610.0

gesis® FLEX power supply module 3-phase incl. gesis® plugs

System gesis® FLEX - The 3-phase power supply module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, allows a mains supply separate from the base module within a modular system. This means that the output loads can be split over different fuse circuits. It can be integrated in the system as often as required. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation. All necessary plugs are enclosed.

Supply mains:

Nominal voltage: 230/400 V AC

Nominal current: 3x16 A

Electrical connections: Mains supply according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 95 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed plugs are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis FLEX-MS Z

Part No.: 83.020.0610.1

gesis® FLEX power supply module 1-phase

The 1-phase power supply module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, allows a mains supply separate from the base module within a modular system. This means that the output loads can be split over different fuse circuits. It can be integrated in the system as often as required. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation.

Supply mains:

Nominal voltage: 230 V AC

Nominal current: 16 A

Electrical connections: Mains supply according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 95 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-MS SP

Part No.: 83.020.0611.0

gesis® FLEX power supply module 1-phase incl. gesis® plugs

System gesis® FLEX - The 1-phase power supply module with flat surface mounted housing, which can be fitted on DIN rails for decentralized installation, allows a mains supply separate from the base module within a modular system. This means that the output loads can be split over different fuse circuits. It can be integrated in the system as often as required. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation. All necessary plugs are enclosed.

Supply mains:

Nominal voltage: 230 V AC

Nominal current: 16 A

Electrical connections: Mains supply according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 95 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed plugs are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis FLEX-MS SP Z

Part No.: 83.020.0611.1

## Binary inputs

gesis® FLEX binary input 8-fold

System gesis® FLEX - The 8-fold binary input 12 VDC, for connecting potential-free contacts, with flat surface mounted housing which can be fitted on in DIN rail for decentralized installation, is managed by the base module. It receives mains and bus supply from the upstream module. The extensive parameter set enables different automation functions. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation.

Supply KNX: via upstream module

Supply mains: via upstream module

Signal voltage: 12 V DC (SELV)

Power-on time: 100 % for all inputs at a time

Max. cable length: 100 m

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: all connections for sensors according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 95 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-8/0 (12)

Part No.: 83.020.0622.0

gesis® FLEX binary input 8-fold incl. gesis® plugs

System gesis® FLEX - The 8-fold binary input 12 VDC, for connecting potential-free contacts, with flat surface mounted housing which can be fitted on in DIN rail for decentralized installation, is managed by the base module. It receives mains and bus supply from the upstream module. The extensive parameter set enables different automation functions. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation. All necessary plugs are enclosed.

Supply KNX: via upstream module

Supply mains: via upstream module

Signal voltage: 12 V DC (SELV)

Power-on time: 100 % for all inputs at a time

Max. cable length: 100 m

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: all connections for sensors according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 95 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed plugs are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis FLEX-8/0 (12) Z

Part No.: 83.020.0622.1

## Binary outputs

gesis® FLEX binary output 4-fold

System gesis® FLEX - The 4-fold relay output 230 V/16 A, with flat surface mounted housing which can be fitted on DIN rails for decentralized installation, is managed by the base module. It receives mains and bus supply from the upstream module. The extensive parameter set enables different automation functions. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation.

Supply KNX: via upstream module

Supply mains: via upstream module

Nominal voltage: 230 V AC

Nominal current: 16 A (ohmic load)

Inrush current: max. 200 A (50 ms)

Number: 4 binary outputs (bistable relay)

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: all connections for loads according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 130 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-0/4

Part No.: 83.020.0623.0

gesis® FLEX binary output 4-fold incl. gesis® plugs

System gesis® FLEX - The 4-fold relay output 230 V/16 A, with flat surface mounted housing which can be fitted on DIN rails for decentralized installation, is managed by the base module. It receives mains and bus supply from the upstream module. The extensive parameter set enables different automation functions. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation. All necessary plugs are enclosed.

Supply KNX: via upstream module

Supply mains: via upstream module

Nominal voltage: 230 V AC

Nominal current: 16 A (ohmic load)

Inrush current: max. 200 A (50 ms)

Number: 4 binary outputs (bistable relay)

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: all connections for loads according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 130 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed plugs are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis FLEX-0/4 Z

Part No.: 83.020.0623.1

## Shutter outputs

gesis® FLEX shutter output 2-fold

System gesis® FLEX - The 2-fold shutter output 230 V/8 A, with flat surface mounted housing which can be fitted on in DIN rail for decentralized installation, is managed by the base module. It receives mains and bus supply from the upstream module. The parameter set enables different automation functions. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation.

Supply KNX: via upstream module

Supply mains: via upstream module

Nominal voltage: 230 V AC

Nominal current: 8 A (ohmic load)

Number: 2 shutter outputs (4-pole, up/down)

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: all connections for loads according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 130 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-0/2W

Part No.: 83.020.0624.0

gesis® FLEX shutter output 2-fold incl. gesis® plugs

System gesis® FLEX - The 2-fold shutter output 230 V/8 A, with flat surface mounted housing which can be fitted on in DIN rail for decentralized installation, is managed by the base module. It receives mains and bus supply from the upstream module. The parameter set enables different automation functions. The manual operation level allows function tests without prior system integration. The electrical connections, which are pluggable in accordance with IEC 61535, separate automation and installation. All necessary plugs are enclosed.

Supply KNX: via upstream module

Supply mains: via upstream module

Nominal voltage: 230 V AC

Nominal voltage: 230 V AC

Nominal current: 8 A (ohmic load)

Number: 2 shutter outputs (4-pole, up/down)

Manual control: buttons on module

Status bar: LEDs on module

Electrical connections: all connections for loads according to IEC 61535

Protection class: IP20

Housing: halogen-free

Flammability class: UL 94-V-2

Housing color: upper part light grey, lower part black

Dimensions:

Length: 130 mm (assembled)

Width: 149 mm incl. plug locking

Height: 44 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Accessories: needed plugs are part of the delivery

Brand: Wieland Electric GmbH

Type: gesis FLEX-0/2W Z

Part No.: 83.020.0624.1

## System-compatible housings

gesis® FLEX system-compatible housing 4 MW

System gesis® FLEX - The system-compatible housing module for DIN rail surface mounting for decentralized installation can be used to install DIN rail mounted devices according to DIN 43880 with up to four module width. Mains and bus supply are passed from upstream to downstream module. Main supply can be internally gripped. Cable glands have to be yield on side.

Mounting possibility: DIN rail mounted device according to DIN 43880, 4 MW (72 mm)

Supply KNX: extern

Supply mains: via upstream module, can be gripped internally

Through wiring: Mains- and bus are passed from upstream to downstream module

Dimensions:

Length: 130 mm (assembled)

Width: approx. 140 mm

Height: 80 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-REG4

Part No.: 83.020.0660.0

gesis® FLEX system-compatible housing 4 MW with cable glands

System gesis® FLEX - The system-compatible housing module for DIN rail surface mounting for decentralized installation can be used to install DIN rail mounted devices according to DIN 43880 with up to four module width. Mains and bus supply are passed from upstream to downstream module. Main supply can be internally gripped. The module comes with 3 cable glands.

Mounting possibility: DIN rail mounted device according to DIN 43880, 4 MW (72 mm)

Supply KNX: extern

Supply mains: via upstream module, can be gripped internally

Through wiring: Mains- and bus are passed from upstream to downstream module

Cable glands: 1x cable diameter 5-9 mm, 2x cable diameter 7-13 mm

Dimensions:

Length: 130 mm (assembled)

Width: approx. 173 mm (incl. cable glands)

Height: 80 mm without DIN rail

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-REG4 V

Part No.: 83.020.0661.0

gesis® FLEX system-compatible housing 4 MW with clear cover

System gesis® FLEX - The system-compatible housing module for DIN rail surface mounting for decentralized installation can be used to install DIN rail mounted devices according to DIN 43880 with up to four module width. Mains and bus supply are passed from upstream to downstream module. Main supply can be internally gripped. Cable glands have to be yield on side. The module has a clear cover to protect the internal device.

Mounting possibility: DIN rail mounted device according to DIN 43880, 4 MW (72 mm)

Supply KNX: extern

Supply mains: via upstream module, can be gripped internally

Through wiring: Mains- and bus are passed from upstream to downstream module

Clear cover: for 4 MW

Dimensions:

Length: 130 mm (assembled)

Width: approx. 140 mm

Height: 94 mm without DIN rail (incl. clear cover)

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-REG4 D

Part No.: 83.020.0662.0

gesis® FLEX system-compatible housing 4 MW with cable glands and clear cover

System gesis® FLEX - The system-compatible housing module for DIN rail surface mounting for decentralized installation can be used to install DIN rail mounted devices according to DIN 43880 with up to four module width. Mains and bus supply are passed from upstream to downstream module. Main supply can be internally gripped. The module comes with 3 cable glands and has a clear cover to protect the internal device.

Mounting possibility: DIN rail mounted device according to DIN 43880, 4 MW (72 mm)

Supply KNX: extern

Supply mains: via upstream module, can be gripped internally

Through wiring: Mains- and bus are passed from upstream to downstream module

Cable glands: 1x cable diameter 5-9 mm, 2x cable diameter 7-13 mm

Clear cover: for 4 MW

Dimensions:

Length: 130 mm (assembled)

Width: approx. 173 mm (incl. cable glands)

Height: 94 mm without DIN rail (incl. clear cover)

Mounting: surface mounted, DIN rail TH35, system-compatible mounting frame or in flat mounting areas

Brand: Wieland Electric GmbH

Type: gesis FLEX-REG4 DV

Part No.: 83.020.0663.0

## Extension cables

gesis® FLEX extension cable mains 0.5 m

System gesis® FLEX - An extension of the internal mains for the flat, DIN rail surface mounted system for decentralized installation is possible with up to 1.0 m. It interlocks automatically if it is plugged. Because of the mechanical coding main and bus supply cannot be mixed.

Length: 0.5 m

Nominal voltage: 230/400 V AC

Nominal current: 3x16 A

Plug-system: GST15i5 white

Brand: Wieland Electric GmbH

Type: GST15i5KS BS X15 V 05WS

Part No.: 91.257.0500.2

gesis® FLEX extension cable mains 1.0 m

System gesis® FLEX - An extension of the internal mains for the flat, DIN rail surface mounted system for decentralized installation is possible with up to 1.0 m. It interlocks automatically if it is plugged. Because of the mechanical coding main and bus supply cannot be mixed.

Length: 1.0 m

Nominal voltage: 230/400 V AC

Nominal current: 3x16 A

Plug-system: GST15i5 white

Brand: Wieland Electric GmbH

Type: GST15i5KS BS X15 V 10WS

Part No.: 91.257.1000.2

gesis® FLEX extension cable bus 0.5 m

System gesis® FLEX - An extension of the internal bus for the flat, DIN rail surface mounted system for decentralized installation is possible with up to 1.0 m. It interlocks automatically if it is plugged. Because of the mechanical coding main and bus supply cannot be mixed.

Length: 0.5 m

Nominal voltage: 50 V

Nominal current: 10 A

Plug-system: GST15i5 lighting blue

Brand: Wieland Electric GmbH

Type: GST15i5KS BSX05_V 05BL02

Part No.: 99.400.9999.8

gesis® FLEX extension cable bus 1.0 m

System gesis® FLEX - An extension of the internal bus for the flat, DIN rail surface mounted system for decentralized installation is possible with up to 1.0 m. It interlocks automatically if it is plugged. Because of the mechanical coding main and bus supply cannot be mixed.

Length: 1.0 m

Nominal voltage: 50 V

Nominal current: 10 A

Plug-system: GST15i5 lighting blue

Brand: Wieland Electric GmbH

Type: GST15i5KS BSX05_V 10BL02

Part No.: 99.401.9999.8

## Mounting frames

gesis® FLEX mounting frame 40 cm

System gesis® FLEX - The fit-up aid for the flat, DIN rail surface mounted system for decentralized installation alleviates the mounting to cable trays, in suspended ceilings or raised floors. It grabs different numbers of modules according to its length and comes with a fixing possibility for connected cables. The hole pattern and incl. screws enable a quick mounting.

Length: 40 cm

DIN rail: TH35x7.5

Locking holes: round-, long- and keyhole

Fixing material: roundhead and hook screw for cable trays are part of the delivery

Brand: Wieland Electric GmbH

Type: MB TH35-7,5 HK 40x20 Z

Part No.: Z5.524.1410.0

gesis® FLEX mounting frame 50 cm

System gesis® FLEX - The fit-up aid for the flat, DIN rail surface mounted system for decentralized installation alleviates the mounting to cable trays, in suspended ceilings or raised floors. It grabs different numbers of modules according to its length and comes with a fixing possibility for connected cables. The hole pattern and incl. screws enable a quick mounting.

Length: 50 cm

DIN rail: TH35x7.5

Locking holes: round-, long- and keyhole

Fixing material: roundhead and hook screw for cable trays are part of the delivery

Brand: Wieland Electric GmbH

Type: MB TH35-7,5 HK 50x20 Z

Part No.: Z5.524.1510.0

gesis® FLEX mounting frame 60 cm

System gesis® FLEX - The fit-up aid for the flat, DIN rail surface mounted system for decentralized installation alleviates the mounting to cable trays, in suspended ceilings or raised floors. It grabs different numbers of modules according to its length and comes with a fixing possibility for connected cables. The hole pattern and incl. screws enable a quick mounting.

Length: 60 cm

DIN rail: TH35x7.5

Locking holes: round-, long- and keyhole

Fixing material: roundhead and hook screw for cable trays are part of the delivery

Brand: Wieland Electric GmbH

Type: MB TH35-7,5 HK 60x20 Z

Part No.: Z5.524.1610.0

gesis® FLEX mounting frame 70 cm

System gesis® FLEX - The fit-up aid for the flat, DIN rail surface mounted system for decentralized installation alleviates the mounting to cable trays, in suspended ceilings or raised floors. It grabs different numbers of modules according to its length and comes with a fixing possibility for connected cables. The hole pattern and incl. screws enable a quick mounting.

Length: 70 cm

DIN rail: TH35x7.5

Locking holes: round-, long- and keyhole

Fixing material: roundhead and hook screw for cable trays are part of the delivery

Brand: Wieland Electric GmbH

Type: MB TH35-7,5 HK 70x20 Z

Part No.: Z5.524.1710.0

gesis® FLEX mounting frame 80 cm

System gesis® FLEX - The fit-up aid for the flat, DIN rail surface mounted system for decentralized installation alleviates the mounting to cable trays, in suspended ceilings or raised floors. It grabs different numbers of modules according to its length and comes with a fixing possibility for connected cables. The hole pattern and incl. screws enable a quick mounting.

Length: 80 cm

DIN rail: TH35x7.5

Locking holes: round-, long- and keyhole

Fixing material: roundhead and hook screw for cable trays are part of the delivery

Brand: Wieland Electric GmbH

Type: MB TH35-7,5 HK 80x20 Z

Part No.: Z5.524.1810.0

gesis® FLEX mounting frame 90 cm

System gesis® FLEX - The fit-up aid for the flat, DIN rail surface mounted system for decentralized installation alleviates the mounting to cable trays, in suspended ceilings or raised floors. It grabs different numbers of modules according to its length and comes with a fixing possibility for connected cables. The hole pattern and incl. screws enable a quick mounting.

Length: 90 cm

DIN rail: TH35x7.5

Locking holes: round-, long- and keyhole

Fixing material: roundhead and hook screw for cable trays are part of the delivery

Brand: Wieland Electric GmbH

Type: MB TH35-7,5 HK 90x20 Z

Part No.: Z5.524.1910.0

gesis® FLEX mounting frame 100 cm

System gesis® FLEX - The fit-up aid for the flat, DIN rail surface mounted system for decentralized installation alleviates the mounting to cable trays, in suspended ceilings or raised floors. It grabs different numbers of modules according to its length and comes with a fixing possibility for connected cables. The hole pattern and incl. screws enable a quick mounting.

Length: 100 cm

DIN rail: TH35x7.5

Locking holes: round-, long- and keyhole

Fixing material: roundhead and hook screw for cable trays are part of the delivery

Brand: Wieland Electric GmbH

Type: MB TH35-7,5 HK 100x20 Z

Part No.: Z5.524.2010.0

83.020.0600.0	2

83.020.0600.1	3

83.020.0601.0	4

83.020.0601.1	4

83.020.0610.0	5

83.020.0610.1	5

83.020.0611.0	6

83.020.0611.1	6

83.020.0622.0	7

83.020.0622.1	8

83.020.0623.0	9

83.020.0623.1	10

83.020.0624.0	11

83.020.0624.1	12

83.020.0660.0	13

83.020.0661.0	13

83.020.0662.0	14

83.020.0663.0	14

91.257.0500.2	15

91.257.1000.2	15

99.400.9999.8	15

99.401.9999.8	16

Z5.524.1410.0	17

Z5.524.1510.0	17

Z5.524.1610.0	17

Z5.524.1710.0	18

Z5.524.1810.0	18

Z5.524.1910.0	18

Z5.524.2010.0	18