1	gesis® MINI - Building installation systems	2

1.1	2-pole - GST15i2	2

1.1.1	Connectors	2

1.1.1.1	Female connector with screw connection	2

1.1.1.2	Male with screw connection	7

1.1.2	Snap-In	12

1.1.2.1	Female connector with screw connection	12

1.1.2.2	Male with screw connection	15

1.1.3	Cables	18

1.1.3.1	Cable assemblies, 1.5 mm², containing halogen	18

1.1.3.2	Cable assemblies, 1.5 mm², halogen-free	22

1.2	3-pole - GST15i3	26

1.2.1	Connectors	26

1.2.1.1	Female connector with screw connection	26

1.2.1.2	Male with screw connection	29

1.2.2	Snap-In	32

1.2.2.1	Female connector with screw connection	32

1.2.2.2	Male with screw connection	35

1.2.3	Distribution blocks	38

1.2.4	Accessories	41

1.2.5	Cables	43

1.2.5.1	Cable assemblies, 1.5 mm², containing halogen	43

1.2.5.2	Cable assemblies, 1.5 mm², halogen-free	47

1.2.6	Assembled Cables	50

1.3	4-pole - GST15i4	52

1.3.1	Connectors	52

1.3.1.1	Female connector with screw connection	52

1.3.1.2	Male with screw connection	54

1.3.2	Snap-In	56

1.3.2.1	Female connector with screw connection	56

1.3.2.2	Male with screw connection	57

1.3.3	Cables	58

1.3.3.1	Cable assemblies, 1.5 mm², containing halogen	58

1.3.3.2	Cable assemblies, 1.5 mm², halogen-free	60

1.4	5-pole - GST15i5	62

1.4.1	Connectors	62

1.4.1.1	Female connector with screw connection	62

1.4.1.2	Male with screw connection	67

1.4.2	Snap-In	72

1.4.2.1	Female connector with spring clamp connection	72

1.4.2.2	Male with spring clamp connection	75

1.4.3	Distribution blocks	78

1.4.4	Accessories	80

1.4.5	Cables	82

1.4.5.1	Cable assemblies, 1.5 mm², containing halogen	82

1.4.5.2	Cable assemblies, 1.5 mm², halogen-free	86

# gesis® MINI - Building installation systems

# 2-pole - GST15i2

## Connectors

### Female connector with screw connection

gesis® connector, female, 2-pole, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 2-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 7.7 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S B1 Z R1 W WS

Part No.: 91.921.3053.0

gesis® connector, female, 2-pole, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 2-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 7.7 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S B1 Z R1 W SW

Part No.: 91.921.3053.1

gesis® connector, female, 2-pole, 250 V, 6 A, pastel blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, female version, 2-pole, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 7.7 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: D2, D1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S B1 Z R1 WW PB01

Part No.: 91.921.3453.0

gesis® connector, female, 2-pole, 250 V, 6 A, pastel blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, female version, 2-pole, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 7.7 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: D2, D1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S B1 Z R1 WS PB01

Part No.: 91.921.3453.1

gesis® connector, female, 2-pole, 50 V, 16 A, light blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, female version, 2-pole, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 7.7 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S B1 Z R1 WW BL02

Part No.: 91.921.3353.0

gesis® connector, female, 2-pole, 50 V, 16 A, light blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, female version, 2-pole, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 7.7 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S B1 Z R1 WS BL02

Part No.: 91.921.3353.1

gesis® connector, female, 2-pole, 250 V, 16 A, white

System gesis® MINI - Installation connector, female version, 2-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, stranded: 0.75 mm²

Cable diameter: 3.3 x 5.0 mm (H03V2V2H2-F)

Housing material: Polyamide

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S B1 Z F1 W WS

Part No.: 91.921.2053.0

gesis® connector, female, 2-pole, 250 V, 16 A, black

System gesis® MINI - Installation connector, female version, 2-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, stranded: 0.75 mm²

Cable diameter: 3.3 x 5.0 mm (H03V2V2H2-F)

Housing material: Polyamide

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S B1 Z F1 W SW

Part No.: 91.921.2053.1

gesis® connector, female, 2-pole, 250 V, 6 A, pastel blue/white

System gesis® MINI - Installation connector, for dimming applications, female version, 2-pole, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, stranded: 0.75 mm²

Cable diameter: 3.3 x 5.0 mm (H03V2V2H2-F)

Housing material: Polyamide

Connections per pole: 1

Marking: D2, D1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S B1 Z F1 WW PB01

Part No.: 91.921.2453.0

gesis® connector, female, 2-pole, 250 V, 6 A, pastel blue/black

System gesis® MINI - Installation connector, for dimming applications, female version, 2-pole, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, stranded: 0.75 mm²

Cable diameter: 3.3 x 5.0 mm (H03V2V2H2-F)

Housing material: Polyamide

Connections per pole: 1

Marking: D2, D1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S B1 Z F1 WS PB01

Part No.: 91.921.2453.1

gesis® connector, female, 2-pole, 50 V, 16 A, light blue/white

System gesis® MINI - Installation connector, for low voltage applications, female version, 2-pole, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, stranded: 0.75 mm²

Cable diameter: 3.3 x 5.0 mm (H03V2V2H2-F)

Housing material: Polyamide

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S B1 Z F1 WW BL02

Part No.: 91.921.2353.0

gesis® connector, female, 2-pole, 50 V, 16 A, light blue/black

System gesis® MINI - Installation connector, for low voltage applications, female version, 2-pole, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, stranded: 0.75 mm²

Cable diameter: 3.3 x 5.0 mm (H03V2V2H2-F)

Housing material: Polyamide

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S B1 Z F1 WS BL02

Part No.: 91.921.2353.1

### Male with screw connection

gesis® connector, male, 2-pole, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 2-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 7.7 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S S1 Z R1 W WS

Part No.: 91.922.3053.0

gesis® connector, male, 2-pole, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 2-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 7.7 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S S1 Z R1 W SW

Part No.: 91.922.3053.1

gesis® connector, male, 2-pole, 250 V, 6 A, pastel blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, male version, 2-pole, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 7.7 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S S1 Z R1 WW PB01

Part No.: 91.922.3453.0

gesis® connector, male, 2-pole, 250 V, 6 A, pastel blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, male version, 2-pole, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 7.7 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S S1 Z R1 WS PB01

Part No.: 91.922.3453.1

gesis® connector, male, 2-pole, 50 V, 16 A, light blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, male version, 2-pole, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 7.7 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S S1 Z R1 WW BL02

Part No.: 91.922.3353.0

gesis® connector, male, 2-pole, 50 V, 16 A, light blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, male version, 2-pole, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 7.7 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S S1 Z R1 WS BL02

Part No.: 91.922.3353.1

gesis® connector, male, 2-pole, 250 V, 16 A, white

System gesis® MINI - Installation connector, male version, 2-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, stranded: 0.75 mm²

Cable diameter: 3.3 x 5.0 mm (H03V2V2H2-F)

Housing material: Polyamide

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S S1 Z F1 W WS

Part No.: 91.922.2053.0

gesis® connector, male, 2-pole, 250 V, 16 A, black

System gesis® MINI - Installation connector, male version, 2-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, stranded: 0.75 mm²

Cable diameter: 3.3 x 5.0 mm (H03V2V2H2-F)

Housing material: Polyamide

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S S1 Z F1 W SW

Part No.: 91.922.2053.1

gesis® connector, male, 2-pole, 250 V, 6 A, pastel blue/white

System gesis® MINI - Installation connector, for dimming applications, male version, 2-pole, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, stranded: 0.75 mm²

Cable diameter: 3.3 x 5.0 mm (H03V2V2H2-F)

Housing material: Polyamide

Connections per pole: 1

Marking: D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S S1 Z F1 WW PB01

Part No.: 91.922.2453.0

gesis® connector, male, 2-pole, 250 V, 6 A, pastel blue/black

System gesis® MINI - Installation connector, for dimming applications, male version, 2-pole, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, stranded: 0.75 mm²

Cable diameter: 3.3 x 5.0 mm (H03V2V2H2-F)

Housing material: Polyamide

Connections per pole: 1

Marking: D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S S1 Z F1 WS PB01

Part No.: 91.922.2453.1

gesis® connector, male, 2-pole, 50 V, 16 A, light blue/white

System gesis® MINI - Installation connector, for low voltage applications, male version, 2-pole, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, stranded: 0.75 mm²

Cable diameter: 3.3 x 5.0 mm (H03V2V2H2-F)

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S S1 Z F1 WW BL02

Part No.: 91.922.2353.0

gesis® connector, male, 2-pole, 50 V, 16 A, light blue/black

System gesis® MINI - Installation connector, for low voltage applications, male version, 2-pole, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, stranded: 0.75 mm²

Cable diameter: 3.3 x 5.0 mm (H03V2V2H2-F)

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2 S S1 Z F1 WS BL02

Part No.: 91.922.2353.1

## Snap-In

### Female connector with screw connection

gesis® Snap-In, female, 2-pole, for panel mounting, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 2-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2S B1 R W WS

Part No.: 91.921.9053.0

gesis® Snap-In, female, 2-pole, for panel mounting, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 2-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2S B1 R W SW

Part No.: 91.921.9053.1

gesis® Snap-In, female, 2-pole, for panel mounting, 250 V, 6 A, pastel blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, female version, 2-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: D2, D1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2S B1 R WW PB01

Part No.: 91.921.9453.0

gesis® Snap-In, female, 2-pole, for panel mounting, 250 V, 6 A, pastel blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, female version, 2-pole, turned contacts with screw connection, with black frame, snapable in housing, with integrated locking, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: D2, D1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2S B1 R WS PB01

Part No.: 91.921.9453.1

gesis® Snap-In, female, 2-pole, for panel mounting, 50 V, 16 A, light blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, female version, 2-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2S B1 R WW BL02

Part No.: 91.921.9353.0

gesis® Snap-In, female, 2-pole, for panel mounting, 50 V, 16 A, light blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, female version, 2-pole, turned contacts with screw connection, with black frame, snapable in housing, with integrated locking, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2S B1 R WS BL02

Part No.: 91.921.9353.1

### Male with screw connection

gesis® Snap-In, male, 2-pole, for panel mounting, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 2-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2S S1 R W WS

Part No.: 91.922.9053.0

gesis® Snap-In, male, 2-pole, for panel mounting, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 2-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2S S1 R W SW

Part No.: 91.922.9053.1

gesis® Snap-In, male, 2-pole, for panel mounting, 250 V, 6 A, pastel blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, male version, 2-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2S S1 R WW PB01

Part No.: 91.922.9453.0

gesis® Snap-In, male, 2-pole, for panel mounting, 250 V, 6 A, pastel blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, male version, 2-pole, turned contacts with screw connection, with black frame, snapable in housing, with integrated locking, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2S S1 R WS PB01

Part No.: 91.922.9453.1

gesis® Snap-In, male, 2-pole, for panel mounting, 50 V, 16 A, light blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, male version, 2-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2S S1 R WW BL02

Part No.: 91.922.9353.0

gesis® Snap-In, male, 2-pole, for panel mounting, 50 V, 16 A, light blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, male version, 2-pole, turned contacts with screw connection, with black frame, snapable in housing, with integrated locking, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i2S S1 R WS BL02

Part No.: 91.922.9353.1

## Cables

### Cable assemblies, 1.5 mm², containing halogen

gesis® extension cable, female, male, 2x 1.5 mm², 250 V, 16 A, length: x m, white

System gesis® MINI - assembled H05VV-F extension cable, 2-pole, 1.5 mm², male GST15i2, female GST15i2, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS BS 15 W x0WS

Part No.: 91.222.x000.2 (x corresponds to length in m)

gesis® extension cable, female, male, 2x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® MINI - assembled H05VV-F extension cable, 2-pole, 1.5 mm², male GST15i2, female GST15i2, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS BS 15 W x0SW

Part No.: 91.222.x000.1 (x corresponds to length in m)

gesis® extension cable, female, male, 2x 1.5 mm², 250 V, 6 A, length: x m, pastel blue

System gesis® MINI - assembled H05VV-F extension cable, 2-pole, 1.5 mm², for dimming applications, male GST15i2, female GST15i2, according IEC 61535, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS BS 15 W x0PB01

Part No.: 91.222.x000.9 (x corresponds to length in m)

gesis® extension cable, female, male, 2x 1.5 mm², 50 V, 16 A, length: x m, light blue

System gesis® MINI - assembled H05VV-F extension cable, 2-pole, 1.5 mm², for low voltage applications, male GST15i2, female GST15i2, according IEC 61535, mechanical coding code 2, color coding light blue.

Rated voltage: 50 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS BS 15 W x0BL02

Part No.: 91.222.x000.6 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 1.5 mm², 250 V, 16 A, length: x m, white

System gesis® MINI - assembled H05VV-F extension cable, 2-pole, 1.5 mm², female GST15i2, free end, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS B- 15 W x0WS

Part No.: 91.222.x003.2 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® MINI - assembled H05VV-F extension cable, 2-pole, 1.5 mm², female GST15i2, free end, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS B- 15 W x0SW

Part No.: 91.222.x003.1 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 1.5 mm², 250 V, 6 A, length: x m, pastel blue

System gesis® MINI - assembled H05VV-F extension cable, 2-pole, 1.5 mm², for dimming applications, female GST15i2, free end, according IEC 61535, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS B- 15 W x0PB01

Part No.: 91.222.x003.9 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 1.5 mm², 50 V, 16 A, length: x m, light blue

System gesis® MINI - assembled H05VV-F extension cable, 2-pole, 1.5 mm², for low voltage applications, female GST15i2, free end, according IEC 61535, mechanical coding code 2, color coding light blue.

Rated voltage: 50 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS B- 15 W x0BL02

Part No.: 91.222.x003.6 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 1.5 mm², 250 V, 16 A, length: x m, white

System gesis® MINI - assembled H05VV-F extension cable, 2-pole, 1.5 mm², male GST15i2, free end, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS -S 15 W x0WS

Part No.: 91.222.x004.2 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® MINI - assembled H05VV-F extension cable, 2-pole, 1.5 mm², male GST15i2, free end, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS -S 15 W x0SW

Part No.: 91.222.x004.1 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 1.5 mm², 250 V, 6 A, length: x m, pastel blue

System gesis® MINI - assembled H05VV-F extension cable, 2-pole, 1.5 mm², for dimming applications, male GST15i2, free end, according IEC 61535, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS -S 15 W x0PB01

Part No.: 91.222.x004.9 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 1.5 mm², 50 V, 16 A, length: x m, light blue

System gesis® MINI - assembled H05VV-F extension cable, 2-pole, 1.5 mm², for low voltage applications, male GST15i2, free end, according IEC 61535, mechanical coding code 2, color coding light blue.

Rated voltage: 50 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS -S 15 W x0BL02

Part No.: 91.222.x004.6 (x corresponds to length in m)

### Cable assemblies, 1.5 mm², halogen-free

gesis® extension cable, female, male, 2x 1.5 mm², 250 V, 16 A, length: x m, white

System gesis® MINI - assembled S05Z1Z1-F extension cable, 2-pole, 1.5 mm², male GST15i2, female GST15i2, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: S05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS BS 15 HW x0WS

Part No.: 91.222.x060.2 (x corresponds to length in m)

gesis® extension cable, female, male, 2x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® MINI - assembled S05Z1Z1-F extension cable, 2-pole, 1.5 mm², male GST15i2, female GST15i2, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: S05Z1Z1-F

Cable color: black

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS BS 15 HW x0SW

Part No.: 91.222.x060.1 (x corresponds to length in m)

gesis® extension cable, female, male, 2x 1.5 mm², 250 V, 6 A, length: x m, pastel blue

System gesis® MINI - assembled S05Z1Z1-F extension cable, 2-pole, 1.5 mm², for dimming applications, male GST15i2, female GST15i2, according IEC 61535, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: S05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS BS 15 HW x0PB01

Part No.: 91.222.x060.9 (x corresponds to length in m)

gesis® extension cable, female, male, 2x 1.5 mm², 50 V, 16 A, length: x m, light blue

System gesis® MINI - assembled S05Z1Z1-F extension cable, 2-pole, 1.5 mm², for low voltage applications, male GST15i2, female GST15i2, according IEC 61535, mechanical coding code 2, color coding light blue.

Rated voltage: 50 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: S05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS BS 15 HW x0BL02

Part No.: 91.222.x060.6 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 1.5 mm², 250 V, 16 A, length: x m, white

System gesis® MINI - assembled S05Z1Z1-F extension cable, 2-pole, 1.5 mm², female GST15i2, free end, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: S05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS B- 15 HW x0WS

Part No.: 91.222.x063.2 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® MINI - assembled S05Z1Z1-F extension cable, 2-pole, 1.5 mm², female GST15i2, free end, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: S05Z1Z1-F

Cable color: black

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS B- 15 HW x0SW

Part No.: 91.222.x063.1 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 1.5 mm², 250 V, 6 A, length: x m, pastel blue

System gesis® MINI - assembled S05Z1Z1-F extension cable, 2-pole, 1.5 mm², for dimming applications, female GST15i2, free end, according IEC 61535, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: S05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS B- 15 HW x0PB01

Part No.: 91.222.x063.9 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 1.5 mm², 50 V, 16 A, length: x m, light blue

System gesis® MINI - assembled S05Z1Z1-F extension cable, 2-pole, 1.5 mm², for low voltage applications, female GST15i2, free end, according IEC 61535, mechanical coding code 2, color coding light blue.

Rated voltage: 50 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: S05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS B- 15 HW x0BL02

Part No.: 91.222.x063.6 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 1.5 mm², 250 V, 16 A, length: x m, white

System gesis® MINI - assembled S05Z1Z1-F extension cable, 2-pole, 1.5 mm², male GST15i2, free end, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: S05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS -S 15 HW x0WS

Part No.: 91.222.x064.2 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® MINI - assembled S05Z1Z1-F extension cable, 2-pole, 1.5 mm², male GST15i2, free end, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: S05Z1Z1-F

Cable color: black

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS -S 15 HW x0SW

Part No.: 91.222.x064.1 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 1.5 mm², 250 V, 6 A, length: x m, pastel blue

System gesis® MINI - assembled S05Z1Z1-F extension cable, 2-pole, 1.5 mm², for dimming applications, male GST15i2, free end, according IEC 61535, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: S05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS -S 15 HW x0PB01

Part No.: 91.222.x064.9 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 1.5 mm², 50 V, 16 A, length: x m, light blue

System gesis® MINI - assembled S05Z1Z1-F extension cable, 2-pole, 1.5 mm², for low voltage applications, male GST15i2, free end, according IEC 61535, mechanical coding code 2, color coding light blue.

Rated voltage: 50 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: S05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i2 KS -S 15 HW x0BL02

Part No.: 91.222.x064.6 (x corresponds to length in m)

# 3-pole - GST15i3

## Connectors

### Female connector with screw connection

gesis® connector, female, 3-pole, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 3-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 5.5 - 8.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 S B1 Z R1 W WS

Part No.: 91.931.3053.0

gesis® connector, female, 3-pole, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 3-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 5.5 - 8.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 S B1 Z R1 W SW

Part No.: 91.931.3053.1

gesis® connector, female, 3-pole, 250 V, 16 A, brown/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for switching applications, female version, 3-pole, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 4, color coding brown.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 5.5 - 8.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 S B1 Z R1 WW BR01

Part No.: 91.931.3853.0

gesis® connector, female, 3-pole, 250 V, 16 A, brown/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for switching applications, female version, 3-pole, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 4, color coding brown.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 5.5 - 8.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 S B1 Z R1 WS BR01

Part No.: 91.931.3853.1

gesis® connector, female, 3-pole, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 3-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 1.5 - 2.5 mm²

Terminal cross-section, stranded: 1.5 - 2.5 mm²

Cable diameter: 7.8 - 10.3 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 S B1 Z R1 WS

Part No.: 91.931.4053.0

gesis® connector, female, 3-pole, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 3-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 1.5 - 2.5 mm²

Terminal cross-section, stranded: 1.5 - 2.5 mm²

Cable diameter: 7.8 - 10.3 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 S B1 Z R1 SW

Part No.: 91.931.4053.1

### Male with screw connection

gesis® connector, male, 3-pole, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 3-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 5.5 - 8.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: L, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 S S1 Z R1 W WS

Part No.: 91.932.3053.0

gesis® connector, male, 3-pole, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 3-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 5.5 - 8.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: L, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 S S1 Z R1 W SW

Part No.: 91.932.3053.1

gesis® connector, male, 3-pole, 250 V, 16 A, brown/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for switching applications, male version, 3-pole, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 4, color coding brown.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 5.5 - 8.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 S S1 Z R1 WW BR01

Part No.: 91.932.3853.0

gesis® connector, male, 3-pole, 250 V, 16 A, brown/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for switching applications, male version, 3-pole, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 4, color coding brown.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 5.5 - 8.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 S S1 Z R1 WS BR01

Part No.: 91.932.3853.1

gesis® connector, male, 3-pole, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 3-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 1.5 - 2.5 mm²

Terminal cross-section, stranded: 1.5 - 2.5 mm²

Cable diameter: 7.8 - 10.3 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: L, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 S S1 Z R1 WS

Part No.: 91.932.4053.0

gesis® connector, male, 3-pole, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 3-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 1.5 - 2.5 mm²

Terminal cross-section, stranded: 1.5 - 2.5 mm²

Cable diameter: 7.8 - 10.3 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: L, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 S S1 Z R1 SW

Part No.: 91.932.4053.1

## Snap-In

### Female connector with screw connection

gesis® Snap-In, female, 3-pole, for panel mounting, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 3-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3S B1 R W WS

Part No.: 91.931.9053.0

gesis® Snap-In, female, 3-pole, for panel mounting, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 3-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3S B1 R W SW

Part No.: 91.931.9053.1

gesis® Snap-In, female, 3-pole, for panel mounting, 250 V, 16 A, brown/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for switching applications, female version, 3-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 4, color coding brown.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3S B1 R WW BR01

Part No.: 91.931.9853.0

gesis® Snap-In, female, 3-pole, for panel mounting, 250 V, 16 A, brown/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for switching applications, female version, 3-pole, turned contacts with screw connection, with black frame, snapable in housing, with integrated locking, mechanical coding code 4, color coding brown.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3S B1 R WS BR01

Part No.: 91.931.9853.1

gesis® Snap-In, female, 3-pole, for panel mounting, jut-out, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 3-pole, turned contacts with screw connection, with white frame, snapable in housing, jut-out version, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3S B1 U W WS

Part No.: 91.931.9153.0

gesis® Snap-In, female, 3-pole, for panel mounting, jut-out, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 3-pole, turned contacts with screw connection, with white frame, snapable in housing, jut-out version, with integrated locking, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3S B1 U W SW

Part No.: 91.931.9153.1

### Male with screw connection

gesis® Snap-In, male, 3-pole, for panel mounting, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 3-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: L, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3S S1 R W WS

Part No.: 91.932.9053.0

gesis® Snap-In, male, 3-pole, for panel mounting, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 3-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: L, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3S S1 R W SW

Part No.: 91.932.9053.1

gesis® Snap-In, male, 3-pole, for panel mounting, 250 V, 16 A, brown/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for switching applications, male version, 3-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 4, color coding brown.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3S S1 R WW BR01

Part No.: 91.932.9853.0

gesis® Snap-In, male, 3-pole, for panel mounting, 250 V, 16 A, brown/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for switching applications, male version, 3-pole, turned contacts with screw connection, with black frame, snapable in housing, with integrated locking, mechanical coding code 4, color coding brown.

Rated voltage: 250 V

Rated current: 6 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3S S1 R WS BR01

Part No.: 91.932.9853.1

gesis® Snap-In, male, 3-pole, for panel mounting, jut-out, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 3-pole, turned contacts with screw connection, with white frame, snapable in housing, jut-out version, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: L, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3S S1 U W WS

Part No.: 91.932.9153.0

gesis® Snap-In, male, 3-pole, for panel mounting, jut-out, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 3-pole, turned contacts with screw connection, with white frame, snapable in housing, jut-out version, with integrated locking, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: L, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3S S1 U W SW

Part No.: 91.932.9153.1

## Distribution blocks

gesis® distribution block, 3-pole, 1 input, 2 outputs, 250 V, 16 A, white

System gesis® MINI - Distribution block for installation connectors according to IEC 61535, h-shaped distribution block, 3-pole, turned contacts, 1 input, 2 outputs, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Outputs: 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 V 2P1 H W WS

Part No.: 91.030.6053.0

gesis® distribution block, 3-pole, 1 input, 2 outputs, 250 V, 16 A, black

System gesis® MINI - Distribution block for installation connectors according to IEC 61535, h-shaped distribution block, 3-pole, turned contacts, 1 input, 2 outputs, with integrated locking, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Outputs: 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 V 2P1 H W SW

Part No.: 91.030.6053.1

gesis® distribution block, 3-pole, 1 input, 3 outputs, 250 V, 16 A, white

System gesis® MINI - Distribution block for installation connectors according to IEC 61535, H-shaped distribution block, 3-pole, turned contacts, 1 input, 3 outputs, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 V 3P1 H W WS

Part No.: 91.030.4953.0

gesis® distribution block, 3-pole, 1 input, 3 outputs, 250 V, 16 A, black

System gesis® MINI - Distribution block for installation connectors according to IEC 61535, H-shaped distribution block, 3-pole, turned contacts, 1 input, 3 outputs, with integrated locking, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 V 3P1 H W SW

Part No.: 91.030.4953.1

gesis® distribution block, 3-pole, 1 input, 5 outputs, 250 V, 16 A, white

System gesis® MINI - Distribution block for installation connectors according to IEC 61535, H-shaped distribution block, 3-pole, turned contacts, 1 input, 5 outputs, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Outputs: 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 V 5P1 H W WS

Part No.: 91.030.5253.0

gesis® distribution block, 3-pole, 1 input, 5 outputs, 250 V, 16 A, black

System gesis® MINI - Distribution block for installation connectors according to IEC 61535, H-shaped distribution block, 3-pole, turned contacts, 1 input, 5 outputs, with integrated locking, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Outputs: 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 V 5P1 H W SW

Part No.: 91.030.5253.1

## Accessories

gesis® intermediate coupling, 3-pole, 1 input, 1 output, 250 V, 16 A, white

System gesis® MINI - Intermediate coupling for installation connectors according to IEC 61535, for direct forwarding e.g. between two luminaires, 3-pole, turned contacts, 1 input, 1 output, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Output: 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 Z 1P1 WS

Part No.: 91.030.5953.0

gesis® intermediate coupling, 3-pole, 1 input, 1 output, 250 V, 16 A, black

System gesis® MINI - Intermediate coupling for installation connectors according to IEC 61535, for direct forwarding e.g. between two luminaires, 3-pole, turned contacts, 1 input, 1 output, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Output: 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 Z 1P1 SW

Part No.: 91.030.5953.1

gesis® U-piece, 3-pole, 1 input, 1 output, 250 V, 16 A, white

System gesis® MINI - U-piece for installation connectors according to IEC 61535, for direct forwarding e.g. between two luminaires, 3-pole, turned contacts, 1 input, 1 output, with locking option, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Output: 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 Z 1P1U W WS

Part No.: 91.030.5853.0

gesis® U-piece, 3-pole, 1 input, 1 output, 250 V, 16 A, black

System gesis® MINI - U-piece for installation connectors according to IEC 61535, for direct forwarding e.g. between two luminaires, 3-pole, turned contacts, 1 input, 1 output, with locking option, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Output: 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i3 Z 1P1U W SW

Part No.: 91.030.5853.1

## Cables

### Cable assemblies, 1.5 mm², containing halogen

gesis® extension cable, female, male, 3x 1.5 mm², 250 V, 16 A, length: x m, white

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 3-pole, 1.5 mm², male GST15i3, female GST15i3, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS BS 15 W x0WS

Part No.: 91.232.x000.2 (x corresponds to length in m)

gesis® extension cable, female, male, 3x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 3-pole, 1.5 mm², male GST15i3, female GST15i3, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS BS 15 W x0SW

Part No.: 91.232.x000.1 (x corresponds to length in m)

gesis® connection cable, female, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, white

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 3-pole, 1.5 mm², female GST15i3, free end, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS B- 15 W x0WS

Part No.: 91.232.x003.2 (x corresponds to length in m)

gesis® connection cable, female, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 3-pole, 1.5 mm², female GST15i3, free end, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS B- 15 W x0SW

Part No.: 91.232.x003.1 (x corresponds to length in m)

gesis® connection cable, male, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, white

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 3-pole, 1.5 mm², male GST15i3, free end, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS -S 15 W x0WS

Part No.: 91.232.x004.2 (x corresponds to length in m)

gesis® connection cable, male, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 3-pole, 1.5 mm², male GST15i3, free end, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS -S 15 W x0SW

Part No.: 91.232.x004.1 (x corresponds to length in m)

gesis® extension cable, female, male, 3x 1.5 mm², 250 V, 16 A, length: x m, white

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 3-pole, 1.5 mm², male GST18i3, female GST15i3, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS BA 15 W x0WS

Part No.: 91.232.x009.2 (x corresponds to length in m)

gesis® extension cable, female, male, 3x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 3-pole, 1.5 mm², male GST18i3, female GST15i3, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS BA 15 W x0SW

Part No.: 91.232.x009.1 (x corresponds to length in m)

gesis® extension cable, female, male, 3x 1.5 mm², 250 V, 16 A, length: 1.5 m, black

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 3-pole, 1.5 mm², male GST15i3, female GST18i3, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: 1.5 m

Brand: Wieland Electric GmbH

Type: GST15i3 KS AS 15 W 15SW

Part No.: 99.400.4346.1

gesis® extension cable, female, male, 3x 1.5 mm², 250 V, 16 A, length: 3.0 m, black

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 3-pole, 1.5 mm², male GST15i3, female GST18i3, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: 3,0 m

Brand: Wieland Electric GmbH

Type: GST15i3 KS AS 15 W 30SW

Part No.: 99.401.4346.1

gesis® extension cable, female, male, 3x 1.5 mm², 250 V, 16 A, length: 5,0 m, black

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 3-pole, 1.5 mm², male GST15i3, female GST18i3, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: 5,0 m

Brand: Wieland Electric GmbH

Type: GST15i3 KS AS 15 W 50SW

Part No.: 99.402.4346.1

### Cable assemblies, 1.5 mm², halogen-free

gesis® extension cable, female, male, 3x 1.5 mm², 250 V, 16 A, length: x m, white

System gesis® MINI - assembled H05Z1Z1-F extension cable with protective ground, 3-pole, 1.5 mm², male GST15i3, female GST15i3, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS BS 15H W x0WS

Part No.: 91.232.x060.2 (x corresponds to length in m)

gesis® extension cable, female, male, 3x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® MINI - assembled H05Z1Z1-F extension cable with protective ground, 3-pole, 1.5 mm², male GST15i3, female GST15i3, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: black

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS BS 15H W x0SW

Part No.: 91.232.x060.1 (x corresponds to length in m)

gesis® connection cable, female, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, white

System gesis® MINI - assembled H05Z1Z1-F extension cable with protective ground, 3-pole, 1.5 mm², female GST15i3, free end, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS B- 15H W x0WS

Part No.: 91.232.x063.2 (x corresponds to length in m)

gesis® connection cable, female, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® MINI - assembled H05Z1Z1-F extension cable with protective ground, 3-pole, 1.5 mm², female GST15i3, free end, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: black

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS B- 15H W x0SW

Part No.: 91.232.x063.1 (x corresponds to length in m)

gesis® connection cable, male, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, white

System gesis® MINI - assembled H05Z1Z1-F extension cable with protective ground, 3-pole, 1.5 mm², male GST15i3, free end, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS -S 15H W x0WS

Part No.: 91.232.x064.2 (x corresponds to length in m)

gesis® connection cable, male, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® MINI - assembled H05Z1Z1-F extension cable with protective ground, 3-pole, 1.5 mm², male GST15i3, free end, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: black

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS -S 15H W x0SW

Part No.: 91.232.x064.1 (x corresponds to length in m)

gesis® extension cable, female, male, 3x 1.5 mm², 250 V, 16 A, length: x m, white

System gesis® MINI - assembled H05Z1Z1-F extension cable with protective ground, 3-pole, 1.5 mm², male GST18i3, female GST15i3, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS BA 15H W x0WS

Part No.: 91.232.x069.2 (x corresponds to length in m)

gesis® extension cable, female, male, 3x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® MINI - assembled H05Z1Z1-F extension cable with protective ground, 3-pole, 1.5 mm², male GST18i3, female GST15i3, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: black

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i3 KS BA 15H W x0SW

Part No.: 91.232.x069.1 (x corresponds to length in m)

## Assembled Cables

gesis® cable, female, SCHUKO male plug, 3x 1.5 mm², 250 V, 16 A, length: 2,0 m, white

System gesis® MINI - assembled H05VV-F cable with protective ground, 3-pole, 1.5 mm², female GST15i3 with SCHUKO male plug according to DIN 49441, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: 2,0 m

Brand: Wieland Electric GmbH

Type: GST15i3 KS BD 15 20WS

Part No.: 99.641.0000.0

gesis® cable, female, SCHUKO male plug, 3x 1.5 mm², 250 V, 16 A, length: 3.0 m, white

System gesis® MINI - assembled H05VV-F cable with protective ground, 3-pole, 1.5 mm², female GST15i3 with SCHUKO male plug according to DIN 49441, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: 3.0 m

Brand: Wieland Electric GmbH

Type: GST15i3 KS BD 15 30WS

Part No.: 99.642.0000.0

gesis® cable, female, SCHUKO male plug, 3x 1.5 mm², 250 V, 16 A, length: 2,0 m, black

System gesis® MINI - assembled H05VV-F cable with protective ground, 3-pole, 1.5 mm², female GST15i3 with SCHUKO male plug according to DIN 49441, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: 2,0 m

Brand: Wieland Electric GmbH

Type: GST15i3 KS BD 15 20SW

Part No.: 99.640.0000.0

gesis® cable, female, SCHUKO male plug, 3x 1.5 mm², 250 V, 16 A, length: 4.0 m, black

System gesis® MINI - assembled H05VV-F cable with protective ground, 3-pole, 1.5 mm², female GST15i3 with SCHUKO male plug according to DIN 49441, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: 4.0 m

Brand: Wieland Electric GmbH

Type: GST15i3 KS BD 15 40SW

Part No.: 99.643.0000.0

gesis® cable, female, SCHUKO male plug, 3x 1.5 mm², 250 V, 16 A, length: 5,0 m, black

System gesis® MINI - assembled H05VV-F cable with protective ground, 3-pole, 1.5 mm², female GST15i3 with SCHUKO male plug according to DIN 49441, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: 5,0 m

Brand: Wieland Electric GmbH

Type: GST15i3 KS BD 15 50SW

Part No.: 99.668.0000.0

# 4-pole - GST15i4

## Connectors

### Female connector with screw connection

gesis® connector, female, 4-pole, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 4-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i4 S B1 Z R1 WS

Part No.: 91.941.4053.0

gesis® connector, female, 4-pole, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 4-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i4 S B1 Z R1 SW

Part No.: 91.941.4053.1

gesis® connector, female, angled cable entry, 4-pole, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 4-pole, with angled cable entry, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i4 S B1 ZW 1V WS

Part No.: 91.941.3053.0

gesis® connector, female, angled cable entry, 4-pole, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 4-pole, with angled cable entry, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i4 S B1 ZW 1V SW

Part No.: 91.941.3053.1

### Male with screw connection

gesis® connector, male, 4-pole, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 4-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 2, 1, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i4 S S1 Z R1 WS

Part No.: 91.942.4053.0

gesis® connector, male, 4-pole, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 4-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 2, 1, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i4 S S1 Z R1 SW

Part No.: 91.942.4053.1

gesis® connector, male, angled cable entry, 4-pole, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 4-pole, with angled cable entry, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 2, 1, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i4 S S1 ZW 1V WS

Part No.: 91.942.3053.0

gesis® connector, male, angled cable entry, 4-pole, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 4-pole, with angled cable entry, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 2, 1, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i4 S S1 ZW 1V SW

Part No.: 91.942.3053.1

## Snap-In

### Female connector with screw connection

gesis® Snap-In, female, 4-pole, for panel mounting, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 4-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i4S B1 R V WS

Part No.: 91.941.9053.0

gesis® Snap-In, female, 4-pole, for panel mounting, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 4-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i4S B1 R V SW

Part No.: 91.941.9053.1

### Male with screw connection

gesis® Snap-In, male, 4-pole, for panel mounting, 250 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 4-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 2, 1, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i4S S1 R V WS

Part No.: 91.942.9053.0

gesis® Snap-In, male, 4-pole, for panel mounting, 250 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 4-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 2, 1, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i4S S1 R V SW

Part No.: 91.942.9053.1

## Cables

### Cable assemblies, 1.5 mm², containing halogen

gesis® extension cable, female, male, 4x 1.5 mm², 250/400 V, 16 A, length: x m, white

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 4-pole, 1.5 mm², male GST15i4, female GST15i4, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i4 KS BS X15 V x0WS

Part No.: 91.207.x000.2 (x corresponds to length in m)

gesis® connection cable, female, free end, 4x 1.5 mm², 250/400 V, 16 A, length: x m, white

System gesis® MINI - assembled H05VV-F connection cable with protective ground, 4-pole, 1.5 mm², female GST15i4, free end, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i4 KS B- X15 V x0WS

Part No.: 91.207.x003.2 (x corresponds to length in m)

gesis® connection cable, male, free end, 4x 1.5 mm², 250/400 V, 16 A, length: x m, white

System gesis® MINI - assembled H05VV-F connection cable with protective ground, 4-pole, 1.5 mm², male GST15i4, free end, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i4 KS -S X15 V x0WS

Part No.: 91.207.x004.2 (x corresponds to length in m)

### Cable assemblies, 1.5 mm², halogen-free

gesis® extension cable, female, male, 4x 1.5 mm², 250/400 V, 16 A, length: x m, white

System gesis® MINI - assembled H05Z1Z1-F extension cable with protective ground, 4-pole, 1.5 mm², male GST15i4, female GST15i4, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i4 KS BS X15H V x0WS

Part No.: 91.207.x060.2 (x corresponds to length in m)

gesis® connection cable, female, free end, 4x 1.5 mm², 250/400 V, 16 A, length: x m, white

System gesis® MINI - assembled H05Z1Z1-F connection cable with protective ground, 4-pole, 1.5 mm², female GST15i4, free end, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i4 KS B- X15H V x0WS

Part No.: 91.207.x063.2 (x corresponds to length in m)

gesis® connection cable, male, free end, 4x 1.5 mm², 250/400 V, 16 A, length: x m, white

System gesis® MINI - assembled H05Z1Z1-F connection cable with protective ground, 4-pole, 1.5 mm², male GST15i4, free end, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i4 KS -S X15H V x0WS

Part No.: 91.207.x064.2 (x corresponds to length in m)

# 5-pole - GST15i5

## Connectors

### Female connector with screw connection

gesis® connector, female, 5-pole, 250/400 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 5-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S B1 Z R1 W WS

Part No.: 91.951.4053.0

gesis® connector, female, 5-pole, 250/400 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 5-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S B1 Z R1 W SW

Part No.: 91.951.4053.1

gesis® connector, female, 5-pole, 250 V, 16 A, pastel blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, female version, 5-pole, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, L, D2, D1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S B1 Z R1 VW PB01

Part No.: 91.951.4453.0

gesis® connector, female, 5-pole, 250 V, 16 A, pastel blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, female version, 5-pole, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, L, D2, D1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S B1 Z R1 VS PB01

Part No.: 91.951.4453.1

gesis® connector, female, 5-pole, 50 V, 10 A, light blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, female version, 5-pole, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 10 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S B1 Z R1 VW BL02

Part No.: 91.951.4353.0

gesis® connector, female, 5-pole, 50 V, 10 A, light blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, female version, 5-pole, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 10 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S B1 Z R1 VS BL02

Part No.: 91.951.4353.1

gesis® connector, female, angled cable entry, 5-pole, 250/400 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 5-pole, with angled cable entry, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S B1 Z W1 V WS

Part No.: 91.951.3053.0

gesis® connector, female, angled cable entry, 5-pole, 250/400 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 5-pole, with angled cable entry, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S B1 Z W1 V SW

Part No.: 91.951.3053.1

gesis® connector, female, angled cable entry, 5-pole, 250 V, 16 A, pastel blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, female version, 5-pole, with angled cable entry, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, L, D2, D1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S B1 Z W1 VW PB01

Part No.: 91.951.3453.0

gesis® connector, female, angled cable entry, 5-pole, 250 V, 16 A, pastel blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, female version, 5-pole, with angled cable entry, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, L, D2, D1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S B1 Z W1 VS PB01

Part No.: 91.951.3453.1

gesis® connector, female, angled cable entry, 5-pole, 50 V, 10 A, light blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, female version, 5-pole, with angled cable entry, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 10 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S B1 Z W1 VW BL02

Part No.: 91.951.3353.0

gesis® connector, female, angled cable entry, 5-pole, 50 V, 10 A, light blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, female version, 5-pole, with angled cable entry, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 10 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S B1 Z W1 VS BL02

Part No.: 91.951.3353.1

### Male with screw connection

gesis® connector, male, 5-pole, 250/400 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 5-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 3, 2, 1, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S S1 Z R1 W WS

Part No.: 91.952.4053.0

gesis® connector, male, 5-pole, 250/400 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 5-pole, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 3, 2, 1, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S S1 Z R1 W SW

Part No.: 91.952.4053.1

gesis® connector, male, 5-pole, 250 V, 16 A, pastel blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, male version, 5-pole, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: D1, D2, L, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S S1 Z R1 VW PB01

Part No.: 91.952.4453.0

gesis® connector, male, 5-pole, 250 V, 16 A, pastel blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, male version, 5-pole, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: D1, D2, L, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S S1 Z R1 VS PB01

Part No.: 91.952.4453.1

gesis® connector, male, 5-pole, 50 V, 10 A, light blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, male version, 5-pole, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 10 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S S1 Z R1 VW BL02

Part No.: 91.952.4353.0

gesis® connector, male, 5-pole, 50 V, 10 A, light blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, male version, 5-pole, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 10 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Cable diameter: 8.5 - 12.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S S1 Z R1 VS BL02

Part No.: 91.952.4353.1

gesis® connector, male, angled cable entry, 5-pole, 250/400 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 5-pole, with angled cable entry, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 3, 2, 1, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S S1 Z W1 V WS

Part No.: 91.952.3053.0

gesis® connector, male, angled cable entry, 5-pole, 250/400 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 5-pole, with angled cable entry, turned contacts with screw connection, very compact housing with strain relief, field assembly, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 3, 2, 1, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S S1 Z W1 V SW

Part No.: 91.952.3053.1

gesis® connector, male, angled cable entry, 5-pole, 250 V, 16 A, pastel blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, male version, 5-pole, with angled cable entry, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: D1, D2, L, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S S1 Z W1 VW PB01

Part No.: 91.952.3453.0

gesis® connector, male, angled cable entry, 5-pole, 250 V, 16 A, pastel blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, male version, 5-pole, with angled cable entry, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: D1, D2, L, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S S1 Z W1 VS PB01

Part No.: 91.952.3453.1

gesis® connector, male, angled cable entry, 5-pole, 50 V, 10 A, light blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, male version, 5-pole, with angled cable entry, turned contacts with screw connection, very compact housing with white locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 10 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S S1 Z W1 VS BL02

Part No.: 91.952.3353.0

gesis® connector, male, angled cable entry, 5-pole, 50 V, 10 A, light blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, male version, 5-pole, with angled cable entry, turned contacts with screw connection, very compact housing with black locking, field assembly, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 10 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Terminal cross-section, solid: 0.5 - 1.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 6.0 - 11.5 mm (H05VV-F, NYM)

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 S S1 Z W1 VS BL02

Part No.: 91.952.3353.1

## Snap-In

### Female connector with spring clamp connection

gesis® Snap-In, female, 5-pole, for panel mounting, 250/400 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 5-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5S B1 R V WS

Part No.: 91.951.9053.0

gesis® Snap-In, female, 5-pole, for panel mounting, 250/400 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, female version, 5-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5S B1 R V SW

Part No.: 91.951.9053.1

gesis® Snap-In, female, 5-pole, for panel mounting, 250 V, 16 A, pastel blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, female version, 5-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, L, D2, D1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5S B1 R VW PB01

Part No.: 91.951.9453.0

gesis® Snap-In, female, 5-pole, for panel mounting, 250 V, 16 A, pastel blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, female version, 5-pole, turned contacts with screw connection, with black frame, snapable in housing, with integrated locking, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: N, PE, L, D2, D1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5S B1 R VS PB01

Part No.: 91.951.9453.1

gesis® Snap-In, female, 5-pole, for panel mounting, 50 V, 10 A, light blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, female version, 5-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 10 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5S B1 R VW BL02

Part No.: 91.951.9353.0

gesis® Snap-In, female, 5-pole, for panel mounting, 50 V, 10 A, light blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, female version, 5-pole, turned contacts with screw connection, with black frame, snapable in housing, with integrated locking, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 10 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5S B1 R VS BL02

Part No.: 91.951.9353.1

### Male with spring clamp connection

gesis® Snap-In, male, 5-pole, for panel mounting, 250/400 V, 16 A, white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 5-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 3, 2, 1, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5S S1 R V WS

Part No.: 91.952.9053.0

gesis® Snap-In, male, 5-pole, for panel mounting, 250/400 V, 16 A, black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, male version, 5-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 3, 2, 1, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5S S1 R V SW

Part No.: 91.952.9053.1

gesis® Snap-In, male, 5-pole, for panel mounting, 250 V, 16 A, pastel blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, male version, 5-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: D1, D2, L, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5S S1 R VW PB01

Part No.: 91.952.9453.0

gesis® Snap-In, male, 5-pole, for panel mounting, 250 V, 16 A, pastel blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for dimming applications, male version, 5-pole, turned contacts with screw connection, with black frame, snapable in housing, with integrated locking, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: D1, D2, L, PE, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5S S1 R VS PB01

Part No.: 91.952.9453.1

gesis® Snap-In, male, 5-pole, for panel mounting, 50 V, 10 A, light blue/white

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, male version, 5-pole, turned contacts with screw connection, with white frame, snapable in housing, with integrated locking, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 10 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5S S1 R VW BL02

Part No.: 91.952.9353.0

gesis® Snap-In, male, 5-pole, for panel mounting, 50 V, 10 A, light blue/black

System gesis® MINI - Installation connector according to IEC 61535 for permanent connection, for low voltage applications, male version, 5-pole, turned contacts with screw connection, with black frame, snapable in housing, with integrated locking, mechanical coding code 3, color coding light blue.

Rated voltage: 50 V

Rated current: 10 A

Rated impulse voltage: 4 kV

Type of protection: up to IP40

Material thickness: 0.5 - 1.5 mm

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 2.5 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5S S1 R VS BL02

Part No.: 91.952.9353.1

## Distribution blocks

gesis® distribution block, 5-/3-pole, 1 input, 2 outputs, 250/400 V, 16 A, white

System gesis® MINI - Distribution block for installation connectors according to IEC 61535, h-shaped distribution block, 5-/3-pole, turned contacts, 5-pole input GST15i5, 5-pole forwarding output GST15i5, 3-pole output GST18i3, phase L1, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Outputs: 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18/15 WS

Part No.: 91.050.3151.0

gesis® distribution block, 5-/3-pole, 1 input, 2 outputs, 250/400 V, 16 A, white

System gesis® MINI - Distribution block for installation connectors according to IEC 61535, h-shaped distribution block, 5-/3-pole, turned contacts, 5-pole input GST15i5, 5-pole forwarding output GST15i5, 3-pole output GST18i3, phase L2, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Outputs: 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18/15 WS

Part No.: 91.050.3251.0

gesis® distribution block, 5-/3-pole, 1 input, 2 outputs, 250/400 V, 16 A, white

System gesis® MINI - Distribution block for installation connectors according to IEC 61535, h-shaped distribution block, 5-/3-pole, turned contacts, 5-pole input GST15i5, 5-pole forwarding output GST15i5, 3-pole output GST18i3, phase L3, with integrated locking, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Outputs: 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18/15 WS

Part No.: 91.050.3351.0

## Accessories

gesis® intermediate coupling, 5-pole, 1 input, 1 output, 250 V, 16 A, white

System gesis® MINI - Intermediate coupling for installation connectors according to IEC 61535, for direct forwarding e.g. between two luminaires, 5-pole, turned contacts, 1 input, 1 output, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Output: 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 Z 1P1 WS

Part No.: 91.050.5953.0

gesis® intermediate coupling, 5-pole, 1 input, 1 output, 250 V, 16 A, black

System gesis® MINI - Intermediate coupling for installation connectors according to IEC 61535, for direct forwarding e.g. between two luminaires, 5-pole, turned contacts, 1 input, 1 output, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Output: 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 Z 1P1 SW

Part No.: 91.050.5953.1

gesis® intermediate coupling, 5-pole, 1 input, 1 output, 250 V, 16 A, pastel blue

System gesis® MINI - Intermediate coupling for installation connectors according to IEC 61535, for direct forwarding e.g. between two luminaires, 5-pole, turned contacts, 1 input, 1 output, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Housing material: Polyamide

Input: 1

Output: 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST15i5 Z 1P1 V PB01

Part No.: 91.050.6053.0

## Cables

### Cable assemblies, 1.5 mm², containing halogen

gesis® extension cable, female, male, 5x 1.5 mm², 250/400 V, 16 A, length: x m, white

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 5-pole, 1.5 mm², male GST15i5, female GST15i5, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS BS X15 V x0WS

Part No.: 91.257.x000.2 (x corresponds to length in m)

gesis® extension cable, female, male, 5x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 5-pole, 1.5 mm², male GST15i5, female GST15i5, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS BS X15 V x0SW

Part No.: 91.257.x000.1 (x corresponds to length in m)

gesis® extension cable, female, male, 5x 1.5 mm², 250 V, 16 A, length: x m, pastel blue/white

System gesis® MINI - assembled H05VV-F extension cable with protective ground, 5-pole, 1.5 mm², for dimming applications, male GST15i5, female GST15i5, with angled cable entry, according IEC 61535, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS BS X15 V x0PB01

Part No.: 91.257.x000.9 (x corresponds to length in m)

gesis® connection cable, female, free end, 5x 1.5 mm², 250/400 V, 16 A, length: x m, white

System gesis® MINI - assembled H05VV-F connection cable with protective ground, 5-pole, 1.5 mm², female GST15i5, free end, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS B- X15 V x0WS

Part No.: 91.257.x003.2 (x corresponds to length in m)

gesis® connection cable, female, free end, 5x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® MINI - assembled H05VV-F connection cable with protective ground, 5-pole, 1.5 mm², female GST15i5, free end, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS B- X15 V x0SW

Part No.: 91.257.x003.1 (x corresponds to length in m)

gesis® connection cable, female, free end, 5x 1.5 mm², 250 V, 16 A, length: x m, pastel blue/white

System gesis® MINI - assembled H05VV-F connection cable with protective ground, 5-pole, 1.5 mm², for dimming applications, female GST15i5, free end, with angled cable entry, according IEC 61535, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS B- X15 V x0PB01

Part No.: 91.257.x003.9 (x corresponds to length in m)

gesis® connection cable, male, free end, 5x 1.5 mm², 250/400 V, 16 A, length: x m, white

System gesis® MINI - assembled H05VV-F connection cable with protective ground, 5-pole, 1.5 mm², male GST15i5, free end, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS -S X15 V x0WS

Part No.: 91.257.x004.2 (x corresponds to length in m)

gesis® connection cable, male, free end, 5x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® MINI - assembled H05VV-F connection cable with protective ground, 5-pole, 1.5 mm², male GST15i5, free end, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS -S X15 V x0SW

Part No.: 91.257.x004.1 (x corresponds to length in m)

gesis® connection cable, male, free end, 5x 1.5 mm², 250 V, 16 A, length: x m, pastel blue/white

System gesis® MINI - assembled H05VV-F connection cable with protective ground, 5-pole, 1.5 mm², for dimming applications, male GST15i5, free end, with angled cable entry, according IEC 61535, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05VV-F

Cable color: white

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS -S X15 V x0PB01

Part No.: 91.257.x004.9 (x corresponds to length in m)

### Cable assemblies, 1.5 mm², halogen-free

gesis® extension cable, female, male, 5x 1.5 mm², 250/400 V, 16 A, length: x m, white

System gesis® MINI - assembled H05Z1Z1-F extension cable with protective ground, 5-pole, 1.5 mm², male GST15i5, female GST15i5, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS BS X15H V x0WS

Part No.: 91.257.x060.2 (x corresponds to length in m)

gesis® extension cable, female, male, 5x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® MINI - assembled H05Z1Z1-F extension cable with protective ground, 5-pole, 1.5 mm², male GST15i5, female GST15i5, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: black

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS BS X15H V x0SW

Part No.: 91.257.x060.1 (x corresponds to length in m)

gesis® extension cable, female, male, 5x 1.5 mm², 250 V, 16 A, length: x m, pastel blue/white

System gesis® MINI - assembled H05Z1Z1-F extension cable with protective ground, 5-pole, 1.5 mm², for dimming applications, male GST15i5, female GST15i5, with angled cable entry, according IEC 61535, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS BS X15H V x0PB01

Part No.: 91.257.x060.9 (x corresponds to length in m)

gesis® connection cable, female, free end, 5x 1.5 mm², 250/400 V, 16 A, length: x m, white

System gesis® MINI - assembled H05Z1Z1-F connection cable with protective ground, 5-pole, 1.5 mm², female GST15i5, free end, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS B- X15H V x0WS

Part No.: 91.257.x063.2 (x corresponds to length in m)

gesis® connection cable, female, free end, 5x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® MINI - assembled H05Z1Z1-F connection cable with protective ground, 5-pole, 1.5 mm², female GST15i5, free end, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: black

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS B- X15H V x0SW

Part No.: 91.257.x063.1 (x corresponds to length in m)

gesis® connection cable, female, free end, 5x 1.5 mm², 250 V, 16 A, length: x m, pastel blue/white

System gesis® MINI - assembled H05Z1Z1-F connection cable with protective ground, 5-pole, 1.5 mm², for dimming applications, female GST15i5, free end, with angled cable entry, according IEC 61535, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS B- X15H V x0PB01

Part No.: 91.257.x063.9 (x corresponds to length in m)

gesis® connection cable, male, free end, 5x 1.5 mm², 250/400 V, 16 A, length: x m, white

System gesis® MINI - assembled H05Z1Z1-F connection cable with protective ground, 5-pole, 1.5 mm², male GST15i5, free end, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding white.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS -S X15H V x0WS

Part No.: 91.257.x064.2 (x corresponds to length in m)

gesis® connection cable, male, free end, 5x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® MINI - assembled H05Z1Z1-F connection cable with protective ground, 5-pole, 1.5 mm², male GST15i5, free end, with angled cable entry, according IEC 61535, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: black

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS -S X15H V x0SW

Part No.: 91.257.x064.1 (x corresponds to length in m)

gesis® connection cable, male, free end, 5x 1.5 mm², 250 V, 16 A, length: x m, pastel blue/white

System gesis® MINI - assembled H05Z1Z1-F connection cable with protective ground, 5-pole, 1.5 mm², for dimming applications, male GST15i5, free end, with angled cable entry, according IEC 61535, mechanical coding code 2, color coding pastel blue.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection (plugged): IP40

Type of protection (unplugged): IP20

Cable type: H05Z1Z1-F

Cable color: white

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: GST15i5KS -S X15H V x0PB01

Part No.: 91.257.x064.9 (x corresponds to length in m)

91.030.4953.0	39

91.030.4953.1	39

91.030.5253.0	39

91.030.5253.1	40

91.030.5853.0	42

91.030.5853.1	42

91.030.5953.0	41

91.030.5953.1	41

91.030.6053.0	38

91.030.6053.1	38

91.050.3151.0	78

91.050.3251.0	78

91.050.3351.0	79

91.050.5953.0	80

91.050.5953.1	80

91.050.6053.0	81

91.207.x000.2	58

91.207.x003.2	58

91.207.x004.2	59

91.207.x060.2	60

91.207.x063.2	60

91.207.x064.2	61

91.222.x000.1	18

91.222.x000.2	18

91.222.x000.6	19

91.222.x000.9	19

91.222.x003.1	19

91.222.x003.2	19

91.222.x003.6	20

91.222.x003.9	20

91.222.x004.1	21

91.222.x004.2	20

91.222.x004.6	21

91.222.x004.9	21

91.222.x060.1	22

91.222.x060.2	22

91.222.x060.6	23

91.222.x060.9	22

91.222.x063.1	23

91.222.x063.2	23

91.222.x063.6	24

91.222.x063.9	24

91.222.x064.1	25

91.222.x064.2	24

91.222.x064.6	25

91.222.x064.9	25

91.232.x000.1	43

91.232.x000.2	43

91.232.x003.1	44

91.232.x003.2	44

91.232.x004.1	44

91.232.x004.2	44

91.232.x009.1	45

91.232.x009.2	45

91.232.x060.1	47

91.232.x060.2	47

91.232.x063.1	48

91.232.x063.2	47

91.232.x064.1	48

91.232.x064.2	48

91.232.x069.1	49

91.232.x069.2	49

91.257.x000.1	82

91.257.x000.2	82

91.257.x000.9	83

91.257.x003.1	83

91.257.x003.2	83

91.257.x003.9	84

91.257.x004.1	84

91.257.x004.2	84

91.257.x004.9	85

91.257.x060.1	86

91.257.x060.2	86

91.257.x060.9	87

91.257.x063.1	87

91.257.x063.2	87

91.257.x063.9	88

91.257.x064.1	88

91.257.x064.2	88

91.257.x064.9	89

91.921.2053.0	4

91.921.2053.1	5

91.921.2353.0	6

91.921.2353.1	6

91.921.2453.0	5

91.921.2453.1	5

91.921.3053.0	2

91.921.3053.1	2

91.921.3353.0	3

91.921.3353.1	4

91.921.3453.0	3

91.921.3453.1	3

91.921.9053.0	12

91.921.9053.1	12

91.921.9353.0	13

91.921.9353.1	14

91.921.9453.0	13

91.921.9453.1	13

91.922.2053.0	9

91.922.2053.1	9

91.922.2353.0	11

91.922.2353.1	11

91.922.2453.0	10

91.922.2453.1	10

91.922.3053.0	7

91.922.3053.1	7

91.922.3353.0	8

91.922.3353.1	9

91.922.3453.0	8

91.922.3453.1	8

91.922.9053.0	15

91.922.9053.1	15

91.922.9353.0	16

91.922.9353.1	17

91.922.9453.0	16

91.922.9453.1	16

91.931.3053.0	26

91.931.3053.1	26

91.931.3853.0	27

91.931.3853.1	27

91.931.4053.0	27

91.931.4053.1	28

91.931.9053.0	32

91.931.9053.1	32

91.931.9153.0	33

91.931.9153.1	34

91.931.9853.0	33

91.931.9853.1	33

91.932.3053.0	29

91.932.3053.1	29

91.932.3853.0	30

91.932.3853.1	30

91.932.4053.0	30

91.932.4053.1	31

91.932.9053.0	35

91.932.9053.1	35

91.932.9153.0	36

91.932.9153.1	37

91.932.9853.0	36

91.932.9853.1	36

91.941.3053.0	53

91.941.3053.1	53

91.941.4053.0	52

91.941.4053.1	52

91.941.9053.0	56

91.941.9053.1	56

91.942.3053.0	55

91.942.3053.1	55

91.942.4053.0	54

91.942.4053.1	54

91.942.9053.0	57

91.942.9053.1	57

91.951.3053.0	64

91.951.3053.1	65

91.951.3353.0	66

91.951.3353.1	66

91.951.3453.0	65

91.951.3453.1	65

91.951.4053.0	62

91.951.4053.1	62

91.951.4353.0	63

91.951.4353.1	64

91.951.4453.0	63

91.951.4453.1	63

91.951.9053.0	72

91.951.9053.1	72

91.951.9353.0	73

91.951.9353.1	74

91.951.9453.0	73

91.951.9453.1	73

91.952.3053.0	69

91.952.3053.1	69

91.952.3353.0	71

91.952.3353.1	71

91.952.3453.0	70

91.952.3453.1	70

91.952.4053.0	67

91.952.4053.1	67

91.952.4353.0	68

91.952.4353.1	69

91.952.4453.0	68

91.952.4453.1	68

91.952.9053.0	75

91.952.9053.1	75

91.952.9353.0	76

91.952.9353.1	77

91.952.9453.0	76

91.952.9453.1	76

99.400.4346.1	45

99.401.4346.1	46

99.402.4346.1	46

99.640.0000.0	50

99.641.0000.0	50

99.642.0000.0	50

99.643.0000.0	51

99.668.0000.0	51