1	gesis® NRG - flat cable system	2

1.1	gesis® NRG, 2-pole, 1.5 mm²	2

1.1.1	Flat cable adapter	2

1.1.2	Accessories	3

1.1.3	Flat cables	4

1.2	gesis® NRG, 5-pole, 2.5 mm²	5

1.2.1	Flat cable adapter	5

1.2.2	Accessories	7

1.2.3	Flat cables	8

1.3	gesis® NRG, 5-pole, 2.5 mm² + 2-pole, 1.5 mm²	9

1.3.1	Flat cable adapter	9

1.3.2	Accessories	12

1.3.3	Flat cables	13

1.4	gesis® NRG, 5-pole, 10 mm²	14

1.4.1	Flat cable adapter	14

1.4.2	Accessories	15

1.4.3	Flat cables	17

1.5	gesis® NRG, 5-pole, 16 mm²	18

1.5.1	Flat cable adapter	18

1.5.2	Accessories	19

1.5.3	Flat cables	21

# gesis® NRG - flat cable system

## gesis® NRG, 2-pole, 1.5 mm²

## Flat cable adapter

gesis® IDC flat cable adapter, 2-pole, for flat cable 2-pole, green

System gesis® NRG - Adapter to supply and tap bus signals (e.g. KNX). Contacting is realized with insulation technology to flat cable, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Housing material: Polyamide

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 I B1 HZB GN01

Part No.: 93.421.0953.0

gesis® IDC flat cable adapter, 2-pole, for flat cable 2-pole, black

System gesis® NRG - Adapter to supply and tap control signals (e.g. LON). Contacting is realized with insulation technology to flat cable, mechanical coding code 2, color coding black.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Housing material: Polyamide

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 I B1 HZB SW

Part No.: 93.421.2953.0

## Accessories

gesis® cable end cap for flat cable 2-pole

System gesis® NRG - cable end cap for flat cable 2-pole.

Type of protection: IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.562.4400.0

Cable clip for flat cable 2-, 5-, 7-pole

Cable clip for flat cable 2-, 5-, 7-pole, 1.5 or 2.5 mm², gray.

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.562.3000.0

Sheath stripping tool for flat cable 2-, 5-, 7-pole

Sheath stripping tool for flat cable 2-, 5-, 7-pole, 1.5 or 2.5 mm².

Brand: Wieland Electric GmbH

Part No.: 95.350.0200.0

Cable cutter for flat cable 2-, 5-, 7-pole

Cable cutter for flat cable 2-, 5-, 7-pole, 1.5 or 2.5 mm².

Brand: Wieland Electric GmbH

Part No.: 95.300.0300.0

## Flat cables

gesis® flat cable, 2x 1.5 mm², 50 V, 3 A, PVC

System gesis® IDC - Flat cable for bus/control signals, 2x 1.5 mm², as flexible busbar with insulation piercing connection technology, useable in dry rooms, false ceiling, as well as wall ducts and cavities.

Rated voltage: 50 V

Rated current: 3 A

Cable color: dark gray

Insulation material: PVC

Fire behavior: self-extinguishing according to IEC 60332.1

Halogen-free: no

Brand: Wieland Electric GmbH

Part No.: 00.702.1022.3

gesis® flat cable, 2x 1.5 mm², 50 V, 3 A, halogen-free

System gesis® IDC - Flat cable for bus/control signals, 2x 1.5 mm², as flexible busbar with insulation piercing connection technology, useable in dry rooms, false ceiling, as well as wall ducts and cavities.

Rated voltage: 50 V

Rated current: 3 A

Cable color: dark gray

Insulation material: halogen-free

Fire behavior: self-extinguishing according to IEC 60332.1

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 00.709.1022.3

## gesis® NRG, 5-pole, 2.5 mm²

## Flat cable adapter

gesis® IDC flat cable adapter, mains infeed, for flat cable 5-pole 2.5 mm², 5-pole

System gesis® NRG - Adapter for mains infeed. Contacting is realized with insulation technology to flat cable.

Rated voltage: 250/400 V

Rated current: 16 A

Terminal cross-section, solid: 1.5 - 2.5 mm²

Cable diameter: 5 - 13 mm

Type of protection: up to IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18i5 A SI F5 SWUC

Part No.: 92.050.8153.0

gesis® IDC Flat cable adapter mains, for flat cable 5-pole 2.5 mm², 5-pole

System gesis® NRG - Flat cable mains adapter. Contacting is realized with insulation technology to flat cable.

Rated voltage: 250/400 V

Rated current: 16 A

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, stranded: 0.5 - 1.5 mm²

Cable diameter: 5 - 13 mm

Connections per pole: 2

Type of protection: up to IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18i5 A FI F5 SWUC

Part No.: 92.050.8653.0

gesis® IDC flat cable adapter, pluggable output, for flat cable 5-pole 2.5 mm², 3-pole, L1

System gesis® NRG - Adapter for 1-phase mains output, phase L1. Contacting is realized with insulation technology to flat cable, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Type of protection: IP 20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18i3 I B1V F5 1 SW

Part No.: 92.031.5153.1

gesis® IDC flat cable adapter, pluggable output, for flat cable 5-pole 2.5 mm², 3-pole, L2

System gesis® NRG - Adapter for 1-phase mains output, phase L2. Contacting is realized with insulation technology to flat cable, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Type of protection: IP 20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18i3 I B1V F5 2 SW

Part No.: 92.031.5253.1

gesis® IDC flat cable adapter, pluggable output, for flat cable 5-pole 2.5 mm², 3-pole, L3

System gesis® NRG - Adapter for 1-phase mains output, phase L3. Contacting is realized with insulation technology to flat cable, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Type of protection: IP 20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18i3 I B1V F5 3 SW

Part No.: 92.031.5353.1

gesis® IDC flat cable adapter, pluggable output, for flat cable 5-pole 2.5 mm², 5-pole

System gesis® NRG - Adapter for 3-phase mains output. Contacting is realized with insulation technology to flat cable, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Type of protection: IP 20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18i5 I B1V F5 SW

Part No.: 92.051.0553.1

## Accessories

gesis® cable end cap for flat cable 5-pole, 2.5 mm²

System gesis® NRG - cable end cap for flat cable 5-pole, 2.5 mm².

Type of protection: IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.563.4700.0

Cable clip for flat cable 2-, 5-, 7-pole

Cable clip for flat cable 2-, 5-, 7-pole, 1.5 or 2.5 mm², gray.

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.562.3000.0

Sheath stripping tool for flat cable 2-, 5-, 7-pole

Sheath stripping tool for flat cable 2-, 5-, 7-pole, 1.5 or 2.5 mm².

Brand: Wieland Electric GmbH

Part No.: 95.350.0200.0

Cable cutter for flat cable 2-, 5-, 7-pole

Cable cutter tool for flat cable 2-, 5-, 7-pole, 1.5 or 2.5 mm².

Brand: Wieland Electric GmbH

Part No.: 95.300.0300.0

gesis® locking GST18, 3-, 4- or 5-pole, black

System gesis® NRG - locking for floating cable connections GST18, 3-, 4- or 5-pole, black.

Material: Polyamide

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18 SW

Part No.: 05.587.3156.1

## Flat cables

gesis® flat cable, 5x 2.5 mm², 250/400 V, 16 A, PVC

System gesis® IDC - Flat cable for mains, 5x 2.5 mm², as flexible busbar with insulation piercing connection technology, useable in dry rooms, false ceiling, as well as wall ducts and cavities.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Cable color: light green

Insulation material: PVC

Fire behavior: self-extinguishing according to IEC 60332.1

Halogen-free: no

Brand: Wieland Electric GmbH

Part No.: 00.702.0303.7

gesis® flat cable, 5x 2.5 mm², 250/400 V, 16 A, halogen-free

System gesis® IDC - Flat cable for mains, 5x 2.5 mm², as flexible busbar with insulation piercing connection technology, useable in dry rooms, false ceiling, as well as wall ducts and cavities.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Cable color: light green

Insulation material: halogen-free

Fire behavior: self-extinguishing according to IEC 60332.1

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 00.709.0303.7

## gesis® NRG, 5-pole, 2.5 mm² + 2-pole, 1.5 mm²

## Flat cable adapter

gesis® IDC flat cable adapter, mains infeed, for flat cable 5+2-pole, 5-pole

System gesis® NRG - Adapter for mains infeed. Contacting is realized with insulation technology to flat cable.

Rated voltage: 250/400 V

Rated current: 16 A

Terminal cross-section, solid: 1.5 - 2.5 mm²

Cable diameter: 5 - 13 mm

Type of protection: up to IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18i5 A SI F7 SWUC

Part No.: 92.050.8053.0

gesis® IDC flat cable adapter, signal infeed, for flat cable 5+2-pole, 2-pole

System gesis® NRG - Adapter for signal infeed. Contacting is realized with insulation technology to flat cable.

Rated voltage: 50 V

Rated current: 3 A

Terminal cross-section, solid: 1.5 mm²

Cable diameter: 3 - 8 mm

Type of protection: up to IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 A SI F7 SW

Part No.: 93.420.1053.0

gesis® IDC flat cable adapter, pluggable output, for flat cable 5+2-pole, 2-pole, green

System gesis® NRG - Adapter as signal output (e.g. KNX). Contacting is realized with insulation technology to flat cable, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 I B1VZB GN01

Part No.: 93.421.0853.0

gesis® IDC flat cable adapter, pluggable output, for flat cable 5+2-pole, 2-pole, green

System gesis® NRG - Adapter as signal output (e.g. KNX) with spacer for optimal mounting of 1-phase/3-pole gesis® EIB V actuators. Contacting is realized with insulation technology to flat cable, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 I B1VZB GN01

Part No.: 93.421.1153.0

gesis® IDC flat cable adapter, pluggable output, for flat cable 5+2-pole, 2-pole, black

System gesis® NRG - Adapter as signal output (e.g. LON). Contacting is realized with insulation technology to flat cable, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 I B1VZB SW

Part No.: 93.421.2853.0

gesis® IDC flat cable adapter, pluggable output, for flat cable 5+2-pole, 3-pole, L1

System gesis® NRG - Adapter for 1-phase mains output, phase L1. Contacting is realized with insulation technology to flat cable, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Type of protection: IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18i3 I B1V F7 1 SW

Part No.: 92.031.4153.1

gesis® IDC flat cable adapter, pluggable output, for flat cable 5+2-pole, 3-pole, L2

System gesis® NRG - Adapter for 1-phase mains output, phase L2. Contacting is realized with insulation technology to flat cable, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Type of protection: IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18i3 I B1V F7 2 SW

Part No.: 92.031.4253.1

gesis® IDC flat cable adapter, pluggable output, for flat cable 5+2-pole, 3-pole, L3

System gesis® NRG - Adapter for 1-phase mains output, phase L3. Contacting is realized with insulation technology to flat cable, mechanical coding code 1, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Type of protection: IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18i3 I B1V F7 3 SW

Part No.: 92.031.4353.1

gesis® IDC flat cable adapter, pluggable output, for flat cable 5+2-pole, 5-pole

System gesis® NRG - Adapter for 3-phase mains output. Contacting is realized with insulation technology to flat cable, mechanical coding code 1, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Type of protection: IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18i5 I B1V F7 SW

Part No.: 92.051.0353.1

## Accessories

gesis® cable end cap for flat cable 5+2-pole

System gesis® NRG - cable end cap for flat cable 5-pole, 2.5 mm² + 2-pole, 1.5 mm².

Type of protection: IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.562.2900.0

Cable clip for flat cable 2-, 5-, 7-pole

Cable clip for flat cable 2-, 5-, 7-pole, 1.5 or 2.5 mm², gray.

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.562.3000.0

Sheath stripping tool for flat cable 2-, 5-, 7-pole

Sheath stripping tool for flat cable 2-, 5-, 7-pole, 1.5 or 2.5 mm².

Brand: Wieland Electric GmbH

Part No.: 95.350.0200.0

Cable cutter for flat cable 2-, 5-, 7-pole

Sheath stripping tool for flat cable 2-, 5-, 7-pole, 1.5 or 2.5 mm².

Brand: Wieland Electric GmbH

Part No.: 95.300.0300.0

gesis® locking GST18, 3-, 4- or 5-pole, black

System gesis® NRG - locking for floating cable connections GST18, 3-, 4- or 5-pole, black.

Material: Polyamide

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: GST18 SW

Part No.: 05.587.3156.1

## Flat cables

gesis® flat cable, 5x 2.5 mm², 250/400 V, 16 A + 2x 1.5 mm², 50 V, 3 A, PVC

System gesis® IDC - Flat cable for mains, 5x 2.5 mm² + Signal (e.g. KNX or LON), 2x 1.5 mm², as flexible busbar with insulation piercing connection technology, useable in dry rooms, false ceiling, as well as wall ducts and cavities.

Rated voltage mains: 250/400 V

Rated current mains: 16 A

Rated voltage signals: 50 V

Rated current signals: 3 A

Rated impulse voltage: 4 kV

Cable color: purple

Insulation material: PVC

Fire behavior: self-extinguishing according to IEC 60332.1

Halogen-free: no

Brand: Wieland Electric GmbH

Part No.: 00.702.0323.9

gesis® flat cable, 5x 2.5 mm², 250/400 V, 16 A + 2x 1.5 mm², 50 V, 3 A, halogen-free

System gesis® IDC - Flat cable for mains, 5x 2.5 mm² + Signal (e.g. KNX or LON), 2x 1.5 mm², as flexible busbar with insulation piercing connection technology, useable in dry rooms, false ceiling, as well as wall ducts and cavities.

Rated voltage mains: 250/400 V

Rated current mains: 16 A

Rated voltage signals: 50 V

Rated current signals: 3 A

Rated impulse voltage: 4 kV

Cable color: purple

Insulation material: halogen-free

Fire behavior: self-extinguishing according to IEC 60332.1

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 00.709.0323.9

## gesis® NRG, 5-pole, 10 mm²

## Flat cable adapter

gesis® IDC flat cable adapter, mains infeed, for flat cable 5-pole, 10 mm²

System gesis® NRG - Adapter for main infeed at a cable end. Flat cable contacting via terminal blocks 5x 10 mm².

Rated voltage: 250/400 V

Rated current: 50 A

Terminal cross-section, solid: 10 mm²

Cable diameter: metric cable gland M32 (NYM, H05VV-F, 5x 10 mm²)

Type of protection: up to IP20

Halogen-free: yes

Dimension: 260x90x70 mm

Brand: Wieland Electric GmbH

Type: GST18i5 A SIE F8

Part No.: 92.050.8253.0

gesis® IDC flat cable adapter, mains middle infeed, for flat cable 5-pole, 10 mm²

System gesis® NRG - Adapter for main infeed somewhere on the cable. Flat cable contacting via terminal blocks 5x 10 mm².

Rated voltage: 250/400 V

Rated current: 50 A

Terminal cross-section, solid: 10 mm²

Cable diameter: metric cable gland M32 (NYM, H05VV-F, 5x 10 mm²)

Type of protection: up to IP20

Halogen-free: yes

Dimension: 260x170x70 mm

Brand: Wieland Electric GmbH

Type: GST18i5 A S E F8

Part No.: 92.050.8853.0

gesis® IDC flat cable adapter, mains output, for flat cable 5-pole, 10 mm²

System gesis® NRG - Adapter for 3-phase mains output. Contacting is realized with insulation technology to flat cable.

Rated voltage: 250/400 V

Rated current: 25 A

Terminal cross-section (solid/stranded): 1.5 - 4.0 mm²

Cable diameter: 5x 2.5 mm² - 5x 4.0 mm² (NYM, H05VV-F)

Type of protection: IP20

Halogen-free: yes

Dimension: 110x51x48 mm

Brand: Wieland Electric GmbH

Type: GST18i5A FIA F8 SWUC

Part No.: 92.050.8353.0

## Accessories

gesis® cable end cap for flat cable 5-pole, 10 mm²

System gesis® NRG - cable end cap for flat cable 5-pole, 10 mm².

Type of protection: IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.563.9553.0

Cable clip for flat cable 5-pole, 10/16 mm²

Cable clip for flat cable 5-pole, 10/16 mm².

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.563.9753.0

Stripping knife for flat cable 5-pole, 10/16 mm²

Stripping knife for flat cable 5-pole, 10/16 mm².

Brand: Wieland Electric GmbH

Part No.: 95.350.0500.0

Cable gland for junction box, M40

Cable gland for junction box, M40x 1.5.

Clamping range: 16 - 28 mm

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: Z5.507.1953.0

Cable gland for junction box, M25

Cable gland for junction box, M25x 1.5.

Clamping range: 7 - 16 mm

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: Z5.507.1553.0

Cable gland for junction box, M25, metall

Cable gland for junction box, M25x 1.5.

Clamping range: 11 - 18 mm

Brand: Wieland Electric GmbH

Part No.: Z5.507.1521.0

Filler-plug for junction box, M25

Filler-plug for junction box, M25x 1.5.

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.507.4153.0

## Flat cables

gesis® flat cable, 5x 10 mm², 250/400 V, 50 A, PVC

System gesis® IDC - Flat cable for mains, 5x 10 mm², as flexible busbar with insulation piercing connection technology, useable in dry rooms, false ceiling, as well as wall ducts and cavities.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Cable color: light green

Insulation material: PVC

Fire behavior: self-extinguishing according to IEC 60332.1

Halogen-free: no

Dimension: 38.5x10 mm

Brand: Wieland Electric GmbH

Part No.: 00.702.0306.7

gesis® flat cable, 5x 10 mm², 250/400 V, 50 A, halogen-free

System gesis® IDC - Flat cable for mains, 5x 10 mm², as flexible busbar with insulation piercing connection technology, useable in dry rooms, false ceiling, as well as wall ducts and cavities.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Cable color: light green

Insulation material: halogen-free

Fire behavior: self-extinguishing according to IEC 60332.1

Halogen-free: yes

Dimension: 38.5x10 mm

Brand: Wieland Electric GmbH

Part No.: 00.709.0306.7

## gesis® NRG, 5-pole, 16 mm²

## Flat cable adapter

gesis® IDC flat cable adapter, mains infeed, for flat cable 5-pole, 16 mm²

System gesis® NRG - Adapter for mains infeed. Contacting is realized with insulation technology to flat cable.

Rated voltage: 250/400 V

Rated current: 63 A

Terminal cross-section, solid: 16 mm²

Type of protection: up to IP65

Halogen-free: yes

Dimension: 200x85x91 mm

Brand: Wieland Electric GmbH

Type: GST18i5 A SIE F9 SWUC

Part No.: 92.050.8453.0

gesis® IDC flat cable adapter, mains output, for flat cable 5-pole, 16 mm²

System gesis® NRG - Adapter for 3-phase mains output. Contacting is realized with insulation technology to flat cable.

Rated voltage: 250/400 V

Rated current: 32 A

Terminal cross-section, solid: 6,0 mm²

Type of protection: up to IP65

Halogen-free: yes

Dimension: 200x85x73 mm

Brand: Wieland Electric GmbH

Type: GST18i5A SIA F9 SWUC

Part No.: 92.050.8553.0

gesis® IDC flat cable adapter, mains output incl. line safety switch, for flat cable 5-pole, 16 mm²

System gesis® NRG - Adapter for 3-phase mains output incl. line safety switch und pluggable gesis® - outputs. Contacting is realized with insulation technology to flat cable.

Rated voltage: 250/400 V

Rated current: 16 A

Line safety switch: 3x B16 A

Type of protection: up to IP20

Output 5-pole: 1x GST18i5, Code 1, black

Outputs 3-pole: 3x GST18i3, Code 1, black

Halogen-free: yes

Dimension: 220x110x110 mm

Brand: Wieland Electric GmbH

Type: GST18i5A SIA F9 SWUC

Part No.: G0.000.0044.7

## Accessories

gesis® cable end cap for flat cable 5-pole, 16 mm²

System gesis® NRG - cable end cap for flat cable 5-pole, 16 mm².

Type of protection: IP20

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.563.9453.0

Cable clip for flat cable 5-pole, 10/16 mm²

Cable clip for flat cable 5-pole, 10/16 mm².

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.563.9753.0

Stripping knife for flat cable 5-pole, 10/16 mm²

Stripping knife for flat cable 5-pole, 10/16 mm².

Brand: Wieland Electric GmbH

Part No.: 95.350.0500.0

Cable gland for junction box, M40

Cable gland for junction box, M40x 1.5.

Clamping range: 16 - 28 mm

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: Z5.507.1953.0

Cable gland for junction box, M25

Cable gland for junction box, M25x 1.5.

Clamping range: 7 - 16 mm

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: Z5.507.1553.0

Cable gland for junction box, M25, metall

Cable gland for junction box, M25x 1.5.

Clamping range: 11 - 18 mm

Brand: Wieland Electric GmbH

Part No.: Z5.507.1521.0

Filler-plug for junction box, M25

Filler-plug for junction box, M25x 1.5.

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.507.4153.0

## Flat cables

gesis® flat cable, 5x 16 mm², 250/400 V, 63 A, PVC

System gesis® IDC - Flat cable for mains, 5x 16 mm², as flexible busbar with insulation piercing connection technology, useable in dry rooms, false ceiling, as well as wall ducts and cavities.

Rated voltage: 250/400 V

Rated current: 63 A

Rated impulse voltage: 4 kV

Cable color: light gray

Insulation material: PVC

Fire behavior: self-extinguishing according to IEC 60332.1

Halogen-free: no

Dimension: 48.5x11.3 mm

Brand: Wieland Electric GmbH

Part No.: 00.702.0307.3

gesis® flat cable, 5x 16 mm², 250/400 V, 63 A, halogen-free

System gesis® IDC - Flat cable for mains, 5x 16 mm², as flexible busbar with insulation piercing connection technology, useable in dry rooms, false ceiling, as well as wall ducts and cavities.

Rated voltage: 250/400 V

Rated current: 63 A

Rated impulse voltage: 4 kV

Cable color: light gray

Insulation material: halogen-free

Fire behavior: self-extinguishing according to IEC 60332.1

Halogen-free: yes

Dimension: 48.5x11.3 mm

Brand: Wieland Electric GmbH

Part No.: 00.709.0307.3

00.702.0303.7	8

00.702.0306.7	17

00.702.0307.3	21

00.702.0323.9	13

00.702.1022.3	4

00.709.0303.7	8

00.709.0306.7	17

00.709.0307.3	21

00.709.0323.9	13

00.709.1022.3	4

05.507.4153.0	16, 20

05.562.2900.0	12

05.562.3000.0	3, 7, 12

05.562.4400.0	3

05.563.4700.0	7

05.563.9453.0	19

05.563.9553.0	15

05.563.9753.0	15, 19

05.587.3156.1	7, 12

92.031.4153.1	10

92.031.4253.1	10

92.031.4353.1	11

92.031.5153.1	5

92.031.5253.1	6

92.031.5353.1	6

92.050.8053.0	9

92.050.8153.0	5

92.050.8253.0	14

92.050.8353.0	14

92.050.8453.0	18

92.050.8553.0	18

92.050.8653.0	5

92.050.8853.0	14

92.051.0353.1	11

92.051.0553.1	6

93.420.1053.0	9

93.421.0853.0	9

93.421.0953.0	2

93.421.1153.0	10

93.421.2853.0	10

93.421.2953.0	2

95.300.0300.0	3, 7, 12

95.350.0200.0	3, 7, 12

95.350.0500.0	15, 19

G0.000.0044.7	18

Z5.507.1521.0	16, 20

Z5.507.1553.0	15, 19

Z5.507.1953.0	15, 19