1	gesis® NV - Bus-/Signal-Connectors	2

1.1	2-pole - BST14i2	2

1.1.1	Connectors	2

1.1.1.1	Female connector with spring clamp connection	2

1.1.1.2	Male with spring clamp connection	3

1.1.2	Snap-In	4

1.1.2.1	Female connector with spring clamp connection	4

1.1.2.2	Male with spring clamp connection	5

1.1.3	Luminaire connection	6

1.1.4	Distribution blocks	7

1.1.5	Accessories	9

1.1.6	Cables	10

1.1.6.1	Cable assemblies, 0.5 mm², containing halogen	10

1.1.6.2	Cable assemblies, 0.5 mm², halogen-free	12

1.2	3-pole - BST14i3	14

1.2.1	Connectors	14

1.2.1.1	Female connector with spring clamp connection	14

1.2.1.2	Male with spring clamp connection	15

1.2.2	Snap-In	16

1.2.2.1	Female connector with spring clamp connection	16

1.2.2.2	Male with spring clamp connection	17

1.2.3	Distribution blocks	18

1.2.4	Accessories	20

1.2.5	Cables	21

1.2.5.1	Cable assemblies, 0.5 mm², containing halogen	21

1.2.5.2	Cable assemblies, 0.5 mm², halogen-free	23

# gesis® NV - Bus-/Signal-Connectors

# 2-pole - BST14i2

## Connectors

### Female connector with spring clamp connection

gesis® connector, female, 2-pole, 50 V, 3 A, black/green

System gesis® NV - Connectors for bus/signal cables (connectors according to KNX manual), female version, 2-pole, with spring clamp connection, compact housing with strain relief and locking, field assembly, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Coding: according to KNX standard

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Cable diameter: 5.5 - 6.5 mm

Housing material: Polyamide

Connections per pole: 1

Marking: 1+, 2-

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 F B1 Z R1 S MGN01

Part No.: 93.421.0553.1

gesis® connector, female, 2-pole, 50 V, 3 A, black/pastel blue

System gesis® NV - Connectors for bus/signal cables, female version, 2-pole, with spring clamp connection, compact housing with strain relief and locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Cable diameter: 5.5 - 6.5 mm

Housing material: Polyamide

Connections per pole: 1

Marking: 1+, 2-

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 F B1 Z R1 S MPB02

Part No.: 93.421.4553.1

### Male with spring clamp connection

gesis® connector, male, 2-pole, 50 V, 3 A, black/green

System gesis® NV - Connectors for bus/signal cables (connectors according to KNX manual), male version, 2-pole, with spring clamp connection, compact housing with strain relief and locking, field assembly, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Coding: according to KNX standard

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Cable diameter: 5.5 - 6.5 mm

Housing material: Polyamide

Connections per pole: 1

Marking: 2-, 1+

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 F S1 Z R1 S MGN01

Part No.: 93.422.0553.1

gesis® connector, male, 2-pole, 50 V, 3 A, black/pastel blue

System gesis® NV - Connectors for bus/signal cables, male version, 2-pole, with spring clamp connection, compact housing with strain relief and locking, field assembly, mechanical coding code 2, color coding pastel blue.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Cable diameter: 5.5 - 6.5 mm

Housing material: Polyamide

Connections per pole: 1

Marking: 2-, 1+

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 F S1 Z R1 S MPB02

Part No.: 93.422.4553.1

## Snap-In

### Female connector with spring clamp connection

gesis® Snap-In, female, 2-pole, for panel mounting, 50 V, 3 A, black/green

System gesis® NV - Connectors for bus/signal cables (connectors according to KNX manual), female version, 2-pole, with spring clamp connection, snapable in housing, with integrated locking, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Coding: according to KNX standard

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 1+, 2-

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 F B1 R S GN01

Part No.: 93.421.0353.1

gesis® Snap-In, female, 2-pole, for panel mounting, 50 V, 3 A, black/pastel blue

System gesis® NV - Connectors for bus/signal cables, female version, 2-pole, with spring clamp connection, snapable in housing, with integrated locking and end-cap, mechanical coding code 2, color coding pastel blue.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 1+, 2-

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 F B1 R S PB02

Part No.: 93.421.4353.1

### Male with spring clamp connection

gesis® Snap-In, male, 2-pole, for panel mounting, 50 V, 3 A, black/green

System gesis® NV - Connectors for bus/signal cables (connectors according to KNX manual), male version, 2-pole, with spring clamp connection, snapable in housing, with integrated locking, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Coding: according to KNX standard

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 2-, 1+

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 F S1 R S GN01

Part No.: 93.422.0353.1

gesis® Snap-In, male, 2-pole, for panel mounting, 50 V, 3 A, black/pastel blue

System gesis® NV - Connectors for bus/signal cables, male version, 2-pole, with spring clamp connection, snapable in housing, with integrated locking and end-cap, mechanical coding code 2, color coding pastel blue.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 2-, 1+

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 F S1 R S PB02

Part No.: 93.422.4353.1

## Luminaire connection

gesis® TT-distribution block, 2-pole, 50 V, 3 A, pastel blue

System gesis® NV - TT-Distribution blocks for bus/signal cables, for a direct, pluggable connection to corresponding luminaires, 2-pole, with integrated locking and end-cap, mechanical coding code 2, color coding pastel blue.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Housing material: Polyamide

Connections per pole: 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 V 2P1KR PB02

Part No.: 93.420.4553.0

## Distribution blocks

gesis® distribution block, 2-pole, 1 input, 2 outputs, 50 V, 3 A, green

System gesis® NV - Distribution blocks for bus/signal cables (connectors according to KNX manual), T-shaped distribution block, 2-pole, 1 input, 2 outputs, with integrated locking, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Coding: according to KNX standard

Housing material: Polyamide

Input: 1

Outputs: 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 V 2P1 T GN01

Part No.: 93.420.0653.0

gesis® distribution block, 2-pole, 1 input, 2 outputs, 50 V, 3 A, pastel blue

System gesis® NV - Distribution blocks for bus/signal cables, T-shaped distribution block, 2-pole, 1 input, 2 outputs, with integrated locking, mechanical coding code 2, color coding pastel blue.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Housing material: Polyamide

Input: 1

Outputs: 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 V 2P1 T PB02

Part No.: 93.420.4653.0

gesis® distribution block, 2-pole, 1 input, 3 outputs, 50 V, 3 A, green

System gesis® NV - Distribution blocks for bus/signal cables (connectors according to KNX manual), H-shaped distribution block, 2-pole, 1 input, 3 outputs, with integrated locking, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Coding: according to KNX standard

Housing material: Polyamide

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 V 3P1 T GN01

Part No.: 93.420.0453.0

gesis® distribution block, 2-pole, 1 input, 5 outputs, 50 V, 3 A, green

System gesis® NV - Distribution blocks for bus/signal cables (connectors according to KNX manual), distribution block, 2-pole, 1 input, 5 outputs, with integrated locking, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Coding: according to KNX standard

Housing material: Polyamide

Input: 1

Outputs: 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i2 V 5P1 T GN01

Part No.: 93.420.0053.0

## Accessories

gesis® cover for female, black

System gesis® NV - Cover for female parts BST14, black.

Material: Polyamide

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.563.7753.0

gesis® cover for male, black

System gesis® NV - Cover for male parts BST14, black.

Material: Polyamide

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.563.7853.0

## Cables

### Cable assemblies, 0.5 mm², containing halogen

gesis® extension cable, female, male, 2x 0.5 mm², 50 V, 3 A, length: x m, green

System gesis® NV - assembled FB-2Y(St)2Y 2x(2x0.8) extension cable, 2-pole, 0.5 mm², male BST14i2, female BST14i2, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Approval: KNX certified

Cable type: FB-2Y(St)2Y 2x(2x0.8)

Cable color: green

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i2 KF BS 50 x0GN01

Part No.: 94.425.x000.7 (x corresponds to length in m)

gesis® extension cable, female, male, 2x 0.5 mm², 50 V, 3 A, length: x m, black

System gesis® NV - assembled L03VV-U2x0.5 extension cable, 2-pole, 0.5 mm², male BST14i2, female BST14i2, mechanical coding code 2, color coding pastel blue.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: L03VV-U2x0.5

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i2 KF BS 50L x0PB02

Part No.: 94.425.x030.9 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 0.5 mm², 50 V, 3 A, length: x m, green

System gesis® NV - assembled FB-2Y(St)2Y 2x(2x0.8) connection cable, 2-pole, 0.5 mm², female BST14i2, free end, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Approval: KNX certified

Cable type: FB-2Y(St)2Y 2x(2x0.8)

Cable color: green

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i2 KF B- 50 x0GN01

Part No.: 94.425.x003.7 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 0.5 mm², 50 V, 3 A, length: x m, black

System gesis® NV - assembled L03VV-U2x0.5 connection cable, 2-pole, 0.5 mm², female BST14i2, free end, mechanical coding code 2, color coding pastel blue.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: L03VV-U2x0.5

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i2 KF B- 50L x0PB02

Part No.: 94.425.x033.9 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 0.5 mm², 50 V, 3 A, length: x m, green

System gesis® NV - assembled FB-2Y(St)2Y 2x(2x0.8) connection cable, 2-pole, 0.5 mm², male BST14i2, free end, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Approval: KNX certified

Cable type: FB-2Y(St)2Y 2x(2x0.8)

Cable color: green

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i2 KF -S 50 x0GN01

Part No.: 94.425.x004.7 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 0.5 mm², 50 V, 3 A, length: x m, black

System gesis® NV - assembled L03VV-U2x0.5 connection cable, 2-pole, 0.5 mm², male BST14i2, free end, mechanical coding code 2, color coding pastel blue.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: L03VV-U2x0.5

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i2 KF -S 50L x0PB02

Part No.: 94.425.x034.9 (x corresponds to length in m)

### Cable assemblies, 0.5 mm², halogen-free

gesis® extension cable, female, male, 2x 0.5 mm², 50 V, 3 A, length: x m, green

System gesis® NV - assembled FB-H(St) 2x(2x0.8) extension cable, 2-pole, 0.5 mm², male BST14i2, female BST14i2, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Approval: KNX certified

Cable type: FB-H(St) 2x(2x0.8)

Cable color: green

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i2 KF BS 50H x0GN01

Part No.: 94.425.x060.7 (x corresponds to length in m)

gesis® extension cable, female, male, 2x 0.5 mm², 50 V, 3 A, length: x m, black

System gesis® NV - assembled L03Z1Z1-U2x0.5 extension cable, 2-pole, 0.5 mm², male BST14i2, female BST14i2, mechanical coding code 2, color coding pastel blue.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: L03Z1Z1-U2x0.5

Cable color: black

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i2 KF BS 50Z x0PB02

Part No.: 94.425.x090.9 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 0.5 mm², 50 V, 3 A, length: x m, green

System gesis® NV - assembled FB-H(St) 2x(2x0.8) connection cable, 2-pole, 0.5 mm², female BST14i2, free end, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Approval: KNX certified

Cable type: FB-H(St) 2x(2x0.8)

Cable color: green

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i2 KF B- 50H x0GN01

Part No.: 94.425.x063.7 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 0.5 mm², 50 V, 3 A, length: x m, black

System gesis® NV - assembled L03Z1Z1-U2x0.5 connection cable, 2-pole, 0.5 mm², female BST14i2, free end, mechanical coding code 2, color coding pastel blue.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: L03Z1Z1-U2x0.5

Cable color: black

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i2 KF B- 50Z x0PB02

Part No.: 94.425.x093.9 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 0.5 mm², 50 V, 3 A, length: x m, green

System gesis® NV - assembled FB-H(St) 2x(2x0.8) connection cable, 2-pole, 0.5 mm², male BST14i2, free end, mechanical coding code 1, color coding green.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Approval: KNX certified

Cable type: FB-H(St) 2x(2x0.8)

Cable color: green

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i2 KF -S 50H x0GN01

Part No.: 94.425.x064.7 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 0.5 mm², 50 V, 3 A, length: x m, black

System gesis® NV - assembled L03Z1Z1-U2x0.5 connection cable, 2-pole, 0.5 mm², male BST14i2, free end, mechanical coding code 2, color coding pastel blue.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: L03Z1Z1-U2x0.5

Cable color: black

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i2 KF -S 50Z x0PB02

Part No.: 94.425.x094.9 (x corresponds to length in m)

# 3-pole - BST14i3

## Connectors

### Female connector with spring clamp connection

gesis® connector, female, 3-pole, 50 V, 3 A, white

System gesis® NV - Connectors for bus/signal cables, female version, 3-pole, with spring clamp connection, compact housing with strain relief and locking, field assembly, mechanical coding code 3, color coding white.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Cable diameter: 5.5 - 6.5 mm

Housing material: Polyamide

Connections per pole: 1

Marking: 1+, 2-

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i3 F B1 Z R1 MWS

Part No.: 93.431.2553.0

gesis® connector, female, 3-pole, 50 V, 3 A, black

System gesis® NV - Connectors for bus/signal cables (e.g. LON), female version, 3-pole, with spring clamp connection, compact housing with strain relief and locking, field assembly, mechanical coding code 3, color coding black.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Cable diameter: 5.5 - 6.5 mm

Housing material: Polyamide

Connections per pole: 1

Marking: 1+, 2-

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i3 F B1 Z R1 MSW

Part No.: 93.431.2553.1

### Male with spring clamp connection

gesis® connector, male, 3-pole, 50 V, 3 A, white

System gesis® NV - Connectors for bus/signal cables, male version, 2-pole, with spring clamp connection, compact housing with strain relief and locking, field assembly, mechanical coding code 3, color coding white.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Cable diameter: 5.5 - 6.5 mm

Housing material: Polyamide

Connections per pole: 1

Marking: 2-, 1+

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i3 F S1 Z R1 MWS

Part No.: 93.432.2553.0

gesis® connector, male, 3-pole, 50 V, 3 A, black

System gesis® NV - Connectors for bus/signal cables (e.g. LON), male version, 3-pole, with spring clamp connection, compact housing with strain relief and locking, field assembly, mechanical coding code 3, color coding black.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Cable diameter: 5.5 - 6.5 mm

Housing material: Polyamide

Connections per pole: 1

Marking: 2-, 1+

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i3 F S1 Z R1 MSW

Part No.: 93.432.2553.1

## Snap-In

### Female connector with spring clamp connection

gesis® Snap-In, female, 3-pole, for panel mounting, 50 V, 3 A, white

System gesis® NV - Connectors for bus/signal cables, female version, 3-pole, with spring clamp connection, snapable in housing, with integrated locking, mechanical coding code 3, color coding white.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 1+, 2-

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i3 F B1 R WS

Part No.: 93.431.2353.0

gesis® Snap-In, female, 3-pole, for panel mounting, 50 V, 3 A, black

System gesis® NV - Connectors for bus/signal cables (e.g. LON), female version, 3-pole, with spring clamp connection, snapable in housing, with integrated locking, mechanical coding code 3, color coding black.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 1+, 2-

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i3 F B1 R SW

Part No.: 93.431.2353.1

### Male with spring clamp connection

gesis® Snap-In, male, 3-pole, for panel mounting, 50 V, 3 A, white

System gesis® NV - Connectors for bus/signal cables, male version, 3-pole, with spring clamp connection, snapable in housing, with integrated locking, mechanical coding code 3, color coding white.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 1+, 2-

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i3 F S1 R WS

Part No.: 93.432.2353.0

gesis® Snap-In, male, 3-pole, for panel mounting, 50 V, 3 A, black

System gesis® NV - Connectors for bus/signal cables (e.g. LON), male version, 3-pole, with spring clamp connection, snapable in housing, with integrated locking, mechanical coding code 3, color coding black.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Terminal cross-section, solid: 0.25 - 0.75 mm²

Terminal cross-section, stranded: 0.25 - 0.75 mm²

Housing material: Polyamide

Connections per pole: 1

Marking: 1+, 2-

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i3 F S1 R SW

Part No.: 93.432.2353.1

## Distribution blocks

gesis® distribution block, 3-pole, 1 input, 2 outputs, 50 V, 3 A, white

System gesis® NV - Distribution blocks for bus/signal cables, T-shaped distribution block, 3-pole, 1 input, 2 outputs, with integrated locking, mechanical coding code 3, color coding white.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Housing material: Polyamide

Input: 1

Outputs: 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i3 V 2P1 T WS

Part No.: 93.430.2653.0

gesis® distribution block, 3-pole, 1 input, 2 outputs, 50 V, 3 A, black

System gesis® NV - Distribution blocks for bus/signal cables (e.g. LON), T-shaped distribution block, 3-pole, 1 input, 2 outputs, with integrated locking, mechanical coding code 3, color coding black.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Housing material: Polyamide

Input: 1

Outputs: 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i3 V 2P1 T SW

Part No.: 93.420.2653.1

gesis® distribution block, 3-pole, 1 input, 3 outputs, 50 V, 3 A, white

System gesis® NV - Distribution blocks for bus/signal cables, H-shaped distribution block, 3-pole, 1 input, 3 outputs, with integrated locking, mechanical coding code 3, color coding white.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Housing material: Polyamide

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i3 V 3P1 T WS

Part No.: 93.430.2453.0

gesis® distribution block, 3-pole, 1 input, 3 outputs, 50 V, 3 A, black

System gesis® NV - Distribution blocks for bus/signal cables (e.g. LON), H-shaped distribution block, 3-pole, 1 input, 3 outputs, with integrated locking, mechanical coding code 3, color coding black.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Housing material: Polyamide

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i3 V 3P1 T SW

Part No.: 93.420.2453.1

gesis® distribution block, 3-pole, 1 input, 5 outputs, 50 V, 3 A, white

System gesis® NV - Distribution blocks for bus/signal cables, distribution block, 3-pole, 1 input, 5 outputs, with integrated locking, mechanical coding code 3, color coding white.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Housing material: Polyamide

Input: 1

Outputs: 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i3 V 5P1 T WS

Part No.: 93.430.2053.0

gesis® distribution block, 3-pole, 1 input, 5 outputs, 50 V, 3 A, black

System gesis® NV - Distribution blocks for bus/signal cables (e.g. LON), distribution block, 3-pole, 1 input, 5 outputs, with integrated locking, mechanical coding code 3, color coding black.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Housing material: Polyamide

Input: 1

Outputs: 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: BST14i3 V 5P1 T SW

Part No.: 93.420.2053.1

## Accessories

gesis® cover for female, black

System gesis® NV - Cover for female parts BST14, black.

Material: Polyamide

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.563.7753.0

gesis® cover for male, black

System gesis® NV - Cover for male parts BST14, black.

Material: Polyamide

Halogen-free: yes

Brand: Wieland Electric GmbH

Part No.: 05.563.7853.0

## Cables

### Cable assemblies, 0.5 mm², containing halogen

gesis® extension cable, female, male, 2x 0.5 mm², shed, 50 V, 3 A, length: x m, white

System gesis® NV - assembled FB-2Y(St)2Y 2x(2x0.8) extension cable, 3-pole, 0.5 mm², male BST14i3, female BST14i3, mechanical coding code 3, color coding white.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: FB-2Y(St)2Y 2x(2x0.8)

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i3 KF BS 50 x0WS

Part No.: 94.435.x000.2 (x corresponds to length in m)

gesis® extension cable, female, male, 2x 0.5 mm², shed, 50 V, 3 A, length: x m, black

System gesis® NV - assembled FB-2Y(St)2Y 2x(2x0.8) extension cable, 3-pole, 0.5 mm², male BST14i3, female BST14i3, mechanical coding code 3, color coding black.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: FB-2Y(St)2Y 2x(2x0.8)

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i3 KF BS 50 x0SW

Part No.: 94.435.x000.1 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 0.5 mm², shed, 50 V, 3 A, length: x m, white

System gesis® NV - assembled FB-2Y(St)2Y 2x(2x0.8) connection cable, 3-pole, 0.5 mm², female BST14i3, free end, mechanical coding code 3, color coding white.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: FB-2Y(St)2Y 2x(2x0.8)

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i3 KF B- 50 x0WS

Part No.: 94.435.x003.2 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 0.5 mm², shed, 50 V, 3 A, length: x m, black

System gesis® NV - assembled FB-2Y(St)2Y 2x(2x0.8) connection cable, 3-pole, 0.5 mm², female BST14i3, free end, mechanical coding code 3, color coding black.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: FB-2Y(St)2Y 2x(2x0.8)

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i3 KF B- 50 x0SW

Part No.: 94.435.x003.1 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 0.5 mm², shed, 50 V, 3 A, length: x m, white

System gesis® NV - assembled FB-2Y(St)2Y 2x(2x0.8) connection cable, 3-pole, 0.5 mm², male BST14i3, free end, mechanical coding code 3, color coding white.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: FB-2Y(St)2Y 2x(2x0.8)

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i3 KF -S 50 x0WS

Part No.: 94.435.x004.2 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 0.5 mm², shed, 50 V, 3 A, length: x m, black

System gesis® NV - assembled FB-2Y(St)2Y 2x(2x0.8) connection cable, 3-pole, 0.5 mm², male BST14i3, free end, mechanical coding code 3, color coding black.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: FB-2Y(St)2Y 2x(2x0.8)

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i3 KF -S 50 x0SW

Part No.: 94.435.x004.1 (x corresponds to length in m)

### Cable assemblies, 0.5 mm², halogen-free

gesis® extension cable, female, male, 2x 0.5 mm², shed, 50 V, 3 A, length: x m, black

System gesis® NV - assembled FB-H(St) 2x(2x0.8) extension cable, 3-pole, 0.5 mm², male BST14i3, female BST14i3, mechanical coding code 3, color coding black.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: FB-H(St) 2x(2x0.8)

Cable color: green

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i3 KF BS 50H x0SW

Part No.: 94.435.x060.1 (x corresponds to length in m)

gesis® connection cable, female, free end, 2x 0.5 mm², shed, 50 V, 3 A, length: x m, black

System gesis® NV - assembled FB-H(St) 2x(2x0.8) connection cable, 3-pole, 0.5 mm², female BST14i3, free end, mechanical coding code 3, color coding black.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: FB-H(St) 2x(2x0.8)

Cable color: green

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i3 KF B- 50H x0SW

Part No.: 94.435.x063.1 (x corresponds to length in m)

gesis® connection cable, male, free end, 2x 0.5 mm², shed, 50 V, 3 A, length: x m, black

System gesis® NV - assembled FB-H(St) 2x(2x0.8) connection cable, 3-pole, 0.5 mm², male BST14i3, free end, mechanical coding code 3, color coding black.

Rated voltage: 50 V

Rated current: 3 A

Type of protection: IP20

Cable type: FB-H(St) 2x(2x0.8)

Cable color: green

Halogen-free: yes

Length: x m

Brand: Wieland Electric GmbH

Type: BST14i3 KF -S 50H x0SW

Part No.: 94.435.x064.1 (x corresponds to length in m)

05.563.7753.0	9, 20

05.563.7853.0	9, 20

93.420.0053.0	8

93.420.0453.0	7

93.420.0653.0	7

93.420.2053.1	19

93.420.2453.1	19

93.420.2653.1	18

93.420.4553.0	6

93.420.4653.0	7

93.421.0353.1	4

93.421.0553.1	2

93.421.4353.1	4

93.421.4553.1	2

93.422.0353.1	5

93.422.0553.1	3

93.422.4353.1	5

93.422.4553.1	3

93.430.2053.0	19

93.430.2453.0	18

93.430.2653.0	18

93.431.2353.0	16

93.431.2353.1	16

93.431.2553.0	14

93.431.2553.1	14

93.432.2353.0	17

93.432.2353.1	17

93.432.2553.0	15

93.432.2553.1	15

94.425.x000.7	10

94.425.x003.7	10

94.425.x004.7	11

94.425.x030.9	10

94.425.x033.9	11

94.425.x034.9	11

94.425.x060.7	12

94.425.x063.7	12

94.425.x064.7	13

94.425.x090.9	12

94.425.x093.9	13

94.425.x094.9	13

94.435.x000.1	21

94.435.x000.2	21

94.435.x003.1	22

94.435.x003.2	21

94.435.x004.1	22

94.435.x004.2	22

94.435.x060.1	23

94.435.x063.1	23

94.435.x064.1	23